## Slide 1
We offload the feature matching bottleneck onto HW
  custom HW architecture to do exact matching
  orders of magnitude more efficient than SW implementation
Compute-bound: RN/corpus_size TD per sec
Memory-bound : TBW/corpus_size TD per sec
REALTIME 3D RECONSTRUCTION OF REALWORLD SCENES
Yu Wang, Hyun Soo Park, Peter Milder, James C. Hoe, Yaser Sheikh (CMU); Eriko Nurvitadhi, Mei Chen (Intel)
Camera pose
estimation
3D point
cloud (corpus)
Reconstructed Scene
Video Stream
Problem: Perceptually responsive systems require realtime 3D knowledge of environment
Example: to track user movements in a space, and the nearby objects in that space that user can interact with
Project goal: produce a low energy, memory-bandwidth efficient embedded solution for realtime 3D reconstruction of dynamic environments from monocular video
(1) OVERVIEW
3D Point Cloud Corpus
Prototyping Platform
(Altera DE4 Board)
Input Video Stream
Mobile Camera
3D Camera Motion
(4) FPGA PROOF-OF-CONCEPT
  B
Matching Accelerator
Nearest neighbor update
distances
Corpus
in
DRAM
Buffer
- hold T descriptors at a time
- hold per descriptor nearest
neighbor bookkeeping
Station
- pipelined
- R L2_norms/sec
TD
N parallel stations
TD stream
BW desc/sec
(3) FEATURE MATCHING ACCELERATOR
Feature matching: for each feature in each incoming image, find 2 nearest neighbor (L2-norm) in 3D point cloud corpus
Input Video
30K-60K TDs/ sec
(VGA)
10K-1M RDs
3D point cloud corpus of known reference descriptors (RD)
Match
Target Descriptor (TD)
Feature matching on Altera DE4 board (Stratix IV GX FPGA)
  utilizes 10 parallel stations, runs at 150 MHz clock freq
  occupies ~200K (50%) FPGA logic & 1MB (47%) on-chip mem
  15 ms & 32 ms per VGA frame (14K & 22K corpus)
What’s next
  Accelerate feature extraction
  3D point cloud corpus reconstruction in realtime
(2) CAMERA POSE ESTIMATION
Feature
Extraction
2 nearest neighbor
Video Stream
Chart: Corpus size
| 14K | 22K
Others | 0.2771 | 0.3022
Extraction | 0.5309 | 0.4791
Matching | 0.3609 | 1.0474
Chart: Corpus size
| 14K | 22K
Others | 3.238 | 3.2871
Extraction | 5.0763 | 5.1485
Matching | 2.1511 | 8.3391
SW is too slow even on an aggressive OoO proc (1+ sec/frame), and much worse on an embedded proc
Feature
Matching
Others
Camera
Pose
Corpus
Performance of software (SW) implementation
RD
Given a video stream from a camera, and a 3D point cloud corpus of the area, estimate camera pose w.r.t the corpus
On an OoO proc
(2.93 GHz)
On an in-order embedded proc
(1.3 GHz)
24x & 144x faster over SW on OoO proc (14K & 22K corpus)
As corpus size increases with larger and/or more complex scenes, feature matching becomes the bottleneck
32x & 257x faster over SW on embedded proc (14K & 22K corpus)
Note: we use SIFT feature, and our SW uses fast approximate method for matching. The accuracy of this method may become unacceptable with larger corpus sizes. Exact matching is preferred, but very slow to do in SW (for our experiments, ~10x slower than approximate)
Realtime speed (31+ fps)