## Slide 1: Flipping Bits in Memory Without Accessing Them
Yoongu Kim
Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee,
Donghyuk Lee, Chris Wilkerson, Konrad Lai, Onur Mutlu
DRAM Disturbance Errors

## Slide 2
DRAM Chip
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Aggressor Row
Repeatedly opening and closing a row induces disturbance errors in adjacent rows
Opened
Closed

## Slide 3: Quick Summary of Paper
We expose the existence and prevalence of disturbance errors in DRAM chips of today
  110 of 129 modules are vulnerable
  Affects modules of 2010 vintage or later
We characterize the cause and symptoms
  Toggling a row accelerates charge leakage in adjacent rows: row-to-row coupling
We prevent errors using a system-level approach
  Each time a row is closed, we refresh the charge stored in its adjacent rows with a low probability

## Slide 4
1. Historical Context
2. Demonstration (Real System)
3. Characterization (FPGA-Based)
4. Solutions

## Slide 5: A Trip Down Memory Lane
1968
IBM’s patent on DRAM
Suffered bitline-to-cell coupling
Intel commercializes DRAM (Intel 1103)
1971
Cell
8um
Bitline
6um
Bitline
“... this big fat metal line with full level signals running right over the storage node (of cell).”
– Joel Karp (1103 Designer)
Interview: Comp. History Museum
2014
2013

## Slide 6: A Trip Down Memory Lane
Intel’s patents mention “Row Hammer”
2014
We observe row-to-row coupling
2013
Earliest DRAM with row-to-row coupling
2010
Suffered bitline-to-cell coupling
Intel commercializes DRAM (Intel 1103)
1971
IBM’s patent on DRAM
1968

## Slide 7: Lessons from History
Coupling in DRAM is not new
  Leads to disturbance errors if not addressed
  Remains a major hurdle in DRAM scaling
Traditional efforts to contain errors
  Design-Time: Improve circuit-level isolation
  Production-Time: Test for disturbance errors
Despite such efforts, disturbance errors have been slipping into the field since 2010

## Slide 8
1. Historical Context
2. Demonstration (Real System)
3. Characterization (FPGA-Based)
4. Solutions

## Slide 9: How to Induce Errors
DDR3
DRAM Module
x86 CPU
X
111111111
111111111
111111111
111111111
111111111
111111111
Avoid cache hits
  Flush X from cache
Avoid row hits to X
  Read Y in another row
Y

## Slide 10: How to Induce Errors
DDR3
DRAM Module
x86 CPU
Y
X
111111111
111111111
111111111
111111111
111111111
111111111
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
1111
1111
011011110
110001011
101111101
001110111

## Slide 11: Number of Disturbance Errors
In a more controlled environment, we can induce as many as ten million disturbance errors
Disturbance errors are a serious reliability issue
CPU Architecture | Errors | Access-Rate
Intel Haswell (2013) | 22.9K | 12.3M/sec
Intel Ivy Bridge (2012) | 20.7K | 11.7M/sec
Intel Sandy Bridge (2011) | 16.1K | 11.6M/sec
AMD Piledriver (2012) | 59 | 6.1M/sec

## Slide 12: Security Implications
Breach of memory protection
  OS page (4KB) fits inside DRAM row (8KB)
  Adjacent DRAM row  Different OS page
Vulnerability: disturbance attack
  By accessing its own page, a program could corrupt pages belonging to another program
We constructed a proof-of-concept
  Using only user-level instructions

## Slide 13: Mechanics of Disturbance Errors
Cause 1: Electromagnetic coupling
  Toggling the wordline voltage briefly increases the voltage of adjacent wordlines
  Slightly opens adjacent rows  Charge leakage
Cause 2: Conductive bridges
Cause 3: Hot-carrier injection
Confirmed by at least one manufacturer

## Slide 14
1. Historical Context
2. Demonstration (Real System)
3. Characterization (FPGA-Based)
4. Solutions

## Slide 15: Infrastructure
Test Engine
DRAM Ctrl
PCIe
FPGA Board
PC

## Slide 16
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 17: Tested DDR3 DRAM Modules
43
54
32
Company A
Company B
Company C
Total: 129
Vintage: 2008 – 2014
Capacity: 512MB – 2GB

## Slide 18: Characterization Results
Most Modules Are at Risk
Errors vs. Vintage
Error = Charge Loss
Adjacency: Aggressor & Victim
Sensitivity Studies
Other Results in Paper

## Slide 19: 1. Most Modules Are at Risk
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors

## Slide 20: 2. Errors vs. Vintage
All modules from 2012–2013 are vulnerable
First
Appearance

## Slide 21: 3. Error = Charge Loss
Two types of errors
  ‘1’  ‘0’
  ‘0’  ‘1’
A given cell suffers only one type
Two types of cells
  True: Charged (‘1’)
  Anti: Charged (‘0’)
Manufacturer’s design choice
True-cells have only ‘1’  ‘0’ errors
Anti-cells have only ‘0’  ‘1’ errors
Errors are manifestations of charge loss

## Slide 22: 4. Adjacency: Aggressor & Victim
Most aggressors & victims are adjacent
Note: For three modules with the most errors (only first bank)
Adjacent
Adjacent
Adjacent
Non-Adjacent
Non-Adjacent

## Slide 23: 5. Sensitivity Studies
Access-Interval: 55–500ns
❷
❶
❸
Data-Pattern: all ‘1’s, all ‘0’s, etc.
Test Row 0
Test Row 1
Test Row 2
···
···
Find Errors
in Module
time
Open
Refresh Periodically
Open
Refresh-Interval: 8–128ms
Fill Module
with Data

## Slide 24: ❶ Access-Interval (Aggressor)
Note: For three modules with the most errors (only first bank)
Not Allowed
Less frequent accesses  Fewer errors
55ns
500ns

## Slide 25: 5. Sensitivity Studies
Access-Interval: 55–500ns
❷
❶
❸
Data-Pattern: all ‘1’s, all ‘0’s, etc.
Test Row 0
Test Row 1
Test Row 2
···
···
Find Errors
in Module
time
Open
Refresh Periodically
Open
Refresh-Interval: 8–128ms
Fill Module
with Data

## Slide 26: ❷ Refresh-Interval
Note: Using three modules with the most errors (only first bank)
More frequent refreshes  Fewer errors
~7x frequent
64ms

## Slide 27: 5. Sensitivity Studies
Access-Interval: 55–500ns
❷
❶
❸
Data-Pattern: all ‘1’s, all ‘0’s, etc.
Test Row 0
Test Row 1
Test Row 2
···
···
Find Errors
in Module
time
Open
Refresh Periodically
Open
Refresh-Interval: 8–128ms
Fill Module
with Data

## Slide 28: ❸ Data-Pattern
RowStripe
~RowStripe
111111
111111
111111
111111
000000
000000
000000
000000
000000
111111
000000
111111
111111
000000
111111
000000
Solid
~Solid
10x Errors
Errors affected by data stored in other cells

## Slide 29: Naive Solutions
❶ Throttle accesses to same row
  Limit access-interval: ≥500ns
  Limit number of accesses: ≤128K (=64ms/500ns)
❷ Refresh more frequently
  Shorten refresh-interval by ~7x
Both naive solutions introduce significant overhead in performance and power

## Slide 30: Characterization Results
Most Modules Are at Risk
Errors vs. Vintage
Error = Charge Loss
Adjacency: Aggressor & Victim
Sensitivity Studies
Other Results in Paper

## Slide 31: 6. Other Results in Paper
Victim Cells ≠ Weak Cells (i.e., leaky cells)
  Almost no overlap between them
Errors not strongly affected by temperature
  Default temperature: 50°C
  At 30°C and 70°C, number of errors changes <15%
Errors are repeatable
  Across ten iterations of testing, >70% of victim cells had errors in every iteration

## Slide 32: 6. Other Results in Paper (cont’d)
As many as 4 errors per cache-line
  Simple ECC (e.g., SECDED) cannot prevent all errors
Number of cells & rows affected by aggressor
  Victims cells per aggressor: ≤110
  Victims rows per aggressor: ≤9
Cells affected by two aggressors on either side
  Very small fraction of victim cells (<100) have an error when either one of the aggressors is toggled

## Slide 33
1. Historical Context
2. Demonstration (Real System)
3. Characterization (FPGA-Based)
4. Solutions

## Slide 34: Several Potential Solutions
Cost
Make better DRAM chips
Cost, Power
Sophisticated ECC
Power, Performance
Refresh frequently
Cost, Power, Complexity
Access counters

## Slide 35: Our Solution
PARA: Probabilistic Adjacent Row Activation
Key Idea
  After closing a row, we activate (i.e., refresh) one of its neighbors with a low probability: p = 0.005
Reliability Guarantee
  When p=0.005, errors in one year: 9.4×10-14
  By adjusting the value of p, we can provide an arbitrarily strong protection against errors

## Slide 36: Advantages of PARA
PARA refreshes rows infrequently
  Low power
  Low performance-overhead
    Average slowdown: 0.20% (for 29 benchmarks)
    Maximum slowdown: 0.75%
PARA is stateless
  Low cost
  Low complexity
PARA is an effective and low-overhead solution to prevent disturbance errors

## Slide 37: Conclusion
Disturbance errors are widespread in DRAM chips sold and used today
When a row is opened repeatedly, adjacent rows leak charge at an accelerated rate
We propose a stateless solution that prevents disturbance errors with low overhead
Due to difficulties in DRAM scaling, new and unexpected types of failures may appear

## Slide 38: Flipping Bits in Memory Without Accessing Them
Yoongu Kim
Ross Daly, Jeremie Kim, Chris Fallin, Ji Hye Lee,
Donghyuk Lee, Chris Wilkerson, Konrad Lai, Onur Mutlu
DRAM Disturbance Errors