## Slide 1: A Row Buffer Locality-Aware Caching Policy for Hybrid Memories
HanBin Yoon
Justin Meza
Rachata Ausavarungnirun Rachael Harding
Onur Mutlu

## Slide 2: Overview
Emerging memories such as PCM offer higher density than DRAM, but have drawbacks
Hybrid memories aim to achieve best of both
We identify row buffer locality (RBL) as a key criterion for data placement
  We develop a policy that caches to DRAM rows with low RBL and high reuse
50% perf. improvement over all-PCM memory
Within 23% perf. of all-DRAM memory

## Slide 3: Demand for Memory Capacity
Increasing cores and thread contexts
  Intel Sandy Bridge: 8 cores (16 threads)
  AMD Abu Dhabi: 16 cores
  IBM POWER7: 8 cores (32 threads)
  Sun T4: 8 cores (64 threads)
Modern data-intensive applications operate on huge datasets

## Slide 4: Emerging High Density Memory
DRAM density scaling becoming costly
Phase change memory (PCM)
  + Projected 3−12 denser than DRAM1
However, cannot simply replace DRAM
  − Higher access latency (4−12 DRAM2)
  − Higher access energy (2−40 DRAM2)
  − Limited write endurance (108 writes2)
 Use DRAM as a cache to PCM memory3
[1Mohan HPTS’09; 2Lee+ ISCA’09; 3Qureshi+ ISCA’09]

## Slide 5: Hybrid Memory
Benefits from both DRAM and PCM
  DRAM: Low latency, high endurance
  PCM: High capacity
Key question: Where to place data between these heterogeneous devices?
To help answer this question, let’s take a closer look at these technologies

## Slide 6: Hybrid Memory: A Closer Look
MC
MC
DRAM
(small capacity cache)
PCM (large capacity memory)
CPU
Memory channel
Bank
Bank
Bank
Bank
Row buffer

## Slide 7: Row Buffers and Latency
Memory cells organized in columns and rows
Row buffers store last accessed row
  Hit: Access data from row buffer  fast
  Miss: Access data from cell array  slow

## Slide 8: Key Observation
Row buffers exist in both DRAM and PCM
  Row buffer hit latency similar in DRAM & PCM2
  Row buffer miss latency small in DRAM
  Row buffer miss latency large in PCM
Place data in DRAM which
  Frequently miss in row buffer (low row buffer locality) miss penalty is smaller in DRAM
  Are reused many times  data worth the caching effort (contention in mem. channel and DRAM)
[2Lee+ ISCA’09]

## Slide 9: Data Placement Implications
Let’s say a processor accesses four rows
Row A
Row B
Row C
Row D

## Slide 10: Data Placement Implications
Let’s say a processor accesses four rows with different row buffer localities (RBL)
Row A
Row B
Row C
Row D
Low RBL
(Frequently miss
in row buffer)
High RBL
(Frequently hit
in row buffer)

## Slide 11: RBL-Unaware Policy
A row buffer locality-unaware policy could
place these rows in the following manner
DRAM (High RBL)
PCM (Low RBL)
Row C
Row D
Row A
Row B

## Slide 12: RBL-Unaware Policy
DRAM (High RBL)
PCM (Low RBL)
A
B
C
D
C
C
D
D
A
B
A
B
Accesses pattern to main memory:
A (oldest), B, C, C, C, A, B, D, D, D, A, B (youngest)
Stall time: 6 PCM device accesses
time

## Slide 13: RBL-Aware Policy
A row buffer locality-aware policy would place these rows in the following manner
DRAM (Low RBL)
PCM (High RBL)
 Access data at lower row buffer miss latency of DRAM
 Access data at low row buffer hit latency of PCM
Row A
Row B
Row C
Row D

## Slide 14: RBL-Aware Policy
DRAM (Low RBL)
PCM (High RBL)
A
B
C
D
C
C
D
D
A
B
A
B
Accesses pattern to main memory:
A (oldest), B, C, C, C, A, B, D, D, D, A, B (youngest)
Stall time: 6 DRAM device accesses
Saved cycles
time

## Slide 15: Our Mechanism: DynRBLA
For a subset of recently used rows in PCM:
  Count row buffer misses as indicator of row buffer locality (RBL)
Cache to DRAM rows with misses  threshold
  Row buffer miss counts are periodically reset (only cache rows with high reuse)
Dynamically adjust threshold to adapt to workload/system characteristics
  Interval-based cost-benefit analysis

## Slide 16: Evaluation Methodology
Cycle-level x86 CPU-memory simulator
  CPU: 16 out-of-order cores, 32KB private L1 per core, 512KB shared L2 per core
  Memory: DDR3 1066 MT/s, 1GB DRAM, 16GB PCM, 1KB migration granularity
Multi-programmed server & cloud workloads
  Server (18): TPC-C, TPC-H
  Cloud (18): Webserver, Video, TPC-C/H

## Slide 17: Comparison Points and Metrics
DynRBLA: Adaptive RBL-aware caching
RBLA: Row buffer locality-aware caching
Freq4: Frequency-based caching
DynFreq: Adaptive Freq.-based caching
Weighted speedup (performance) = sum of speedups versus when run alone
Max slowdown (fairness) = highest slowdown experienced by any thread
[4Jiang+ HPCA’10]

## Slide 18: Performance
Weighted Speedup (norm.)
Benefit 1: Reduced memory bandwidth consumption due to stricter caching criteria
Benefit 2: Increased row buffer locality (RBL) in PCM by moving low RBL data to DRAM

## Slide 19: Fairness
Maximum Slowdown (norm.)
Lower contention for row buffer in PCM & memory channel

## Slide 20: Energy Efficiency
Performance per Watt (norm.)
Increased performance & reduced data movement between DRAM and PCM

## Slide 21: Compared to All-PCM/DRAM
Weighted Speedup (norm.)
Maximum Slowdown (norm.)
Our mechanism achieves 50% better performance than all PCM, within 23% of all DRAM performance

## Slide 22: Conclusion
Demand for huge main memory capacity
  PCM offers greater density than DRAM
  Hybrid memories achieve the best of both
We identify row buffer locality (RBL) as a key metric for caching decisions
We develop a policy that caches to DRAM rows with low RBL and high reuse
Enables high-performance energy-efficient hybrid main memories

## Slide 23: Thank you! Questions?