## Slide 1: Write-hotness Aware Retention Management: Efficient Hot/Cold Data Partitioning for SSDs
Saugata Ghose
ghose@cmu.edu ▪ http://ece.cmu.edu/~saugatag/
joint work with Yixin Luo, Yu Cai, Jongmoo Choi, Onur Mutlu
August 10, 2016
Santa Clara, CA

## Slide 3: Executive Summary
Flash memory can achieve up to 50x endurance improvement by relaxing retention time using refresh [Cai+ ICCD ’12]
  Problem: Refresh consumes majority of endurance improvement
  Goal: Reduce refresh overhead to increase flash memory lifetime
Key Observation: Refresh unnecessary for write-hot data
Write-hotness Aware Retention Management (WARM)
  Physically partition write-hot pages and write-cold pages within flash
  Apply different policies (garbage collection, wear-leveling, refresh) to each group
WARM w/o refresh improves lifetime by 3.24x w/ 1.05KB overhead
WARM w/ adaptive refresh improves lifetime by 12.9x (1.21x over refresh)
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 4: Retention Time Relaxation for Flash Memory
Flash memory has limited write endurance
Retention time
  Duration for which flash memory can correctly hold data
  Significantly affects endurance
Chart: Retention Time
| 3-day | 3-week | 3-month | 3-year
P/E Cycles | 150000 | 20000 | 8000 | 3000
Typical flash retention guarantee
Requires refresh to reach this
[Cai+ ICCD ’12]
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 5: Recovering Retention Time with NAND Flash Refresh
Flash Correct and Refresh (FCR), Adaptive Rate FCR (ARFCR) [Cai+ ICCD ’12]
Problem: Flash refresh operations reduce extended lifetime
Nominal endurance
Extended endurance
Unusable endurance (consumed by refresh)
3000
150000
OUR GOAL
Reduce refresh overhead, improve flash lifetime
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 6: Observation 1: High Refresh Overhead
Chart: % of Extended Endurance Consumed by Refresh
| iozone | postmark | financial | proj | prxy | prn | hm | web-vm | src | stg | usr | web | rsrch | ts | wdev | homes | GMean
3-day refresh | 0.013367 | 0.028721 | 0.48359 | 0.65361 | 0.7675 | 0.84382 | 0.91026 | 0.91325 | 0.93367 | 0.93379 | 0.94295 | 0.94661 | 0.95023 | 0.95406 | 0.96606 | 0.97177 | 0.53366
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Notes: Evaluated 16 real workload traces to find %

## Slide 7: Observation 2: Skewed Distribution of Write Activity
Small amount of write-hot data generates large fraction of writes
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 8: Observation 3: Write-hot Pages Can Safely Skip Refresh
Write-Cold Page
Write-Cold Page
Write-Cold Page
Write-Hot Page
Write-Cold Page
Write-Hot Page
Write-Hot Page
Invalid Page
Write-Hot Page
Invalid Page
Write-Hot Page
Retention Effect
Update
Invalid Page
Write-Cold Page
Needs Refresh
Refresh Unnecessary
Write-Hot Page
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 9: Conventional Write-hotness Oblivious Management
Flash Memory
Page 1
Page 0
Page 2
Page 255
……
Page 257
Page 256
Page 258
Page 511
……
……
Page M+1
Page M
Page M+2
Page M+255
……
Flash Controller
Hot Page 1
Cold Page 2
Hot Page 1
Cold Page 3
Hot Page 4
Cold Page 5
Hot Page 4
Hot Page 1
Hot Page 4
Cold Page 2
Cold Page 3
Cold Page 4
Read
Write
Erase
Unable to relax retention time for blocks with both write-hot and write-cold pages
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 10: Key Idea: Write-hotness Aware Management
Flash Memory
Page 1
Page 0
Page 2
Page 255
……
Page 257
Page 256
Page 258
Page 511
……
……
Page M+1
Page M
Page M+2
Page M+255
……
Flash Controller
Hot Page 1
Cold Page 2
Hot Page 1
Cold Page 3
Hot Page 4
Cold Page 5
Hot Page 4
Hot Page 1
Hot Page 4
Hot Page 1
Hot Page 4
Hot Page 1
Can relax retention time for blocks with only write-hot pages
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 11: WARM: Write-hotness Aware Retention Management
Design Goal: Relax retention time w/o refresh for blocks that only hold write-hot data
Write-hot/write-cold data partitioning algorithm
Write-hotness aware flash policies
  Partition write-hot and write-cold data into separate blocks
  Skip refreshes for write-hot blocks
  More efficient garbage collection and wear-leveling
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 12: Write-hot/Write-cold Data Partitioning Algorithm
Cold Virtual Queue
Cold Data
……
①
TAIL
HEAD
1. Initially, all data is cold and is stored in cold virtual queue.
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Notes: Dynamically partitions write-hot and write-cold data into separate queues, allowing WARM to quickly adapt to workload behavior.

## Slide 13: Write-hot/Write-cold Data Partitioning Algorithm
Cold Virtual Queue
Cold Data
……
①
TAIL
HEAD
2. On write operation, data is pushed to tail of cold virtual queue.
②
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 14: Write-hot/Write-cold Data Partitioning Algorithm
Cold Virtual Queue
Cold Data
……
①
TAIL
HEAD
Recently written data is at tail of cold virtual queue.
②
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 15: Write-hot/Write-cold Data Partitioning Algorithm
Hot Virtual Queue
Hot Window
Hot Data
Cold Virtual Queue
Cooldown Window
Cold Data
……
④
②
①
③
TAIL
TAIL
HEAD
3, 4. On write hit in cooldown window, data is promoted to hot virtual queue.
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 16: Write-hot/Write-cold Data Partitioning Algorithm
Hot Virtual Queue
Hot Window
Hot Data
Cold Virtual Queue
Cooldown Window
Cold Data
……
④
②
①
③
TAIL
HEAD
TAIL
HEAD
Data is sorted by write-hotness in hot virtual queue.
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 17: Write-hot/Write-cold Data Partitioning Algorithm
Hot Virtual Queue
Hot Window
Hot Data
Cold Virtual Queue
Cooldown Window
Cold Data
……
④
⑤
②
①
③
TAIL
HEAD
TAIL
HEAD
5. On write hit in hot virtual queue, data is pushed to the tail.
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 18: Write-hot/Write-cold Data Partitioning Algorithm
Hot Virtual Queue
Hot Window
Hot Data
Cold Virtual Queue
Cooldown Window
Cold Data
……
④
⑥
⑤
②
①
③
TAIL
HEAD
TAIL
HEAD
6. Unmodified hot data will be demoted to cold virtual queue.
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 19: Conventional Flash Management Policies
Flash Translation Layer (FTL)
  Map data to erased blocks
  Translate logical page number to physical page number
Garbage Collection
  Triggered before erasing a victim block
  Remap all valid data on the victim block
Wear-leveling
  Triggered to balance wear-level among blocks
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 20: Write-hotness Aware Flash Policies
Flash Drive
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Block 8
Block 9
Block 10
Block 11
Hot Block Pool
Cold Block Pool
Block 0
Block 1
Block 2
Block 3
Block 4
Block 5
Block 6
Block 7
Block 8
Block 9
Block 10
Block 11
Write-hot data  naturally relaxed retention time
Program in block order
Garbage collect in block order
All blocks naturally wear-leveled
Write-cold data  lower write frequency, less wear-out
Conventional garbage collection
Conventional wear-leveling algorithm
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 21: Dynamically Sizing Hot & Cold Pools
All blocks are divided between the hot and cold block pools
Find the maximum hot pool size
Reduce hot virtual queue size to maximize cold pool lifetime
Size cooldown window to minimize ping-ponging of data between the two pools
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Notes: Guarantees data in the hot block pool is hot enough to skip refresh
Cold pool lifetime usually limits overall lifetime
Ping ponging hurts flash lifetime

## Slide 22: WARM Overhead
Dynamic window tuning counters: 4 × 32-bit counters
Cooldown window tracking: 128 × 8-byte block IDs
Hot pool tracking: 4 × 8-byte block IDs
Total Storage Overhead: 1.05KB
Minimal performance impact
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Notes: Two counters track the number of
writes to the hot and cold pools. A third counter tracks the
number of hot virtual queue write hits (6 in Figure 4). The
fourth counter tracks the number of pages moved from the
hot virtual queue into the cooldown window (5 in Figure 4).
We allocate a contiguous series
of block IDs to the hot pool, reducing the tracking overhead
to four registers totaling 32B: the starting ID of the series, the
current size of the pool, a pointer to the most recently written
block (i.e., the block at the tail of the hot virtual queue), and
a pointer to the oldest block yet to be erased (i.e., the block
at the head of the hot virtual queue).

## Slide 23: Evaluation Methodology
DiskSim 4.0 + SSD model
Parameter | Value
Page read to register latency | 25 μs
Page write from register latency | 200 μs
Block erase latency | 1.5 ms
Data bus latency | 50 μs
Page/block size | 8 KB/1 MB
Die/package size | 8 GB/64 GB
Total capacity | 256 GB
Over-provisioning | 15%
Endurance for 3-year retention time | 3,000 PEC
Endurance for 3-day retention time | 150,000 PEC
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 24: WARM Configurations
WARM-Only
  Relax retention time in hot block pool only
  No refresh needed
WARM+FCR
  First apply WARM-Only
  Then also relax retention time in cold block pool
  Refresh cold blocks every 3 days
WARM+ARFCR
  Relax retention time in both hot and cold block pools
  Adaptively increase the refresh frequency over time
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 25: Flash Lifetime Improvements
24
Chart: Norm Lifetime Improvement
| 15% Capacity Over-provisioning
Baseline | 1
WARM | 3.239
FCR | 8.0149
WARM+FCR | 10.4478
ARFCR | 10.6849
WARM+ARFCR | 12.8817
Baseline
WARM-Only
FCR
WARM+FCR
ARFCR
WARM+ARFCR
WARM-Only
3.24x
WARM+FCR
30%
WARM+ARFCR
21%
12.9x
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 26: WARM-Only: Endurance Improvement
Chart: 
| iozone | postmark | financial | homes | web-vm | hm | prn | proj | prxy | rsrch | src | stg | ts | usr | wdev | web | GMean
Cold pool | 0.9 | 0.98 | 0.30712 | 0.15239 | 0.13396 | 0.38488 | 0.9 | 0.24831 | 0.12781 | 0.063735 | 0.10053 | 0.078074 | 0.090213 | 0.18183 | 0.069639 | 0.15077 | 0.19722
Hot pool | 4.4536 | 0.10136 | 5 | 5 | 5 | 5 | 5 | 5 | 5 | 2.892 | 5 | 5 | 5 | 2.892 | 2.892 | 2.892 | 3.3929
3.58x
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 27: WARM+FCR: Reduction in Refresh Operations
Chart: % of Refresh Writes
| iozone | postmark | financial | proj | prxy | prn | hm | web-vm | src | stg | usr | web | rsrch | ts | wdev | homes | GMean
FCR | 0.013367 | 0.028721 | 0.48359 | 0.65361 | 0.7675 | 0.84382 | 0.91026 | 0.91325 | 0.93367 | 0.93379 | 0.94295 | 0.94661 | 0.95023 | 0.95406 | 0.96606 | 0.97177 | 0.53366
WARM+FCR | 0.0084218 | 0.019484 | 0.3699 | 0.53996 | 0.67255 | 0.76879 | 0.86293 | 0.86736 | 0.90029 | 0.90033 | 0.91458 | 0.92037 | 0.92588 | 0.93132 | 0.94993 | 0.95623 | 0.47527
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 28: WARM Performance Impact
Chart: Normalized Avg. Resp. Time
| iozone | postmark | financial | homes | web-vm | hm | prn | proj | prxy | rsrch | src | stg | ts | usr | wdev | web | GMean
Normalized average response time | 0.99879 | 1.0212 | 1.0023 | 1.0578 | 1.0126 | 1.0402 | 1.0268 | 1.0364 | 0.99391 | 1.0009 | 1.0008 | 1.0017 | 1.0002 | 1.0012 | 1.0011 | 1.0071 | 1.0125
Worst Case: < 6%
Avg. Case: < 2%
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Notes: Talk about partition -> garbage collection efficiency is lower in some cases

## Slide 29: Other Results in the Paper
Breakdown of write frequency into host writes, garbage collection writes, refresh writes in hot/cold block pools
  WARM reduces refresh writes significantly
  Low garbage collection overhead
Sensitivity to different capacity over-provisioning amounts
  WARM improves flash lifetime more as over-provisioning increases
Sensitivity to different refresh intervals
  WARM improves flash lifetime more as refresh frequency increases
Y. Luo et al., Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management. MSST 2015.
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 30: Conclusion
Flash memory can achieve up to 50x endurance improvement by relaxing retention time using refresh [Cai+ ICCD ’12]
  Problem: Refresh consumes majority of endurance improvement
  Goal: Reduce refresh overhead to increase flash memory lifetime
Key Observation: Refresh unnecessary for write-hot data
Write-hotness Aware Retention Management (WARM)
  Physically partition write-hot pages and write-cold pages within flash
  Apply different policies (garbage collection, wear-leveling, refresh) to each group
WARM w/o refresh improves lifetime by 3.24x w/ 1.05KB overhead
WARM w/ adaptive refresh improves lifetime by 12.9x (1.21x over refresh)
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 31: Other SAFARI Research on NAND Flash
Flash Memory Summit 2016 Talks
  Pre-Conference Seminar C: Onur Mutlu, Software-Transparent Crash Consistency for Persistent Memory [Ren+ MICRO ’15]
  Forum E-22: Yixin Luo, Practical Threshold Voltage Distribution Modeling [Luo+ JSAC ’16]
  Forum F-22: Onur Mutlu, Large-Scale Study of In-the-Field Flash Failures [Meza+ SIGMETRICS ’15]
Two posters in Booth 933
All available at http://www.ece.cmu.edu/~safari/
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 32: Other SAFARI Research on NAND Flash
Retention noise study and management [Cai+ ICCD ’12, Cai+ HPCA ’15]
Flash-based SSD prototyping and testing platform [Cai+ FCCM ’11]
Overall flash error analysis [Cai+ DATE ’12, Cai+ ITJ ’13]
Program and erase noise study [Cai+ DATE ’13]
Cell-to-cell interference study and tolerance [Cai+ ICCD ’13, Cai+ SIGMETRICS ’14]
Read disturb noise study and mitigation [Cai+ DSN ’15]
Flash errors in the field [Meza+ SIGMETRICS ’15]
Persistent memory [Ren+ MICRO ’15]
All available at http://www.ece.cmu.edu/~safari/
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 34: Write-hotness Aware Retention Management: Efficient Hot/Cold Data Partitioning for SSDs
Saugata Ghose
ghose@cmu.edu ▪ http://ece.cmu.edu/~saugatag/
joint work with Yixin Luo, Yu Cai, Jongmoo Choi, Onur Mutlu
August 10, 2016
Santa Clara, CA

## Slide 35: References to Papers and Talks
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 36: Our FMS Talks and Posters
Onur Mutlu, ThyNVM: Software-Transparent Crash Consistency for Persistent Memory, FMS 2016.
Onur Mutlu, Large-Scale Study of In-the-Field Flash Failures, FMS 2016.
Yixin Luo, Practical Threshold Voltage Distribution Modeling, FMS 2016.
Saugata Ghose, Write-hotness Aware Retention Management, FMS 2016.
Onur Mutlu, Read Disturb Errors in MLC NAND Flash Memory, FMS 2015.
Yixin Luo, Data Retention in MLC NAND Flash Memory, FMS 2015.
Onur Mutlu, Error Analysis and Management for MLC NAND Flash Memory, FMS 2014.
FMS 2016 posters:
  WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management
  Read Disturb Errors in MLC NAND Flash Memory
  Data Retention in MLC NAND Flash Memory
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Page 35 of 32

## Slide 37: Our Flash Memory Works (I)
Retention noise study and management
  Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, Flash Correct-and-Refresh: Retention-Aware Error Management for Increased Flash Memory Lifetime, ICCD 2012.
  Yu Cai, Yixin Luo, Erich F. Haratsch, Ken Mai, and Onur Mutlu, Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery, HPCA 2015.
  Yixin Luo, Yu Cai, Saugata Ghose, Jongmoo Choi, and Onur Mutlu, WARM: Improving NAND Flash Memory Lifetime with Write-hotness Aware Retention Management, MSST 2015.
Flash-based SSD prototyping and testing platform
  Yu Cai, Erich F. Haratsh, Mark McCartney, Ken Mai, FPGA-based solid-state drive prototyping platform, FCCM 2011.
Page 36 of 32
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion

## Slide 38: Our Flash Memory Works (II)
Overall flash error analysis
  Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, Error Patterns in MLC NAND Flash Memory: Measurement, Characterization, and Analysis, DATE 2012.
  Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Adrian Cristal, Osman Unsal, and Ken Mai, Error Analysis and Retention-Aware Error Management for NAND Flash Memory, ITJ 2013.
Program and erase noise study
  Yu Cai, Erich F. Haratsch, Onur Mutlu, and Ken Mai, Threshold Voltage Distribution in MLC NAND Flash Memory: Characterization, Analysis and Modeling, DATE 2013.
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Page 37 of 32

## Slide 39: Our Flash Memory Works (III)
Cell-to-cell interference characterization and tolerance
  Yu Cai, Onur Mutlu, Erich F. Haratsch, and Ken Mai, Program Interference in MLC NAND Flash Memory: Characterization, Modeling, and Mitigation, ICCD 2013.
  Yu Cai, Gulay Yalcin, Onur Mutlu, Erich F. Haratsch, Osman Unsal, Adrian Cristal, and Ken Mai, Neighbor-Cell Assisted Error Correction for MLC NAND Flash Memories, SIGMETRICS 2014.
Read disturb noise study
  Yu Cai, Yixin Luo, Saugata Ghose, Erich F. Haratsch, Ken Mai, and Onur Mutlu, Read Disturb Errors in MLC NAND Flash Memory: Characterization and Mitigation, DSN 2015.
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Page 38 of 32

## Slide 40: Our Flash Memory Works (IV)
Flash errors in the field
  Justin Meza, Qiang Wu, Sanjeev Kumar, and Onur Mutlu, A Large-Scale Study of Flash Memory Errors in the Field, SIGMETRICS 2015.
Persistent memory
  Jinglei Ren, Jishen Zhao, Samira Khan, Jongmoo Choi, Yongwei Wu, and Onur Mutlu, ThyNVM: Enabling Software-Transparent Crash Consistency in Persistent Memory Systems, MICRO 2015.
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Page 39 of 32

## Slide 41: Referenced Papers and Talks
All are available at
  http://users.ece.cmu.edu/~omutlu/projects.htm
  http://users.ece.cmu.edu/~omutlu/talks.htm
And, many other previous works on
  Challenges and opportunities in memory
  NAND flash memory errors and management
  Phase change memory as DRAM replacement
  STT-MRAM as DRAM replacement
  Taking advantage of persistence in memory
  Hybrid DRAM + NVM systems
  NVM design and architecture
Executive Summary • Motivation & Observations • WARM • Partitioning Algorithm • Flash Management • Evaluation • Conclusion
Page 40 of 32