## Slide 1: Reducing DRAM Latency at Low Cost by Exploiting Heterogeneity
Donghyuk Lee
Carnegie Mellon University
Notes: Hello. My name is Donghyuk Lee.
Thank you for attending my thesis defense.
Today, I will talk about reducing DRAM latency at low cost by exploiting heterogeneity.

## Slide 2
Problem: High DRAM Latency
processor
main memory
high latency
Major bottleneck for system performance
stalls: waiting for data
Notes: Modern system consists of processor and main memory.
Compared to the processor, main memory has high latency,
which leads to processor stall for waiting data from main memory.
Therefore, high DRAM latency is a major bottleneck for system performance.

## Slide 3
Chart: Year
| 2000 | 2003 | 2006 | 2008 | 2011
Capacity | 0.125 | 0.25 | 0.5 | 1 | 2
Latency (tRC) | 65 | 60 | 57.5 | 49.5 | 47.91
16X
-20%
Historical DRAM Trends
DRAM latency continues to be a critical bottleneck
Goal: Reduce DRAM latency at low cost
Notes: The figure shows the historical trends of DRAM during the last 12-years, from 2000 to 2011.
During this time, DRAM capacity has increased by 16 times.
On the other hand, DRAM latency has reduced by only 20%.
As a result, the high DRAM latency continues to be a critical bottleneck for system performance.
Our goal is reducing DRAM latency at low cost.

## Slide 4
Why is DRAM slow?
Notes: To achieve this goal, let me start with the fundamental question, why is DRAM slow?

## Slide 5
processor
main memory
peripheral logic
bank
mat
high latency
DRAM Organization
Notes: Right figure shows the picture of real DRAM chip,
which consists of multiple banks and peripheral logic for accessing cells in banks.
Each bank is subdivided into multiple mats.

## Slide 6
DRAM Cell Array: Mat
peripheral logic
cell
mat
mat
sense amplifier
wordline driver
cell
wordline
bitline
Notes: A mat consists of 2d cell array.
The cells are horizontally connected to wordline driver by wordline,
and vertically connected to a sense amplifier by bitline.

## Slide 7
Cell Array (Mat): High Latency
Notes: We observe that this mat organization is the dominant source of DRAM latency.
When accessing a mat in a bank, the command is first transferred to the mat.
Then, the corresponding wordline activates a row of cells.
and sense amplifiers detect data of activated cells.
After these mat operations, fractions of data in sense amplifiers are transferred to processor.

## Slide 8
DRAM Cell Array: High Latency
Outside mat
Inside mat
Narrow poly wire
  Large resistance
  Large capacitance
   Slow
Small cell
  Difficult to detect data in small cell
   Slow
Thick metal wire
  Small resistance
  Small capacitance
   Fast
Notes: In this example,
The control and data signals outside mat use thick metal wire,
which has small resistance and capacitance, leading to fast access.
On the other hand,
The control and data signals inside mat use narrow polysilicon wire,
which has large resistance and capacitance, leading to slow access.
Furthermore,
it takes long time to detect data from the small amount of charge in DRAM cell,
leading to slow access.

## Slide 9
DRAM cell array (mat) is
the dominant latency bottleneck due to three reasons
Notes: Therefore, DRAM cell array, mat, is the dominant latency bottleneck,
due to following three reasons.

## Slide 10
1. Long Narrow Wires
1
Long narrow wires:
enables small area,
increases latency
Notes: First reason is long narrow wires, as we described.
DRAM mat uses long wordline and bitline
to amortize the large area of the wordline driver and sense amplifier,
enabling small area, but, increasing latency.

## Slide 11
2. Operating Conditions
2
Operating conditions:
differing latencies,
uses the same standard value optimized for the worst case
e.g., small cell vs. normal cell
e.g., hot vs. cool
Notes: Second reason is that DRAM is accessed at different operating conditions.
One example is that, due to the process variation, each cell has different size.
Second example is that DRAM can be operated at different temperatures.
These two factors lead to different latency.
However, modern DRAM uses the standard latency, which is optimized for the worst case,
leading to increasing latency.

## Slide 12
3. Distance from Peripheral Logic
3
Distance from peripheral logic:
differing latencies
uses the same standard value optimized for the farthest cell
e.g., near cell vs. far cell
Notes: Third reason is that cells in a mat have different distances from peripheral logic.
Accessing a cell near to peripheral logic takes much less time compared to accessing a cell far from them.
However, modern DRAM uses the standard latency, which is optimized for the farthest cell,
leading to increasing latency.

## Slide 13
Three Sources of High Latency
2
Operating conditions
3
Distance from peripheral logic
1
Long narrow wires
Goal: Reduce DRAM latency at low cost
with three approaches
 AL-DRAM
AVA-DRAM
 TL-DRAM
Notes: Due to these three reasons,
DRAM cell array, mat, has high latency.
In this talk,
we evaluate impacts of these three latency sources,
and provide solutions to reduce latency at low cost with three approaches,
which are TL-DRAM, AL-DRAM, and AVA-DRAM.

## Slide 14
Thesis Statement
DRAM latency can be reduced
by enabling and exploiting
latency heterogeneity in DRAM
Notes: The thesis statement is that
DRAM latency can be reduced by enabling and exploiting latency heterogeneity in DRAM.

## Slide 15
Tiered-Latency DRAM:
Lowering Latency
by Modifying the Bitline Architecture
Approach 1
Lee et al., Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,
HPCA 2013
Outline
Prior Work
Future Research Direction
1. TL-DRAM
Reducing DRAM Latency
by Modifying Bitline Architecture
2. AL-DRAM
Optimizing DRAM Latency
for the Common-Case
3. AVA-DRAM
Lowering DRAM Latency
by Exploiting Architectural Variation
Reducing DRAM Latency
by Modifying Bitline Architecture
1. TL-DRAM
Notes: This is the outline of today’s talk.
We describe the three approaches for reducing DRAM latency.
Then, we explain related prior work and future research direction.
Let me introduce our first approach, TL-DRAM,
which lowering DRAM latency by modifying the DRAM bitline architecture.
This work is published at HPCA 2013.

## Slide 16
 Extremely large (≈100X cell)
Long Bitline: Amortize sense amplifier → Small area
Long Bitline: Large bitline cap. → High latency
Long Bitline  High Latency
DRAM cell
Sense amplifier
wordline
bitline
cell
Bitline: 512 cells
Notes: To understand why the subarray is so slow, let me take a look at the subarray organization.
A subarray consists of a two-dimensional grid of cells.
Each cell consists of one capacitor and one access transistor.
The cell’s capacitor is small and can store only a small amount of charge.
That is why a subarray also has sense-amplifiers,
which are specialized circuits that can detect the small amount of charge.
Unfortunately, a sense-amplifier size is about *100* times the cell size.
So, to amortize the area of the sense-amplifiers,
hundreds of cells share the same sense-amplifier through a long bitline.
However, a long bitline has a large capacitance that increases latency.
Therefore, the long bitline is the dominant source of high DRAM latency.

## Slide 17
Faster
Smaller
Short Bitline
Long Bitline
Trade-Off: Area vs. Latency
Trade-Off: Area vs. Latency
Notes: A naïve way to reduce the DRAM latency is to have short bitlines that have lower latency.
Unfortunately, short bitlines significantly increase the DRAM area.
Therefore, the bitline length exposes an important trade-off between area and latency.

## Slide 18
Chart: Latency (ns)
| 23.10725021132788 | 24.617764350044659 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Commodity DRAM
Long Bitline
Cheaper
Faster
Fancy DRAM
Short Bitline
GOAL
Trade-Off: Area vs. Latency
Notes: This figure shows the trade-off between DRAM area and latency.
Y-axis is the normalized DRAM area compared to a DRAM using 512 cells/bitline. A lower value is cheaper.
X-axis shows the latency in terms of tRC, an important DRAM timing constraint. A lower value is faster.
Commodity DRAMuse long bitlines to minimize area cost. On the other hand, shorter bitlines achieve lower latency at higher cost.
Our goal is to achieve the best of both worlds: low latency and low area cost.

## Slide 19
Short Bitline
Low Latency
Long Bitline
Small Area
Long Bitline
Low Latency
Short Bitline
Our Proposal
Small Area
Short Bitline  Fast
Need Isolation
Add Isolation Transistors
High Latency
Large Area
Approximating Best of Both Worlds
Notes: Remember, long bitline has small area but has high latency, while short bitline has low latency but has large area.
To achieve the best of both worlds, we first start from long bitline, which has small area.
After that, to achieve the low latency of short bitline, we divide the long bitline into two smaller segments.
The bitline length of the segment nearby the sense-amplifier is same as the length of short bitline.
Therefore, the latency of the segment is as low as the latency of the short bitline.
To access the other segment from sense amplifiers, we add isolation transistors that selectively connect the two segments.

## Slide 20
Low Latency
Our Proposal
Small Area
Long Bitline
Small Area
Long Bitline
High Latency
Short Bitline
Low Latency
Short Bitline
Large Area
Tiered-Latency DRAM
Low Latency
Small area using long bitline
Approximating Best of Both Worlds
Notes: This way, our proposed approach achieves small area and low latency.
We call this new DRAM architecture as Tiered-Latency DRAM

## Slide 21
Near Segment
Far Segment
Isolation Transistor
Divide a bitline into two segments with an isolation transistor
Sense Amplifier
Tiered-Latency DRAM
Notes: Again, the key idea is to divide the long bitline into two segments with isolation transistors.
The segment, directly connected to the sense amplifier, is called the near segment.
The other segment is called the far segment.

## Slide 22
Far Segment
Far Segment
Near Segment
Isolation Transistor
Turn off the isolation transistor
Isolation Transistor (off)
Sense Amplifier
Near Segment Access
Reduced bitline capacitance
 Low latency & low power
Reduced bitline length
Notes: When accessing the near segment, the isolation transistor is truned off such that the near segment is electrically decoupled from the far segment.
which leads to the reduced bitline length, which leads to reduced bitline capacitance.
Due to these two reasons, the near segment can be accessed with low latency and low power.

## Slide 23
Near Segment
Near Segment
Turn on the isolation transistor
Far Segment
Isolation Transistor
Isolation Transistor (on)
Sense Amplifier
Far Segment Access
Large bitline capacitance
Additional resistance of isolation transistor
Long bitline length
 High latency & high power
Notes: When accessing the far segment, the isolation transistor is turned on
such that the far segment is electrically connected to the sense amplifier
and the entire bitline is exposed to sense amplifier,
which leads to long bitline,
which leads to large bitline capacitance.
and also isolation transistors have resistance.
Due to these three reasons, accessing the far segment incurs high latency and high power.

## Slide 24
Chart: 
| commodity DRAM | near segment | far segment
Normalized Power Consumption | 1 | 0.49 | 1.49
Chart: 
| commodity DRAM | near segment | far segment
Latency | 1 | 0.56 | 1.23
Latency
Power
  –56%
  +23%
  –51%
  +49%
DRAM Latency (tRC)
DRAM Power
DRAM Area Overhead
  ~3%: Mainly due to the isolation transistors
  TL-DRAM
  Commodity DRAM
  Near Far
  Commodity DRAM
  Near Far
  TL-DRAM
  (52.5ns)
Commodity DRAM vs. TL-DRAM
Notes: This figure compares the latency.
Y-axis is normalized latency.
Compared to commodity DRAM, TL-DRAM’s near segment has 56% lower latency, while the far segment has 23% higher latency.
The right figure compares the power.
Y-axis is normalized power.
Compared to commodity DRAM, TL-DRAM’s near segment has 51% lower power consumption and the far segment has 49% higher power consumption.
Lastly, mainly due to the isolation transistor, Tiered-latency DRAM increases the die-size by about 3%.

## Slide 25
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | Near Segment Length (Cells) | Ref.
Near Segment | 21.5788 | 21.6222 | 21.7276 | 21.9379 | 22.3353 | 23.1073 | 24.6178 | 27.8312 | 35.4616 | 52.5
Far Segment | 66.5641 | 66.4584 | 66.5141 | 66.3587 | 66.4293 | 65.8399 | 64.9221 | 64.0756 | 60.8401 | 52.5
Latency (ns)
Longer near segment length leads to
higher near segment latency
Latency vs. Near Segment Length
Notes: The figure shows the latency of the near and far segments when varying near segment length.
X-axis is near segment length and Y-axis is Latency in nano seconds.
As the figure shows, a longer near segment length leads to higher near segment latency due to the increased bitline capacitance of the near segment.

## Slide 26
Chart: 
| 1 | 2 | 4 | 8 | 16 | 32 | 64 | 128 | 256 | 512 | Near Segment Length (Cells) | Ref.
Near Segment | 21.5788 | 21.6222 | 21.7276 | 21.9379 | 22.3353 | 23.1073 | 24.6178 | 27.8312 | 35.4616 | 52.5
Far Segment | 66.5641 | 66.4584 | 66.5141 | 66.3587 | 66.4293 | 65.8399 | 64.9221 | 64.0756 | 60.8401 | 52.5
Latency (ns)
Far segment latency is higher than
commodity DRAM latency
  Far Segment Length = 512 – Near Segment Length
Latency vs. Near Segment Length
Notes: For the far segment, a shorter far segment length leads to lower latency. However, the far segment latency is higher than commodity DRAM latency.

## Slide 27
Chart: Latency (ns)
| 23.10725021132788 | 24.617764350044659 | 27.831175560551241 | 35.461599363785872 | 52.5
 | 3.7551 | 2.2857 | 1.551 | 1.1837 | 1
64
32
128
256
512 cells/bitline
Cheaper
Faster
Near Segment
Far Segment
GOAL
Trade-Off: Area vs. Latency
Notes: Again, the figure shows the trade-off between area and latency in existing DRAM.
Unlike existing DRAM, TL-DRAM achieves low latency using the near segment while increasing the area by only 3%.
Although the far segment has higher latency than commodity DRAM, we show that efficient use of the near segment enables TL-DRAM to achieve high system performance.

## Slide 28
TL-DRAM is a substrate that can be leveraged by the hardware and/or software
  Use near segment as hardware-managed cache to far segment
Leveraging Tiered-Latency DRAM
Notes: There are multiple ways to leverage the TL-DRAM substrate by hardware or software.
In this slide, I describe many such ways.
First, the near segment can be used as a hardware-managed inclusive cache to the far segment.
Second, the near segment can be used as a hardware-managed exclusive cache to the far segment.
Third, the operating system can intelligently allocate frequently-accessed pages to the near segment.
Forth mechanism is to simple replace DRAM with TL-DRAM without any near segment handling
While our paper provides detailed explanations and evaluations of first three mechanism,
in this talk, we will focus on the first approach, which is to use the near segment as a hardware managed cache for the far segment.

## Slide 29
Chart: 
| IPC Improvement
BBC | 0.12737
Chart: 
| Normalized Power Consumption
BBC | 0.76365
IPC Improvement
Normalized Energy
12.7%
–23%
Using near segment as a cache improves performance and reduces energy consumption
Performance & Energy Evaluation
Notes: This figure shows the IPC improvement of our three caching mechanisms over commodity DRAM.
All of them improve performance and benefit-based caching shows maximum performance improvement by 12.7%.
The right figure shows the normalized power reduction of our three caching mechanisms over commodity DRAM.
All of them reduce power consumption and benefit-based caching shows maximum power reduction by 23%.
Therefore, using near segment as a cache improves performance and reduces power consumption at the cost of 3% area overhead.

## Slide 30
Observation
  Long bitlines are the dominant source of DRAM latency
Idea
  Divide a long bitline into two shorter segments
     Fast and slow segments
Tiered-latency DRAM: Enables latency heterogeneity
  Can leverage this in many ways to improve performance and reduce power consumption
Performance & Power Evaluation
  When the fast segment is used as a cache to the slow segment
   Significant performance improvement (>12%) and power
  reduction (>23%) at low area cost (3%)
Summary: TL-DRAM
Notes: Let me conclude
DRAM timing parameters are dictated by the worst case cell.
We propose Adaptive-Latency DRAM that optimizes DRAM timing parameters for common cases
Our characterization shows the significant potential to lower DRAM timing parameters.
Our real system evaluation shows that our mechanism provides significant performance improvement without introducing errors.

## Slide 31
Adaptive-Latency DRAM:
Optimizing DRAM Latency
for the Common Operating Conditions
Approach 2
Lee et al., Adaptive-Latency DRAM: Optimizing DRAM Timing for the Common-Case,
HPCA 2015
Outline
Prior Work
Future Research Direction
1. TL-DRAM
Reducing DRAM Latency
by Modifying Bitline Architecture
2. AL-DRAM
Optimizing DRAM Latency
for the Common-Case
3. AVA-DRAM
Lowering DRAM Latency
by Exploiting Architectural Variation
Reducing DRAM Latency
by Modifying Bitline Architecture
1. TL-DRAM
Optimizing DRAM Latency
for the Common Case
2. AL-DRAM

## Slide 32
DRAM Stores Data as Charge
1. Sensing
2. Restore
3. Precharge
DRAM cell
Sense amplifier
Three steps of charge movement
Notes: The right figure shows DRAM organization which is consists of DRAM cells and sense-amplifiers.
There are three steps for accessing DRAM.
First, when DRAM selects one of rows in its cell array, the selected cells drive their charge to sense-amplifiers.
Then, sense-amplifiers detect the charge, recognizing data of cells.
We call this operation as sensing.
Second, after sensing data from DRAM cells, sense-amplifiers drive charge to the cells for reconstructing original data.
We call this operation as restore.
Third, after restoring the cell data, DRAM deselects the accessed row and puts the sense-amplifiers to original state for next access.
We call this operation as precharge.
As shown in these three steps, DRAM operation is charge movement between cell and sense-amplifier.

## Slide 33
Sensing
Restore
Timing Parameters
Data 0
Data 1
cell
time
charge
Sense amplifier
DRAM Charge over Time
Why does DRAM need the extra timing margin?
In theory
margin
cell
Sense amplifier
In practice
Notes: Timing parameters exist to ensure sufficient movement of charge.
The figure shows the timeline for accessing DRAM in X-axis and Y-axis shows the charge amount in DRAM cell and sense-amplifier.
When selecting a row of cells, each cell drives their charge toward to the corresponding sense-amplifier.
If driven charge is more than enough to detect the data, the sense-amplifier starts to restore data by driving charge toward the cell.
This restore operation finishes when the cell is fully charged.
Ideally, DRAM timing parameters are just enough for the sufficient movement of charge.
However, in practice, there are large margin in DRAM timing parameters.
Why are these margin required?

## Slide 34
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cell that can store small amount of charge
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Two Reasons for Timing Margin
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cell that can store small amount of charge;
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cells that can store large amount of charge
Notes: There are two reasons for the margin in DRAM timing parameters.
First is process variation and second is temperature dependence.
Let me introduce the first factor, process variation.

## Slide 35
Same size 
Same charge 
Different size 
Different charge 
Same latency
Different latency
Large variation in cell size 
Large variation in charge 
Large variation in access latency
DRAM Cells are Not Equal
Real
Ideal
Largest cell
Smallest cell
Notes: Ideally, DRAM would have uniform cells which have same size, thereby having same access latency.
Unfortunately, due to process variation, each cell has different size, thereby having different access latency.
Therefore, DRAM shows large variation in both charge amount in its cell and access latency to its cell.

## Slide 36
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cells that can store large amount of charge
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Two Reasons for Timing Margin
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Notes: There are two reasons for the margin in DRAM timing parameters.
First is process variation and second is temperature dependence.
Let me introduce the first factor, process variation.

## Slide 37
Cells store small charge at high temperature
and large charge at low temperature
 Large variation in access latency
Charge Leakage Temperature
Room Temp.
Hot Temp. (85°C)
Small leakage
Large leakage
Notes: DRAM leakage increases the variation.
DRAM loses their charge over time and loses more charge at higher temperature.
Therefore, DRAM cell has smallest charge when operating at hot temperature, for example 85C which is the highest temperature guaranteed by DRAM standard.
This temperature dependence increases the variation in DRAM cell charge.

## Slide 38
DRAM Timing Parameters
DRAM timing parameters are dictated by the worst case
  The smallest cell with the smallest charge in all DRAM products
  Operating at the highest temperature
Large timing margin for the common case
Can lower latency for the common case

## Slide 39: DRAM Testing Infrastructure
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Notes: This is the photo of our infrastructure, that we built mostly from scratch.
For higher throughput, we employ eight FPGAs, all of which are enclosed in thermally-regulated environment.

## Slide 40
Typical DIMM at
Low Temperature
Obs 1. Faster Sensing
More charge
Strong charge
flow
Faster sensing
Typical DIMM at Low Temperature
 More charge  Faster sensing
Timing
(tRCD)
17% ↓
No Errors
115 DIMM
characterization
Notes: First step in DRAM operation is sensing.
In typical case, there are more charge in DRAM cell compared to the worst case.
The excessive charge enables stronger charge drive to sense-amplifier.
Then, sense-amplifier can detect data of DRAM cell fast, thereby complete sensing operation fast.
In our DRAM latency profiling results of 115 DRAM modules,
we observe that 17% potential reduction for the corresponding timing parameters of sensing.
As a result, more charge in typical cases lead to fast sensing.

## Slide 41
Obs 2. Reducing Restore Time
Larger cell &
Less leakage 
Extra charge
No need to fully
restore charge
Typical DIMM at lower temperature
 More charge  Restore time reduction
Read (tRAS)
37% ↓
Write (tWR)
54% ↓
No Errors
115 DIMM
characterization
Typical DIMM at
Low Temperature
Notes: Second step in DRAM operation is restore.
Due to larger size and less leakage, typical DRAM cells have more charge than the worst cell.
Even though typical DRAM does not restore the excessive charge during restore operation,
eventually the typical cell has more charge than the worst case cell, guaranteeing reliable operations.
By reducing this restore time in DRAM read/write, our DRAM latency characterization shows significant potential to reduce corresponding timing parameters. For example, 37% for read and 54% for write.
As a result, more charge in typical cases enables restore time reduction.

## Slide 42
Empty (0V)
Full (Vdd)
Half
Obs 3. Reducing Precharge Time
Bitline
Sense amplifier
Sensing
Precharge
Precharge ?
– Setting bitline to half-full charge
Typical DIMM at
Low Temperature
Notes: Third step is precharge. Previously we explained the precharge simply as going back to original state.
Let me introduce more details about precharge.
To detect data in DRAM cell, DRAM has sense-amplifier and wire connection to the bitline.
DRAM preserve their a bit of data in two charge state, empty and fully charged.
During sensing and restore, the bitline moves to either of these two states.
After finishing the access, the bitline should be go back to the half of these two state.
We call this precharge. Unfortunately, bitline is usually long by connecting hundred of cells such that it takes long time for precharge.

## Slide 43
Empty (0V)
Full (Vdd)
Half
bitline
Not fully precharged
More charge
 strong sensing
Access empty cell
Access full cell
Timing
(tRP)
35% ↓
No Errors
115 DIMM
characterization
Typical DIMM at Lower Temperature
 More charge  Precharge time reduction
Obs 3. Reducing Precharge Time
Notes: Let us observe the impact of reducing precharge with a simple example.
The sense-amplifier first accesses an empty cell then not fully precharged by reducing corresponding timing parameter.
Then DRAM next access a fully charged cell.
Due to the bias in the bitline, it takes longer time to access the fully charged cell.
However, if the cell has much excessive charge, the strong charge flow overcomes the bias in the bitline, leading to reliable access.
Our DRAM latency evaluation shows that in typical case, we can reduce corresponding timing parameter by 35% without errors.
Therefore, more charge in typical cases enables precharge time reduction.

## Slide 44: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer profiles multiple sets of reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature

## Slide 45
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi-Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
Real System Evaluation
AL-DRAM provides high performance improvement, greater for multi-core workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 46
Summary: AL-DRAM
Observation
  DRAM timing parameters are dictated by the worst-case cell (smallest cell at highest temperature)
Our Approach: Adaptive-Latency DRAM (AL-DRAM)
  Optimizes DRAM timing parameters for the common case (typical DIMM operating at low temperatures)
Analysis: Characterization of 115 DIMMs
  Great potential to lower DRAM timing parameters (17 – 54%) without any errors
Real System Performance Evaluation
  Significant performance improvement (14% for memory-intensive workloads) without errors (33 days)
Notes: Let me summarize.
DRAM timing parameters are dictated by the worst case cell.
We propose Adaptive-Latency DRAM that optimizes DRAM timing parameters for common cases
Our characterization shows the significant potential to lower DRAM timing parameters.
Our real system evaluation shows that our mechanism provides significant performance improvement without introducing errors.

## Slide 47
AVA-DRAM:
Lowering DRAM Latency
by Exploiting Architectural Variation
Approach 3
Lee et al., AVA-DRAM: Reducing DRAM Latency by Exploiting Architectural Variation,
under submission
Outline
Prior Work
Future Research Direction
1. TL-DRAM
Reducing DRAM Latency
by Modifying Bitline Architecture
2. AL-DRAM
Optimizing DRAM Latency
for the Common-Case
3. AVA-DRAM
Lowering DRAM Latency
by Exploiting Architectural Variation
Optimizing DRAM Latency
for the Common Case
2. AL-DRAM
Lowering DRAM Latency
by Exploiting Architectural Variation
3. AVA-DRAM
Notes: So far, we have introduced AL-DRAM
which optimizes DRAM latency for the common-case.
We move on our third approach, AVA-DRAM,
which reduces DRAM latency by exploiting architectural variation.
This work is under submission of a conference.

## Slide 48
Inherently fast
inherently slow
Architectural Variation
slow
fast
slow
fast
Variability in cell access times is
caused by the physical organization of DRAM
sense amplifier
wordline driver
across row
distance from sense amplifier
across column
distance from wordline driver
Notes: As we described, cells in a mat have different distances from peripheral logic.
Cells in different rows have different distance from the sense amplifiers.
Cells in different columns have different distance from the wordline drivers.
Therefore, some regions are inherently faster than other regions,
and some regions are inherently slower than other regions.
We call this architectural variation.

## Slide 49
Our Approach
Experimental study for architectural variation
  Goal: Identify & characterize inherently slower regions
  Methodology: Profiling 96 real DRAM modules by using FPGA-based DRAM test infrastructure
Exploiting architectural variation
  AVA Online Profiling: Dynamic & low cost latency optimization mechanism
  AVA Data Shuffling: Improving reliability by avoiding ECC-uncorrectable errors
Experimental study of architectural variation
  Goal: Identify & characterize inherently slower regions
  Methodology: Profile 96 real DRAM modules by using FPGA-based DRAM test infrastructure
Notes: In order to exploit architectural variation for reducing DRAM latency,
we first do experimental study to identify and characterize architectural variation.
We evaluate 96 real DRAM modules
by using our FPGA-based DRAM test infrastructure,
similar to what we used for AL-DRAM.
We then propose two mechanisms to leverage architectural variation for reducing DRAM latency.
Let me describe our experimental study.

## Slide 50
Internal address
External address
Challenge: External ≠ Internal
External address ≠ Internal address
DRAM chip
IO interface
Address mapping
Notes: As a first step, we explain a challenge for profiling architectural variation.
This figure shows a DRAM chip, which consists of the cell array and IO interface.
To access DRAM, we need to issue commands with address, which we call external address.
Then, the cell array receives internal address, corresponding to the external address.
The problem is that this internal and external addresses do not need to be equal,
and the mapping between external an internal addresses is not exposed to out of DRAM vendors.
Therefore, it makes difficult to know the relative cell locations in a mat, corresponding to the external address.

## Slide 51
Expected Characteristics
Variation
  Some regions are slower than others
  Some regions are more vulnerable than others
  when accessed with reduced latency
Repeatability
  Latency (error) characteristics repeat periodically,
  if the same component (e.g., mat) is duplicated
Similarity
  Across different organizations (e.g., chip/DIMM)
  if they share same design
Notes: Instead, we provide expected characteristics if there exists architectural variation.
First, we expect the variation in latency across regions in a mat.
For example, some regions are slower than other regions,
or some regions are more vulnerable than other regions when accessing reduced latency.
Second, we expect that latency or error characteristics periodically repeat
because mats are duplicated to form a bank.
Third, we expect that latency or error characteristic is similar across different chip/DIMM,
if they are manufactured by the same company at the same manufacturing time.

## Slide 52
1. Variation & Repeatability in Rows
row decoder
512 rows
512 rows
sweep across rows
Latency characteristics vary across 512 rows
global wordline
row decoder
Same organization repeats every 512 rows
Latency characteristics repeat every 512 rows
Notes: First, we observe the variation in rows caused by variation in distance between cell and sense amplifier.
A row of mats are connected to row decoder by global wordline.
Majority DRAMs use 512 rows in a mat,
And cells in different rows have different distance from sense amplifier, leading to variation in latency.
Since mats are duplicated to build bigger cell array,
latency characteristic repeats every 512 rows when sweeping rows.

## Slide 53
1.1. Variation in Rows
Chart: 
Chart: 
Chart: 
row addr. (mod. 512)
row addr. (mod. 512)
row addr. (mod. 512)
Erroneous Request Count
Random
Errors
Periodic
Errors
Mostly
Errors
10.0 ns
7.5 ns
5.0 ns
tRP
Erroneous Request Count
Notes: We sweep rows in a bank by reducing a timing parameter, tRP from 10ns to 5ns.
Left figure shows tRP 10ns evaluation.
Y-axis shows erroneous request count and
X-axis shows row address from 0 to 512.
The erroneous request count are aggregated as modulo of 512.
In 10ns tRP, we observe mostly random errors,
In 7.5ns tRP, we observe large variation in erroneous request count which shows some periodicity.
In 5ns tRP, we observe most requests shows errors.
We focus more on the operating condition, 7.5ns, that shows large variation in erroneous request count.

## Slide 54
1.2. Repeatability in Rows
Chart: 
Chart: 
Erroneous Request Count
row address (mod. 512)
row address
Aggregated & Sorted
Apply sorted order to each 512-row group
Error (latency) characteristics periodically repeat
every 512 rows
Notes: In left figure, we sort the rows as erroneous request count.
As we can see, the erroneous request mostly linearly increase.
Then, we apply this sorted order of rows to each 512-row group in right figure.
As we can see, we observe similar characteristics every 512-row group.
Therefore, error characteristic periodically repeats every 512 rows.
We conclude that the distance from sense amplifier expose variation in erroneous request count,
which also expose variation in latency.

## Slide 55
2. Variation in Columns
row decoder
IO interface
64 bits
8 bits X 8 burst
global sense amplifier
column
column
column
column
Different columns  data from different locations
 different characteristics
global wordline
Notes: Second, we observe the latency variation in columns caused by variation in distance between cell and wordline driver.
A row of mats are connected to row decoder by global wordline.
To transfer data to offchip,
sense amplifiers are connected to global sense amplifier and
the global sense amplifier is connected to IO interface, which is connected to the memory channel.
When a row of cells are activated through both global wordline and wordline,
The time to access cells are varied, due to the distance from wordline driver and row decoder.
Then, sense amplifiers detect all data from the activated cells.
Then, fractions of data in sense amplifiers are transferred to global sense amplifier, based on the issued column address.
Therefore, on read requests with different columns,
cells in different locations are transferred to global sense amplifier, which leads to different latency characteristics.

## Slide 56
2. Variation in Columns
Erroneous Request Count
Chart: 
Chart: 
Error (latency) characteristics in columns have
specific patterns (e.g., 16 or 32 row groups)
Notes: We sweep columns at tRP 7.5ns, the same as row address sweeping evaluation.
We observe that two specific patterns in this DRAM modules,
Some rows induces more errors from 96th to 128th row as shown in left figure,
Some rows induces more errors from 80th to 96th row as shown in right figure.
Unfortunately, due to mismatch between external and internal address,
it is not possible to further analyze the root cause of this.
However, this results shows that specific regions in a mat induce induces more errors,
and thus the regions are slower than other regions

## Slide 57
3. Variation in Data Bits
row decoder
IO interface
64 bits
8 bits X 8 burst
global sense amplifier
Data in a request  transferred as multiple data bursts
Notes: Data in global sense amplifier are transferred to IO interface simultaneously through 64-bit wide bus,
Then IO interface transfer the 64-bit data to memory channel as 8 bursts of 8-bit data.
Therefore,
Data in a request transfers as multiple data bursts.

## Slide 58
8-bit data bus per chip
64-bit data bus in memory channel
Processor
DIMM
Read request
3. Variation in Data Bits
64-bit data from different locations in the same row in the same chip
Data bits in a request  different characteristics
Notes: The figure plots the memory channel connection between process and DRAM module.
Usually memory channel has 64-bit data bus that consist of eight 8-bit data bus, dedicated to each DRAM chip.
Each DRAM chip transfer data as eight burst of eight bit data.
Therefore, 64-bit data from a DRAM chip are from different locations in a row.
Therefore, data bits in a request might have different error characteristics.

## Slide 59
3. Variation in Data Bits
Chart: 
Error Count
data bits in 8 data burst
Specific bits in a request  induce more errors
Notes: The figure shows that error count in Y-axis and data bits in 64-bit data in eight data burst.
As we can see, specific bits in a request induce more errors.

## Slide 60
Exploiting architectural variation
  AVA Online Profiling: Dynamic & low cost latency optimization mechanism
  AVA Data Shuffling: Improving reliability by avoiding ECC uncorrectable errors
Our Approach
Experimental study for architectural variation
  Goal: Identify & characterize inherently slower regions
  Methodology: Profiling 96 real DRAM modules by using FPGA-based DRAM test infrastructure
Experimental study of architectural variation
  Goal: Identify & characterize inherently slower regions
  Methodology: Profile 96 real DRAM modules by using FPGA-based DRAM test infrastructure
Exploiting architectural variation
  AVA Online Profiling: Dynamic & low cost latency optimization mechanism
  AVA Data Shuffling: Improving reliability by avoiding ECC-uncorrectable errors
Notes: So far, we observe architectural variation in DRAM by profiling real DRAM modules.
Now, we move on how we can exploit architectural variation to reliably reduce DRAM latency.
First mechanism, AVA Online Profiling is a dynamic and low cost latency optimization.
Second mechanism, AVA Data Shuffling is a technique to reduce ECC uncorrectable errors.

## Slide 61
1. Challenges of Lowering Latency
Static DRAM latency
  DRAM vendors need to provide standard timings, increasing testing costs
  Doesn’t take into account latency changes over time (e.g., aging and wear out)
Conventional online profiling
  Takes long time (high cost) to profile all DRAM cells
Goal: Dynamic & low cost online latency optimization
Notes: We first explain challenges for reducing DRAM latency.
The first problem is static DRAM latency.
In the policy using static DRAM latency, DRAM vendors need to provide standard timing parameters, increasing test cost.
Furthermore, the static DRAM latency does not take into account latency changes over time.
A solution to mitigate the problem of static DRAM latency is using online profiling mechanism.
However, conventional online profiling takes long time to test all DRAM cells.
Our goal is enable dynamic and low cost online latency optimization.

## Slide 62
1. AVA Online Profiling
inherently slow
Profile only slow regions to determine latency
 Dynamic & low cost latency optimization
sense amplifier
wordline driver
Architectural-Variation-Aware
Notes: We propoe AVA Online profiling.
The key idea is profiling only slow regions to determine latency, leading to low cost online DRAM test.

## Slide 63
inherently slow
1. AVA Online Profiling
slow cells
architectural
variation
process
variation
localized error
random error
online profiling
error-correcting code
Combining error-correcting code & online profiling
 Reliably reduce DRAM latency
Architectural-Variation-Aware
sense amplifier
wordline driver
Notes: However, due to the process variation, some cells are more vulnerable than other cells, as the figure show.
These cells are randomly distributed while cells in the slow regions cause localized error.
To address both type of cells,
We integrate conventional ECC to correct the process variation induced errors.
Therefore, combining ECC and online profiling leads to reliably reducing DRAM latency.

## Slide 64
8-bit data bus per chip
64-bit data bus in memory channel
2. Challenge of Conventional ECC
Processor
DIMM
Read request
Error-Correcting Code (ECC)
Notes: Let me move on our second mechanims.
The figure now shows one more DRAM chips and its dedicated channel.

## Slide 65
8-bit data bus per chip
Processor
DIMM
error
uncorrectable by ECC
uncorrectable by ECC
Conventional ECC leads to more uncorrectable errors due to architectural variation
2. Challenge of Conventional ECC
Notes: The challenge in conventional ECC with reducing DRAM latency is that
due to architectural variation, specific bits induces more errors which exist in the same ECC codeword.
Therefore, it induces ECC uncorrectable errors.

## Slide 66
8-bit data bus per chip
2. AVA Data Shuffling
Processor
DIMM
error
uncorrectable by ECC
uncorrectable by ECC
Shuffle data burst
& shuffle rows
 Reduce uncorrectable errors
shuffling rows
Architectural-Variation-Aware
Notes: Our mechanism, AVA Data Shuffling, is
First distribute this architectural variation induced error over other data bursts.
Then, we shuffle accessed row per chip.
For example, some DRAM chips activated a more error induced row,
while other DRAM chips activated a less error induced rows.
Using this two mechanisms, AVA Data Shuffling reduces ECC uncorrectable error.

## Slide 67
2. AVA Data Shuffling
Chart: 
ECC w/o AVA Suffling | 9.999e-05 | 0.00019998 | 0 | 0.024098 | 0.021598 | 0.035696 | 0.037896 | 0.042896 | 0.075592 | 0.087791 | 0.061194 | 0.062394 | 0.034397 | 0.048095 | 0.10299 | 0.14469 | 0.12119 | 0.24758 | 0.16448 | 0.27927 | 0.19478 | 0.17878 | 0.18438 | 0.14009 | 0.27817 | 0.35106 | 0.39196 | 0.25627 | 0.15648 | 0.35966 | 0.22738 | 0.47225 | 0.51925 | 0.16069
ECC with AVA Suffling | 0 | 0.00049995 | 0.0023998 | 0.022398 | 0.026697 | 0.038996 | 0.090691 | 0.09739 | 0.068893 | 0.061594 | 0.10189 | 0.10969 | 0.14249 | 0.16388 | 0.21278 | 0.24128 | 0.31257 | 0.18908 | 0.31997 | 0.25137 | 0.35696 | 0.43016 | 0.42566 | 0.47055 | 0.38566 | 0.32827 | 0.29857 | 0.46245 | 0.67973 | 0.50175 | 0.76042 | 0.52775 | 0.48075 | 0.25949
Uncorrectable | 0.9999 | 0.9993 | 0.9976 | 0.9535 | 0.9517 | 0.92531 | 0.87141 | 0.85971 | 0.85551 | 0.85061 | 0.83692 | 0.82792 | 0.82312 | 0.78802 | 0.68423 | 0.61404 | 0.56624 | 0.56334 | 0.51555 | 0.46935 | 0.44826 | 0.39106 | 0.38996 | 0.38936 | 0.33617 | 0.32067 | 0.30947 | 0.28127 | 0.16378 | 0.13859 | 0.012199 | 0 | 0 | 0.57982
AVA Shuffling reduces uncorrectable errors significantly
Chart: 
ECC w/o AVA Suffling | 9.999e-05 | 0.00019998 | 0 | 0.024098 | 0.021598 | 0.035696 | 0.037896 | 0.042896 | 0.075592 | 0.087791 | 0.061194 | 0.062394 | 0.034397 | 0.048095 | 0.10299 | 0.14469 | 0.12119 | 0.24758 | 0.16448 | 0.27927 | 0.19478 | 0.17878 | 0.18438 | 0.14009 | 0.27817 | 0.35106 | 0.39196 | 0.25627 | 0.15648 | 0.35966 | 0.22738 | 0.47225 | 0.51925 | 0.16069
ECC with AVA Suffling | 0 | 0.00049995 | 0.0023998 | 0.022398 | 0.026697 | 0.038996 | 0.090691 | 0.09739 | 0.068893 | 0.061594 | 0.10189 | 0.10969 | 0.14249 | 0.16388 | 0.21278 | 0.24128 | 0.31257 | 0.18908 | 0.31997 | 0.25137 | 0.35696 | 0.43016 | 0.42566 | 0.47055 | 0.38566 | 0.32827 | 0.29857 | 0.46245 | 0.67973 | 0.50175 | 0.76042 | 0.52775 | 0.48075 | 0.25949
Uncorrectable | 0.9999 | 0.9993 | 0.9976 | 0.9535 | 0.9517 | 0.92531 | 0.87141 | 0.85971 | 0.85551 | 0.85061 | 0.83692 | 0.82792 | 0.82312 | 0.78802 | 0.68423 | 0.61404 | 0.56624 | 0.56334 | 0.51555 | 0.46935 | 0.44826 | 0.39106 | 0.38996 | 0.38936 | 0.33617 | 0.32067 | 0.30947 | 0.28127 | 0.16378 | 0.13859 | 0.012199 | 0 | 0 | 0.57982
33 DIMMs
average
Fractions of Errors
Notes: This figure shows the effectiveness of ECC with/without AVA Shuffling.
We reduces tRP timing parameters and plot the fractions of uncorrectable and correctable errors in 33 DRAM modules.
The gray portion represents the fractions of uncorrectable errors and blue bars represent ECC correctable error without AVA Shuffling.
Then, we apply AVA Shuffling on top of ECC and plot how much additional fraction of errors can be corrected in red bars.
By using our mechanism, 26% of uncorrectable errors on average of all DRAM modules can be corrected,
which are not possible to be correction with conventional ECC.

## Slide 68
Latency Reduction
AVA-DRAM reduces latency significantly
Read
Write
Chart: 
| 55°C | 85°C | 55°C | 85°C | 55°C | 85°C | AL-DRAM | AVA Profiling | AVA Profiling + Shuffling
Latency Reduction | 0.31202 | 0.25527 | 0.35118 | 0.3464 | 0.36569 | 0.358
Chart: 
| 55°C | 85°C | 55°C | 85°C | 55°C | 85°C | AL-DRAM | AVA Profiling | AVA Profiling + Shuffling
Latency Reduction | 0.36561 | 0.27539 | 0.394 | 0.38718 | 0.41294 | 0.40274
Latency Reduction
Notes: The figure compares latency reduction by using AL-DRAM, AVA Profiling, and both AVA Profiling and Shuffling.
As we can, using AVA profiling and shuffling enables more latency reduction compared to AL-DRAM.
This is mainly because ECC corrects the worst cells in a DRAM module, reducing more latency.
Therefore, we conclude that AVA-DRAM reduces latency significantly.

## Slide 69
System Performance Improvement
Chart: 
| 1-core | 2-core | 4-core | 8-core
AL-DRAM | 0.070305 | 0.1167 | 0.11012 | 0.11484
AVA Profiling | 0.092019 | 0.14709 | 0.13739 | 0.13754
AVA Profiling + Shuffling | 0.09477 | 0.15082 | 0.14199 | 0.14101
Performance Improvement
AVA-DRAM improves performance significantly
Notes: The figure compares system performance improvement
by using AL-DRAM, AVA Profiling, and both AVA Profiling and Shuffling.
Due to the latency reduction, our mechanisms provide significant performance improvement compared to baseline conventional DRAM.
Compared to AL-DRAM, AVA-DRAM improves performance without increasing test cost during manufacturing time,
and optimizes DRAM latency when DRAM latency characteristic changes over time.

## Slide 70
Summary: AVA-DRAM
Observation: Architectural Variation
  DRAM has inherently slow regions due to its cell array organization, which leads to high DRAM latency
Our Approach
  AVA Profiling: Profile only inherently slow regions to determine latency  dynamic & low cost latency optimization
  AVA Shuffling: Distribute data from slow regions to different ECC code words  avoid uncorrectable errors
Analysis: Characterization of 96 DIMMs
  Great potential to lower DRAM timing parameters
System Performance Evaluation
  Significant performance improvement (15% for memory-intensive workloads)
Notes: Let me summarize.
DRAM has inherently slow regions due to its cell array organization, which leads to high DRAM latency.
We call this architectural variation.
We propose two mechanisms to exploit architectural variation for reducing DRAM latency.
First is AVA profiling, a dynamic & low cost latency optimization technique.
Second is AVA Shuffling, a mechanism to reduce ECC uncorrectable errors.
Our characterization shows the significant potential to lower DRAM timing parameters.
Our system performance evaluation shows that
our mechanisms provide significant performance improvement.

## Slide 71
Outline
Prior Work
Future Research Direction
1. TL-DRAM
Reducing DRAM Latency
by Modifying Bitline Architecture
2. AL-DRAM
Optimizing DRAM Latency
for the Common Case
3. AVA-DRAM
Lowering DRAM Latency
by Exploiting Architectural Variation
Lowering DRAM Latency
by Exploiting Architectural Variation
3. AVA-DRAM
Prior Work
Notes: Let me explain related prior works.

## Slide 72
Prior Work
Low latency DRAM
  Having short bitline
  Heterogeneous bitline
Cached DRAM
DRAM with higher parallelism
  Subarray level parallelism
  Parallelizing refreshes with accesses
Memory scheduling
  Memory scheduling for more parallelism
  Application-Aware Memory Scheduling
Caching, Paging, and Prefetching
Notes: Several DRAM use shorter bitline to reduce DRAM latency.
However, this approach significantly increases DRAM area.
Son et al. propose a new DRAM architecture having both short bitline mat and long bitline mat, enabling latency heterogeneity.
However, this mechanisms only provide when latency critical data are allocated to the fast regions.

## Slide 73
Prior Work: Low Latency DRAM
Having shorter bitlines: FCRAM, RL-DRAM
  Lower latency compared to conventional DRAM
  Large area for more sense amplifiers (~55% additional area)
Having shorter bitline regions: [Son et al., ISCA 13]
  Lower latency for data in shorter bitline regions
  Less efficiency due to statically-partitioned lower latency regions
  Not easy to migrate between fast and slow regions
Notes: Several DRAM use shorter bitline to reduce DRAM latency.
However, this approach significantly increases DRAM area.
Son et al. propose a new DRAM architecture having both short bitline mat and long bitline mat, enabling latency heterogeneity.
However, this mechanisms only provide when latency critical data are allocated to the fast regions.

## Slide 74
Prior Work: Cached DRAM
Implementing low-latency SRAM cache in DRAM
  Lower latency for accessing recently-accessed requests
  Large area for SRAM cache (~145% for integrating 6% capacity as SRAM cell)
  Complex control for SRAM cache
Notes: Cached DRAM integrates low latency SRAM cache in DRAM chip, reducing overall access latency.
However, it significantly increase area for SRAM cache.

## Slide 75
Prior Work: More Parallelism
Subarray-Level Parallelism: [Kim+, ISCA 2012]
  Enables independent accesses to different subarrays (a row of mats)
  Does not reduce latency of a single access
Parallelizing refreshes with accesses: [Chang+, HPCA 14]
  Mitigates latency penalty of DRAM refresh operations
  Does not reduce latency of a single access

## Slide 76
Outline
Prior Work
Future Research Direction
1. TL-DRAM
Reducing DRAM Latency
by Modifying Bitline Architecture
2. AL-DRAM
Optimizing DRAM Latency
for the Common Case
3. AVA-DRAM
Lowering DRAM Latency
by Exploiting Architectural Variation
Prior Work
Future Research Direction
Notes: Let me introduce future research direction

## Slide 77
Future Research Direction
Reducing Latency in 3D-stacked DRAM
  Power delivered from the bottom layer up to to the top layer  new source of variation in latency
  Evaluate & exploit power network related variation
Exploiting Variation in Retention Time
  Cells have different retention time based on their contents (i.e., 0 vs. 1), but use the same refresh interval
  Evaluate the relationship between the content in a cell and retention time & exploit the variation in retention time

## Slide 78
Future Research Direction
System Design for Heterogeneous-Latency DRAM
  Design a system that allocates frequently-used or more critical data to fast regions
  Design a system that optimizes DRAM operating conditions for better performance (e.g., reducing DRAM temperature by spreading accesses out to different regions)

## Slide 79
Conclusion
Observation
  DRAM cell array is the dominant source of high latency
  DRAM latency can be reduced by enabling and exploiting latency heterogeneity
Our Three Approaches
  TL-DRAM: Enabling latency heterogeneity by changing DRAM architecture
  AL-DRAM: Exploiting latency heterogeneity from process variation and temperature dependency
  AVA-DRAM: Exploiting latency heterogeneity from architectural variation
Evaluation & Result
  Our mechanisms enable significant latency reduction at low cost and thus improve system performance

## Slide 80
Contributions
Identified three major sources of high DRAM latency
  Long narrow wires
  Uniform latencies despite different operating conditions
  Uniform latencies despite architectural variation
Evaluated the impact of varying DRAM latencies
  Simulation with detailed DRAM model
  Profiled real DRAM (96 – 115 DIMMs) with FPGA-based DRAM test infrastructure
Developed mechanisms to lower DRAM latency, leading to significant performance improvement

## Slide 81: Reducing DRAM Latency at Low Cost by Exploiting Heterogeneity
Donghyuk Lee
Carnegie Mellon University