## Slide 1: ARCHITECTURAL TECHNIQUES TO ENHANCE DRAM SCALING
Thesis Defense Yoongu Kim

## Slide 2
CPU+CACHE
MAIN MEMORY
STORAGE

## Slide 3
Complex Problems
Large Datasets
High Throughput

## Slide 4
DRAM Cell (Capacitor)
DRAM Module
DRAM Chip
‘0’
‘1’

## Slide 5
1971
2015
103 Cells
109 Cells
FIRST DRAM CHIP

## Slide 6
FUTURE?
Chart: 
| 1.0 | 1.2 | 1.4 | 1.6 | 1.8 | 2.0 | 2.2 | 2.4 | 2.6 | 2.8 | 3.0 | 3.2 | 3.4 | 3.6 | 3.8 | 4.0 | 4.2 | 4.4 | 4.6 | 4.8 | 5.0 | 5.2 | 5.4 | 5.6 | 5.8 | 6.0 | 6.2 | 6.4 | 6.6 | 6.8 | 7.0 | 7.2 | 7.4 | 7.6 | 7.8 | 8.0 | 8.200000000000001 | 8.4 | 8.6 | 8.8 | 9.0 | 9.200000000000001 | 9.4 | 9.6 | 9.8 | 10.0
Y-Values | 2 | 2.2974 | 2.639 | 3.0314 | 3.4822 | 4 | 4.5948 | 5.278 | 6.0629 | 6.9644 | 8 | 9.1896 | 10.5561 | 12.1257 | 13.9288 | 16 | 18.3792 | 21.1121 | 24.2515 | 27.8576 | 32 | 36.7583 | 42.2243 | 48.5029 | 55.7152 | 64 | 73.5167 | 84.4485 | 97.0059 | 111.4305 | 128 | 147.0334 | 168.897 | 194.0117 | 222.8609 | 256 | 294.0668 | 337.794 | 388.0234 | 445.7219 | 512 | 588.1336 | 675.5881 | 776.0469 | 891.4438 | 1024
Column1 | 1024 | 891.4438 | 776.0469 | 675.5881 | 588.1336 | 512 | 445.7219 | 388.0234 | 337.794 | 294.0668 | 256 | 222.8609 | 194.0117 | 168.897 | 147.0334 | 128 | 111.4305 | 97.0059 | 84.4485 | 73.5167 | 64 | 55.7152 | 48.5029 | 42.2243 | 36.7583 | 32 | 27.8576 | 24.2515 | 21.1121 | 18.3792 | 16 | 13.9288 | 12.1257 | 10.5561 | 9.1896 | 8 | 6.9644 | 6.0629 | 5.278 | 4.5948 | 4 | 3.4822 | 3.0314 | 2.639 | 2.2974 | 2
1971
2015
CELLS/CHIP
CELL SIZE
103
109

## Slide 7: DRAM SCALING
TECHNOLOGICAL FEASIBILITY Can we make smaller cells?
ECONOMIC VIABILITY Should we make smaller cells?

## Slide 8: 1. RELIABILITY TAX 2. PERFORMANCE TAX
SMALLER CELLS
LOWER COST/BIT

## Slide 9: 1. RELIABILITY
COUPLING BETWEEN NEARBY CELLS
ROW HAMMER (ISCA 2014)
Your DRAM chips are probably broken.

## Slide 10: 2. PERFORMANCE
ABNORMALLY SLOW OUTLIER CELLS
BANK CONFLICTS (ISCA 2012) Our solution may be adopted by industry.

## Slide 11: CO-DESIGN: CPU & DRAM
CPU
Memory Management
DRAM Controller
DRAM
Arch & Interface
Circuits & Devices

## Slide 12: THESIS STATEMENT
The degradation in DRAM reliability & performance can be effectively mitigated by making low-overhead, non-intrusive modifications to the DRAM chips and the DRAM controller.

## Slide 13: DRAM SCALING
ARCHITECTURAL SUPPORT
MAIN MEMORY: LARGER, FASTER, RELIABLE, EFFICIENT

## Slide 14: THREE CONTRIBUTIONS
We show that DRAM scaling is negatively affecting reliability.
We expose a new type of DRAM failure, and propose a cost-effective way to address it.

## Slide 15: THREE CONTRIBUTIONS
We propose a high-performance architecture for DRAM that mitigates its growing latency.
We identify bottlenecks in DRAM’s internal design and alleviate them in a cost-effective manner.

## Slide 16: THREE CONTRIBUTIONS
We develop a new simulator for facilitating rapid design space exploration of DRAM.
The simulator is the fastest, while also being easy to modify due to its modular design.

## Slide 17: OUTLINE
1. RELIABILTY: ROW HAMMER
2. PERF: BANK CONFLICT
3. SIMULATOR: RAMULATOR
4. CONCLUSION

## Slide 18
1. ROW HAMMER
FLIPPING BITS IN MEMORY WITHOUT ACCESSING THEM ISCA 2014

## Slide 19: DRAM CHIP
WORDLINE
ROW
LOW VOLTAGE
HIGH VOLTAGE
VICTIM
VICTIM
AGGRESSOR
READ DATA FROM HERE, GET ERRORS OVER THERE

## Slide 20
GOOGLE’S EXPLOIT
http://googleprojectzero.blogspot.com
“We learned about rowhammer from Yoongu Kim et al.”

## Slide 21
GOOGLE’S EXPLOIT
PROPOSED SOLUTIONS
OUR PROOF-OF-CONCEPT
EMPIRICAL ANALYSIS

## Slide 22: REAL SYSTEM
x86
DRAM
1. CACHE HITS
2. ROW HITS
MANY READS TO SAME ADDRESS
OPEN/CLOSE SAME ROW
≠

## Slide 23
LOOP:
mov (X), %reg
mov (Y), %reg
clflush (X)
clflush (Y)
jmp LOOP
11111111111
11111111111
11111111111
11111111111
Y
X
11111111111
1111
1111
11011110010
10111010111
x86 CPU
DRAM
http://www.github.com/CMU-SAFARI/rowhammer
MANY ERRORS!

## Slide 24
WHY DO THE ERRORS OCCUR?

## Slide 25
DRAM CELLS ARE LEAKY
CHARGE
‘1’
‘0’
64ms
0ms
REFRESH
NORMAL CELL
TIME

## Slide 26
DRAM CELLS ARE LEAKY
CHARGE
‘1’
‘0’
64ms
0ms
REFRESH
VICTIM CELL
AGGRESSOR
TIME

## Slide 27: ROOT CAUSE?
COUPLING
Electromagnetic
Tunneling
⇝
⇝
⇝
⇝
⇝
⇝
⇝
⇝
ACCELERATES CHARGE LOSS

## Slide 28: AS DRAM SCALES …
CELLS BECOME SMALLER Less tolerance to coupling effects
CELLS BECOME PLACED CLOSER Stronger coupling effects
COUPLING ERRORS MORE LIKELY

## Slide 29
ERRORS ARE RECENT Not found in pre-2010 chips
ERRORS ARE WIDESPREAD >80% of chips have errors Up to one error per ~1K cells

## Slide 30
Test Engine
DRAM Ctrl
PCIe
FPGA
PC
DRAM

## Slide 31
Temperature
Controller
PC
Heater
FPGAs
FPGAs

## Slide 32: MOST MODULES AT RISK
A VENDOR
B VENDOR
C VENDOR
86%
83%
88%
(37/43)
(45/54)
(28/32)

## Slide 33
MANUFACTURE DATE
ERRORS PER 109 CELLS
MODULES:  A  B  C

## Slide 34: DISTURBING FACTS
AFFECTS ALL VENDORS Not an isolated incident Deeper issue in DRAM scaling
UNADDRESSED FOR YEARS Could impact systems in the field

## Slide 35
HOW TO PREVENT COUPLING ERRORS?
Previous Approaches
1. Make Better Chips: Expensive
2. Rigorous Testing: Takes Too Long

## Slide 36
ROW
MORE ERRORS
ROW
MORE ERRORS
FASTER ACCESS
ROW
ROW
FEWER ERRORS
ROW
FEWER ERRORS
FREQUENT REFRESH
ROW

## Slide 37
Faster ⟶ Slower
ONE MODULE:  A  B  C
ACCESS INTERVAL (ns)
TOTAL ERRORS
55ns
500ns

## Slide 38
Often ⟵ Seldom
ONE MODULE:  A  B  C
REFRESH INTERVAL (ms)
TOTAL ERRORS
64ms
11ms

## Slide 39: TWO NAIVE SOLUTIONS
LIMIT ACCESSES TO ROW Access Interval > 500ns
REFRESH ALL ROWS OFTEN Refresh Interval < 11ms
LARGE OVERHEAD: PERF, ENERGY, COMPLEXITY

## Slide 40: OUR SOLUTION: PARR
Probabilistic Adjacent Row Refresh
Do nothing
Refresh (=Open) adjacent rows
After closing any row ...
0.1%
99.9%

## Slide 41: PARR: CHANCE OF ERROR
NO REFRESHES IN N TRIALS Probability: 0.999N
N=128K FOR ERROR (64ms) Probability: 0.999128K = 10–56
STRONG RELIABILITY GUARANTEE

## Slide 42
STRONG RELIABILITY
LOW PERF OVERHEAD
9.4×10–14 Errors/Year
0.20% Slowdown
NO STORAGE OVERHEAD
0 Bytes

## Slide 43: RELATED WORK
Security Exploit (Seaborn@Google 2015)
Industry Analysis (Kang@SK Hynix 2014) “... will be [more] severe as technology shrinks down.”
Targeted Row Refresh (JEDEC 2014)
DRAM Testing (e.g., Van de Goor+ 1999)
Disturbance in Flash & Hard Disk

## Slide 44: RECAP: RELIABILITY
CPU
Memory Management
DRAM
Arch & Interface
Circuits & Devices
DRAM Controller
PARR
ROW HAMMER

## Slide 45
2. BANK CONFLICTS
A CASE FOR SUBARRAY PARALLELISM ISCA 2012

## Slide 46
CUTOFF
FASTEST
SLOWEST
DRAM
CELLS
5⨉ “WRITE PENALTY” Source: Samsung & Intel. The Memory Forum 2014

## Slide 47
FIGHT LATENCY WITH MORE PARALLELISM

## Slide 48
BANK
CHIP
BANK
CPU
WR
WR
DIFFERENT BANKS:
SMALL LATENCY

## Slide 49
BANK
CHIP
BANK
CPU
WR
WR
BANK CONFLICT:
LARGE LATENCY

## Slide 50
BANK CONFLICT LATENCY
WR
WR
 SERIALIZATION
 WRITE PENALTY (GETTING WORSE)

TIME
 “ROW-BUFFER” THRASHING



## Slide 51
BANK
BITLINES
ROW
ROW
ROW
ROW
CACHES A COPY OF OPENED ROW
CONNECTS ROWS TO ROW-BUFFER
BUFFER
MEMORY REQUEST
DATA
MEMORY REQUEST
MEMORY REQUEST
MEMORY REQUEST

## Slide 52
HOW TO PARALLELIZE BANK CONFLICTS?
Previous Approaches
1. Have More Banks: Expensive
2. Bank Interleaving: Non-Solution

## Slide 53
BUFFER
BANK (LOGICAL VIEW)
ROW
ROW
ROW
ROW
MANY ROWS (~100K)
JUST ONE
CANNOT DRIVE LONG BITLINES

## Slide 54
ROW
ROW
ROW
ROW
BUFFER
FEWER ROWS (~1K)
BANK (PHYSICAL VIEW)
DECDR
SUB ARRAY
DECODER
LOCAL (SUBARRAY)
GLOBAL (BANK)
BUFFER
BUFFER
DECDR

## Slide 55
ROW
ROW
BUFFER
SHARING = ROOT OF EVIL
DECDR
SUB ARRAY
DECODER
BUFFER
SHARED: 1. GLOBAL DEC. 2. GLOBAL BUF.
NO SUBARRAY
PARALLELISM
ROW
ROW
BUFFER
DECDR

## Slide 56
ROW2
ROW1
BUFFER
ROW4
DECDR
ROW3
BUFFER
DECDR
PROBLEM #1: DECODER
ADDR1
ADDR3
BOTH
DECODER
ROW1 OPENED
ROW1 CLOSED
ROW3 OPENED

## Slide 57
ROW1
BUFFER
REG.
ROW2
DECDR
ROW3
BUFFER
ROW4
DECDR
OUR SOLUTION
ADDR3
ADDR1
DECODER
STORES ADDRESS FOR EACH SUBARRAY
BOTH
STILL OPEN
ALSO OPEN

## Slide 58
ROW2
ROW1
PROBLEM #2: BUFFER
BUFFER
ROW4
ROW3
BUFFER
BUFFER
DECDR
DECDR
DECODER
BOTH

## Slide 59
ROW2
ROW1
OUR SOLUTION
BUFFER
ROW4
ROW3
DECODER
BOTH
REG.
SELECTS SUBARRAY FOR ACCESS
BUFFER
BUFFER
DECDR
DECDR

## Slide 60
WR



SERIAL SUBARRAYS
WR



WR
PARALLEL SUBARRAYS
WR
WR
WR
TIME
TIME

## Slide 61
Chart: SUBARRAY PARALLELISM
| 1x | 2x | 4x | 8x | 16x | 32x | 64x | 128x
Series 1 | 0 | 0.082463 | 0.13688 | 0.16722 | 0.18437 | 0.19313 | 0.19761 | 0.19994
Simulation: Out-of-Order CPU + DDR3-1066
Benchmarks: SPEC/TPC/STREAM/RANDOM
NONPARALLEL
PARALLEL
+17%

## Slide 62
SUBARRAYS
BANKS
PARALLELISM
8x
8x
SPEEDUP
+17%
+20%
vs.
CHIP-SIZE
+0.2%
+36%
Estimated using DRAM area model from Rambus

## Slide 63: RELATED WORK
Module Partitioning (e.g., Zheng+ 2008) Divide module into small, independent subsets Narrower data-bus  Higher unloaded latency
Hierarchical Bank (Yamauchi+ 1997) Parallelizes accesses to different subarrays Does not utilize multiple local row-buffers
Cached DRAM (e.g., Hidaka+ 1990)
Low-Latency DRAM (e.g., Sato+ 1998)

## Slide 64: RECAP: PERFORMANCE
CPU
Memory Management
DRAM
Arch & Interface
Circuits & Devices
DRAM Controller
SUBARRAY AWARE
SLOW OUTLIERS
PARALLEL SUBARRAYS

## Slide 65
3. RAMULATOR
RAMULATOR: A FAST AND EXTENSIBLE DRAM SIMULATOR IEEE CAL 2015

## Slide 66
IDEA
IDEA
IDEA
NEW IDEAS FOR BETTER DRAM ...
DRAM
SIMULATOR
MUST BE VETTED BY SIMULATION

## Slide 67: PREVIOUS SIMULATORS
PRO: HIGH FIDELITY
  Cycle-accurate DRAM models
CON: LOW FLEXIBILITY
  Hardcoded for DDR3/DDR4 DRAM
  Difficult to extend to others E.g., LPDDRx, WIOx, GDDRx, RLDRAMx, HBM, HMC

## Slide 68: OUR RAMULATOR
BUILT FOR EXTENSIBILITY
  Easy to incorporate new ideas
HIGH SIMULATION SPEED
  2.5x faster than the next fastest
PORTABLE: SIMPLE C++ API

## Slide 69: RAMULATOR’S APPROACH
Bank
Bank
Bank
BANK
RANK
CHANNEL
DRAM SYSTEM (STATE MACHINES)
Bank
Bank
Bank
BANK
RANK
CHANNEL
DRAM COMMAND & ADDRESS
(INPUTS)

## Slide 70
BANK
X
Z
Y
RANK
CHANNEL
A
C
B
D
P
Q
TEMPLATE
?
?
?
?
STATE MACHINES ARE DEFINED BY:
STATES
EDGES
RAMULATOR: RECONFIGURABLE STATE MACHINE

## Slide 71
TEMPLATE
TEMPLATE
TEMPLATE
TREE OF STATE MACHINES
COMMAND & ADDRESS
Hierarchy
States
Edges
DDR4
Hierarchy
States
Edges
GDDR5
Hierarchy
States
Edges
HBM
TEMPLATE
TEMPLATE
TEMPLATE

## Slide 72
TMP
TMP
TMP
TMP
TMP
TMP
DDR4
GDDR5
HBM
LPDDR4
WIO2
DRAM CONTROLLER
DRAM TRACE
CPU FRONTEND
FULL SYSTEM
RAMULATOR
PERFORMANCE
POWER (for some)
http://www.github.com/CMU-SAFARI/ramulator

## Slide 73
 | Supported DRAM Specifications | Simulation Speed (DDR3)
Ramulator | DDR3/4, LPDDR3/4, GDDR5, HBM, WIO1/2, Subarray Parallelism, etc. | 2.70x
DRAMSim2 (Rosenfeld et al.) | DDR2/3 | 1x
USIMM (Chatterjee et al.) | DDR3 | 1.08x
DrSim (Jeong et al.) | DDR2/3, LPDDR2 | 0.11x
NVMain (Poremba and Xie) | DDR3, LPDDR3/4 | 0.30x

## Slide 74
4. CONCLUSION

## Slide 75: SUMMARY
Traditional DRAM Scaling at Risk
Architectural Techniques for Coping with Degrading DRAM
Regain Reliability & Performance

## Slide 76: CONTRIBUTIONS
We show that DRAM scaling is negatively affecting reliability.
We propose a high-performance, cost-effective DRAM architecture.
We develop a new simulator for facilitating DRAM research.

## Slide 77: RESEARCH

RELIABILITY
Row Hammer Kim et al., ISCA ’14
Retention Failures Liu et al., ISCA ’13 Khan et al., SIGMETRICS ’14
Speed vs. Reliability Lee et al., HPCA ’15
EFFICIENCY
Bank Conflicts Kim et al., ISCA ’12
In-DRAM Page Copy Seshadri et al., MICRO ’13
Tiered Latency Lee et al., HPCA ’13
Fine-Grained Refreshes Chang et al., HPCA ’14


## Slide 78: RESEARCH
COMPRESSION
Simple & Effective Pekhimenko et al., MICRO ’13
SCHEDULING
High Throughput Kim et al., HPCA ’10
Quality of Service Kim et al., MICRO ’10 Kim et al., IEEE Micro Top Picks ’11 Subramanian et al., HPCA ’13
SIMULATION
Fast & Extensible Kim et al., IEEE CAL ’15






## Slide 79: OUTDATED ASSUMPTIONS
DRAM SCALING WILL TAKE CARE OF MAIN MEMORY
LATEST AND CHEAPEST DRAM IS THE GREATEST

## Slide 80: NEW TECHNOLOGIES
NONVOLATILE
MEMORY (NVM)
3-DIMENSIONAL DIE STACKING
Image: Loke et al., Science 2012
Image: Micron Technology, 2015

## Slide 81: TREND: HETEROGENEITY
CACHE:
MAIN MEMORY:
STORAGE:
SRAM
FLASH/HDD
DRAM
eDRAM
3D DRAM
NVM

## Slide 82: TREND: SPECIALIZATION
MOBILE
GRAPHICS
NETWORKS
PC/SERVER
BANDWIDTH
POWER
LATENCY
COST

## Slide 83
HOW TO REFORMULATE THE MEMORY HIERARCHY?

## Slide 84
NEW SOFTWARE ABSTRACTIONS Primitives for managing heterogeneity
NEW HARDWARE TRADE-OFFS Defining appropriate roles for each tier
RICH MEMORY CAPABILITIES Memory as more than a “bag of bits”

## Slide 85: ARCHITECTURAL TECHNIQUES TO ENHANCE DRAM SCALING
Thesis Defense Yoongu Kim