## Slide 1: 18-447 Computer Architecture Lecture 30: Interconnection Networks
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2014, 4/28/2014

## Slide 2: Lab 7: Multi-Core Cache Coherence
Last submission accepted on May 9, 11:59:59 pm
Cycle-level modeling of the MESI cache coherence protocol
Since this is the last lab
  An automatic extension of 7 days granted for everyone
  No other late days accepted

## Slide 3: Midterm 2 Grade Distribution
Chart: Midterm 2 Grade Distribution
| 0.0 | 10.0 | 20.0 | 30.0 | 40.0 | 50.0 | 60.0 | 70.0 | 80.0 | 90.0 | 100.0
 | 0 | 0 | 3 | 9 | 10 | 8 | 1 | 2 | 2 | 1 | 0

## Slide 4: Midterm 2 Statistics
MAX 90.71
MIN 22.86
MEDIAN 48.01
MEAN 42.5
STD 16.24

## Slide 5: Final Exam: May 6
May 6, 8:30-11:30am, Hamerschlag Hall B103
Comprehensive (over all topics in course)
Three cheat sheets allowed
We might have a review session
Remember this is 25% of your grade
  I will take into account your improvement over the course
  Know all concepts, especially the previous midterm concepts
  Same advice as before for Midterms I and II

## Slide 6: A Note on 742, Research, Jobs
I am teaching Parallel Computer Architecture next semester (Fall 2014)
  Deep dive into many topics we covered
  And, many topics we did not cover
  Research oriented with an open-ended research project
  Cutting edge research and topics in HW/SW interface
If you are enjoying 447 and are doing well, you can take it
 no need to have taken 640/740
 talk with me
If you are excited about Computer Architecture research or looking for a job/internship in this area
 talk with me

## Slide 7: Last Two Lectures
Multiprocessors
Bottlenecks in parallel processing
Multiprocessor correctness
  Sequential consistency
  Weaker consistency
Cache coherence
  Software vs. hardware
  Update vs. invalidate
  Snoopy cache vs. directory based
  VI  MSI  MESI  MOESI  …

## Slide 8: Today
Wrap up cache coherence
Interconnection networks

## Slide 9: Readings: Multiprocessing
Required
  Amdahl, “Validity of the single processor approach to achieving large scale computing capabilities,” AFIPS 1967.
  Lamport, “How to Make a Multiprocessor Computer That Correctly Executes Multiprocess Programs,” IEEE Transactions on Computers, 1979
Recommended
  Mike Flynn, “Very High-Speed Computing Systems,” Proc. of IEEE, 1966
  Hill, Jouppi, Sohi, “Multiprocessors and Multicomputers,” pp. 551-560 in Readings in Computer Architecture.
  Hill, Jouppi, Sohi, “Dataflow and Multithreading,” pp. 309-314 in Readings in Computer Architecture.

## Slide 10: Readings: Memory Consistency
Required
  Lamport, “How to Make a Multiprocessor Computer That Correctly Executes Multiprocess Programs,” IEEE Transactions on Computers, 1979
Recommended
  Gharachorloo et al., “Memory Consistency and Event Ordering in Scalable Shared-Memory Multiprocessors,” ISCA 1990.
  Charachorloo et al., “Two Techniques to Enhance the Performance of Memory Consistency Models,” ICPP 1991.
  Ceze et al., “BulkSC: bulk enforcement of sequential consistency,” ISCA 2007.

## Slide 11: Readings: Cache Coherence
Required
  Culler and Singh, Parallel Computer Architecture
    Chapter 5.1 (pp 269 – 283), Chapter 5.3 (pp 291 – 305)
  P&H, Computer Organization and Design
    Chapter 5.8 (pp 534 – 538 in 4th and 4th revised eds.)
  Papamarcos and Patel, “A low-overhead coherence solution for multiprocessors with private cache memories,” ISCA 1984.
Recommended
  Censier and Feautrier, “A new solution to coherence problems in multicache systems,” IEEE Trans. Computers, 1978.
  Goodman, “Using cache memory to reduce processor-memory traffic,” ISCA 1983.
  Laudon and Lenoski, “The SGI Origin: a ccNUMA highly scalable server,” ISCA 1997.
  Martin et al, “Token coherence: decoupling performance and correctness,” ISCA 2003.
  Baer and Wang, “On the inclusion properties for multi-level cache hierarchies,” ISCA 1988.

## Slide 12: Cache Coherence

## Slide 13: Review: MESI State Machine from Lab 7

## Slide 14: Review: Intel Pentium Pro
Slide credit: Yale Patt

## Slide 15: Snoopy Cache vs. Directory Coherence
Snoopy Cache
  + Miss latency (critical path) is short: request  bus transaction to mem.
  + Global serialization is easy: bus provides this already (arbitration)
  + Simple: can adapt bus-based uniprocessors easily
  - Relies on broadcast messages to be seen by all caches (in same order):
   single point of serialization (bus): not scalable
   need a virtual bus (or a totally-ordered interconnect)
Directory
  - Adds indirection to miss latency (critical path): request  dir.  mem.
  - Requires extra storage space to track sharer sets
    Can be approximate (false positives are OK)
  - Protocols and race conditions are more complex (for high-performance)
  + Does not require broadcast to all caches
  + Exactly as scalable as interconnect and directory storage (much more scalable than bus)
Notes: Make reference to SGI Origin paper

## Slide 16: Revisiting Directory-Based Cache Coherence

## Slide 17: Remember: Directory Based Coherence
Idea: A logically-central directory keeps track of where the copies of each cache block reside. Caches consult this directory to ensure coherence.
An example mechanism:
  For each cache block in memory, store P+1 bits in directory
    One bit for each cache, indicating whether the block is in cache
    Exclusive bit: indicates that the cache that has the only copy of the block and can update it without notifying others
  On a read: set the cache’s bit and arrange the supply of data
  On a write: invalidate all caches that have the block and reset their bits
  Have an “exclusive bit” associated with each block in each cache

## Slide 18: Remember: Directory Based Coherence Example

## Slide 19: Directory-Based Protocols
Required when scaling past the capacity of a single bus
Distributed, but:
  Coherence still requires single point of serialization (for write serialization)
  Serialization location can be different for every block (striped across nodes)
We can reason about the protocol for a single block: one server (directory node), many clients (private caches)
Directory receives Read and ReadEx requests, and sends Invl requests: invalidation is explicit (as opposed to snoopy buses)

## Slide 20: Directory: Basic Operations
Follow semantics of snoop-based system
  but with explicit request, reply messages
Directory:
  Receives Read, ReadEx, Upgrade requests from nodes
  Sends Inval/Downgrade messages to sharers if needed
  Forwards request to memory if needed
  Replies to requestor and updates sharing state
Protocol design is flexible
  Exact forwarding paths depend on implementation
  For example, do cache-to-cache transfer?

## Slide 21: MESI Directory Transaction: Read
P0
Home
1. Read
2. DatEx (DatShr)
Culler/Singh Fig. 8.16
P0 acquires an address for reading:
P1

## Slide 22: RdEx with Former Owner
P0
Home
1. RdEx
3b. DatEx
Owner
2. Invl
3a. Rev
Notes: Why speculative reply? Allows silent eviction of E (clean exclusive) block. Otherwise, have to make another roundtrip to home node to get data for requestor.

## Slide 23: Contention Resolution (for Write)
P0
Home
1a. RdEx
2a. DatEx
P1
1b. RdEx
2b. NACK


3. RdEx
4. Invl
5a. Rev
5b. DatEx


## Slide 24: Issues with Contention Resolution
Need to escape race conditions by:
  NACKing requests to busy (pending invalidate) entries
    Original requestor retries
  OR, queuing requests and granting in sequence
  Or some combination thereof
Fairness
  Which requestor should be preferred in a conflict?
  Both interconnect delivery order and distance matter
Preventing ping-ponging is important
  Can be achieved with better synchronization mechanisms or better prediction mechanisms

## Slide 25: Scaling the Directory: Some Questions
How large is the directory?
How can we reduce the access latency to the directory?
How can we scale the system to thousands of nodes?
Can we get the best of snooping and directory protocols?
  Think heterogeneity

## Slide 26: Directory: Data Structures
Required to support invalidation and cache block requests
Key operation to support is set inclusion test
  False positives are OK: want to know which caches may contain a copy of a block, and spurious invalidations are ignored
  False positive rate determines performance
Most accurate (and expensive): full bit-vector
Compressed representation, linked list, Bloom filters are all possible
0x00
0x04
0x08
0x0C
…
Shared: {P0, P1, P2}
---
Exclusive: P2
---
---

## Slide 27: Interconnection Network Basics

## Slide 28: Where Is Interconnect Used?
To connect components
Many examples
  Processors and processors
  Processors and memories (banks)
  Processors and caches (banks)
  Caches and caches
  I/O devices
Interconnection network

## Slide 29: Why Is It Important?
Affects the scalability of the system
  How large of a system can you build?
  How easily can you add more processors?
Affects performance and energy efficiency
  How fast can processors, caches, and memory communicate?
  How long are the latencies to memory?
  How much energy is spent on communication?

## Slide 30: Interconnection Network Basics
Topology
  Specifies the way switches are wired
  Affects routing, reliability, throughput, latency, building ease
Routing (algorithm)
  How does a message get from source to destination
  Static or adaptive
Buffering and Flow Control
  What do we store within the network?
    Entire packets, parts of packets, etc?
  How do we throttle during oversubscription?
  Tightly coupled with routing strategy

## Slide 31: Topology
Bus (simplest)
Point-to-point connections (ideal and most costly)
Crossbar (less costly)
Ring
Tree
Omega
Hypercube
Mesh
Torus
Butterfly
…

## Slide 32: Metrics to Evaluate Interconnect Topology
Cost
Latency (in hops, in nanoseconds)
Contention
Many others exist you should think about
  Energy
  Bandwidth
  Overall system performance

## Slide 33: Bus
+ Simple
+ Cost effective for a small number of nodes
+ Easy to implement coherence (snooping and serialization)
- Not scalable to large number of nodes (limited bandwidth, electrical loading  reduced frequency)
- High contention  fast saturation
0
1
2
3
4
5
6
7

## Slide 34: Point-to-Point
Every node connected to every other
+ Lowest contention
+ Potentially lowest latency
+ Ideal, if cost is not an issue
-- Highest cost
O(N) connections/ports
per node
O(N2) links
-- Not scalable
-- How to lay out on chip?
0
1
2
3
4
5
6
7

## Slide 35: Crossbar
Every node connected to every other (non-blocking) except one can be using the connection at any given time
Enables concurrent transfers to non-conflicting destinations
Could be cost-effective for small number of nodes
+ Low latency and high throughput
- Expensive
- Not scalable  O(N2) cost
- Difficult to arbitrate as N increases
Used in core-to-cache-bank
networks in
- IBM POWER5
- Sun Niagara I/II
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 36: Another Crossbar Design
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7

## Slide 37: Sun UltraSPARC T2 Core-to-Cache Crossbar
High bandwidth interface between 8 cores and 8 L2 banks & NCU
4-stage pipeline: req, arbitration, selection, transmission
2-deep queue for each src/dest pair to hold data transfer request

## Slide 38: Bufferless and Buffered Crossbars
Output
Arbiter
Output
Arbiter
Output
Arbiter
Output
Arbiter
Flow
Control
Flow
Control
Flow
Control
Flow
Control
NI
NI
NI
NI
Buffered
Crossbar
0
1
2
3
NI
NI
NI
NI
Bufferless
Crossbar
0
1
2
3
+ Simpler arbitration/ scheduling
+ Efficient support for variable-size packets
- Requires N2 buffers

## Slide 39: Can We Get Lower Cost than A Crossbar?
Yet still have low contention compared to a bus?
Idea: Multistage networks

## Slide 40: Multistage Logarithmic Networks
Idea: Indirect networks with multiple layers of switches between terminals/nodes
Cost: O(NlogN), Latency: O(logN)
Many variations (Omega, Butterfly, Benes, Banyan, …)
Omega Network:
conflict

## Slide 41: Multistage Networks (Circuit Switched)
Multistage has more restrictions on feasible concurrent Tx-Rx pairs
But more scalable than crossbar in cost, e.g., O(N logN) for Butterfly
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 crossbar

## Slide 42: Multistage Networks (Packet Switched)
Packets “hop” from router to router, pending availability of the next-required switch and buffer
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
2-by-2 router

## Slide 43: Aside: Circuit vs. Packet Switching
Circuit switching sets up full path
  Establish route then send data
  Noone else can use those links
  + faster arbitration
  -- setting up and bringing down links takes time
Packet switching routes per packet
  Route each packet individually (possibly via different paths)
  If link is free, any packet can use it
  -- potentially slower --- must dynamically switch
  + no setup, bring down time
  + more flexible, does not underutilize links

## Slide 44: Switching vs. Topology
Circuit/packet switching choice independent of topology
It is a higher-level protocol on how a message gets sent to a destination
However, some topologies are more amenable to circuit vs. packet switching

## Slide 45: Another Example: Delta Network
Single path from source to destination
Each stage has different routers
Proposed to replace costly crossbars as processor-memory interconnect
Janak H. Patel ,“Processor-Memory Interconnections for Multiprocessors,” ISCA 1979.
8x8 Delta network

## Slide 46: Another Example: Omega Network
Single path from source to destination
All stages are the same
Used in NYU Ultracomputer
Gottlieb et al. “The NYU Ultracomputer - Designing an MIMD Shared Memory Parallel Computer,” IEEE Trans. On Comp., 1983.

## Slide 47: Ring
+ Cheap: O(N) cost
- High latency: O(N)
- Not easy to scale
- Bisection bandwidth remains constant
Used in Intel Haswell, Intel Larrabee, IBM Cell, many commercial systems today
Notes: KSR machine, Hector

## Slide 48: Unidirectional Ring
Simple topology and implementation
  Reasonable performance if N and performance needs (bandwidth & latency) still moderately low
  O(N) cost
  N/2 average hops; latency depends on utilization
R
0
R
1
R
N-2
R
N-1
2
2x2 router

## Slide 49: Bidirectional Rings
+ Reduces latency
+ Improves scalability
- Slightly more complex injection policy (need to select which ring to inject a packet into)

## Slide 50: Hierarchical Rings
+ More scalable
+ Lower latency
- More complex

## Slide 51: More on Hierarchical Rings
HiRD: A Low-Complexity, Energy-Efficient Hierarchical Ring Interconnect. SAFARI Technical Report No. 2012-004. December 13, 2012.
Discusses the design and implementation of a mostly-bufferless hierarchical ring

## Slide 52: Mesh
O(N) cost
Average latency: O(sqrt(N))
Easy to layout on-chip: regular and equal-length links
Path diversity: many ways to get from one node to another
Used in Tilera 100-core
And many on-chip network
prototypes
Notes: e.g. Tile64

## Slide 53: Torus
Mesh is not symmetric on edges: performance very sensitive to placement of task on edge vs. middle
Torus avoids this problem
+ Higher path diversity (and bisection bandwidth) than mesh
- Higher cost
- Harder to lay out on-chip
- Unequal link lengths

## Slide 54: Torus, continued
Weave nodes to make inter-node latencies ~constant

## Slide 55: Trees
Planar, hierarchical topology
Latency: O(logN)
Good for local traffic
+ Cheap: O(N) cost
+ Easy to Layout
- Root can become a bottleneck
Fat trees avoid this problem (CM-5)
Fat Tree

## Slide 56: CM-5 Fat Tree
Fat tree based on 4x2 switches
Randomized routing on the way up
Combining, multicast, reduction operators supported in hardware
  Thinking Machines Corp., “The Connection Machine CM-5 Technical Summary,” Jan. 1992.

## Slide 57: Hypercube
Latency: O(logN)
Radix: O(logN)
#links: O(NlogN)
+ Low latency
- Hard to lay out in 2D/3D
0000
0101
0100
0001
0011
0010
0110
0111
1000
1101
1100
1001
1011
1010
1110
1111
Notes: Popular in early message-passing computers (e.g., intel iPSC, NCUBE)

## Slide 58: Caltech Cosmic Cube
64-node message passing machine
Seitz, “The Cosmic Cube,” CACM 1985.

## Slide 59: Handling Contention
Two packets trying to use the same link at the same time
What do you do?
  Buffer one
  Drop one
  Misroute one (deflection)
Tradeoffs?

## Slide 60: Bufferless Deflection Routing
Destination
Key idea: Packets are never buffered in the network. When two packets contend for the same link, one is deflected.1
1Baran, “On Distributed Communication Networks.” RAND Tech. Report., 1962 / IEEE Trans.Comm., 1964.
New traffic can be injected
whenever there is a free
output link.

## Slide 61: Bufferless Deflection Routing
Input buffers are eliminated: packets are buffered in pipeline latches and on network links
North
South
East
West
Local
North
South
East
West
Local
Deflection Routing Logic
Input Buffers

## Slide 62: Routing Algorithm
Types
  Deterministic: always chooses the same path for a communicating source-destination pair
  Oblivious: chooses different paths, without considering network state
  Adaptive: can choose different paths, adapting to the state of the network
How to adapt
  Local/global feedback
  Minimal or non-minimal paths

## Slide 63: Deterministic Routing
All packets between the same (source, dest) pair take the same path
Dimension-order routing
  E.g., XY routing (used in Cray T3D, and many on-chip networks)
  First traverse dimension X, then traverse dimension Y
+ Simple
+ Deadlock freedom (no cycles in resource allocation)
- Could lead to high contention
- Does not exploit path diversity

## Slide 64: Deadlock
No forward progress
Caused by circular dependencies on resources
Each packet waits for a buffer occupied by another packet downstream

## Slide 65: Handling Deadlock
Avoid cycles in routing
  Dimension order routing
    Cannot build a circular dependency
  Restrict the “turns” each packet can take
Avoid deadlock by adding more buffering (escape paths)
Detect and break deadlock
  Preemption of buffers

## Slide 66: Turn Model to Avoid Deadlock
Idea
  Analyze directions in which packets can turn in the network
  Determine the cycles that such turns can form
  Prohibit just enough turns to break possible cycles
Glass and Ni, “The Turn Model for Adaptive Routing,” ISCA 1992.

## Slide 67: Oblivious Routing: Valiant’s Algorithm
An example of oblivious algorithm
Goal: Balance network load
Idea: Randomly choose an intermediate destination, route to it first, then route from there to destination
  Between source-intermediate and intermediate-dest, can use dimension order routing
+ Randomizes/balances network load
- Non minimal (packet latency can increase)
Optimizations:
  Do this on high load
  Restrict the intermediate node to be close (in the same quadrant)

## Slide 68: Adaptive Routing
Minimal adaptive
  Router uses network state (e.g., downstream buffer occupancy) to pick which “productive” output port to send a packet to
  Productive output port: port that gets the packet closer to its destination
  + Aware of local congestion
  - Minimality restricts achievable link utilization (load balance)
Non-minimal (fully) adaptive
  “Misroute” packets to non-productive output ports based on network state
  + Can achieve better network utilization and load balance
  - Need to guarantee livelock freedom

## Slide 69: On-Chip Networks
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
Connect cores, caches, memory controllers, etc
  Buses and crossbars are not scalable
Packet switched
2D mesh: Most commonly used topology
Primarily serve cache misses and memory requests
Notes: One commonly proposed solution is on-chip network (NoC), which allows cores to communicate with a packet switched substrate.
Here is a figure showing an on-chip network that uses a 2d-mesh topology which
is commonly used due to its low layout complexity.
This is also the topology we used for our evaluations, but our mechanism is also applicable to other topologies.
In most multi-core systems, NoC primarily serves cache misses and memory requests.

## Slide 70: On-chip Networks
From East
From West
From North
From South
From PE
VC 0
VC Identifier
VC 1
VC 2
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
Crossbar
(
5
x
5
)
To East
To PE
To West
To North
To South
Input Port with Buffers
Control Logic
Crossbar
R
Router
PE
Processing Element
(Cores, L2 Banks, Memory Controllers etc)
Routing Unit
(
RC
)
VC Allocator
(
VA
)
Switch
Allocator
(SA)

## Slide 71: On-Chip vs. Off-Chip Interconnects
On-chip advantages
  Low latency between cores
  No pin constraints
  Rich wiring resources
  Very high bandwidth
  Simpler coordination
On-chip constraints/disadvantages
  2D substrate limits implementable topologies
  Energy/power consumption a key concern
  Complex algorithms undesirable
  Logic area constrains use of wiring resources

## Slide 72: On-Chip vs. Off-Chip Interconnects (II)
Cost
  Off-chip: Channels, pins, connectors, cables
  On-chip: Cost is storage and switches (wires are plentiful)
  Leads to networks with many wide channels, few buffers
Channel characteristics
  On chip short distance  low latency
  On chip RC lines  need repeaters every 1-2mm
    Can put logic in repeaters
Workloads
  Multi-core cache traffic vs. supercomputer interconnect traffic

## Slide 73: Motivation for Efficient Interconnect
In many-core chips, on-chip interconnect (NoC) consumes significant power
  Intel Terascale: ~28% of chip power
  Intel SCC: ~10%
  MIT RAW: ~36%
Recent work1 uses bufferless deflection routing to reduce power and die area
Core
L1
L2 Slice
Router
1Moscibroda and Mutlu, “A Case for Bufferless Deflection Routing in On-Chip Networks.” ISCA 2009.

## Slide 74: Research Topics in Interconnects
Plenty of topics in interconnection networks. Examples:
Energy/power efficient and proportional design
Reducing Complexity: Simplified router and protocol designs
Adaptivity: Ability to adapt to different access patterns
QoS and performance isolation
  Reducing and controlling interference, admission control
Co-design of NoCs with other shared resources
  End-to-end performance, QoS, power/energy optimization
Scalable topologies to many cores, heterogeneous systems
Fault tolerance
Request prioritization, priority inversion, coherence, …
New technologies (optical, 3D)

## Slide 75: One Example: Packet Scheduling
Which packet to choose for a given output port?
  Router needs to prioritize between competing flits
  Which input port?
  Which virtual channel?
  Which application’s packet?
Common strategies
  Round robin across virtual channels
  Oldest packet first (or an approximation)
  Prioritize some virtual channels over others
Better policies in a multi-core environment
  Use application characteristics
  Minimize energy