## Slide 1: PYREMat
18-549 Embedded System Design
Pooya Khorrami, Yush Gupta, Ross Finman, Evan Mullinix

## Slide 2: The Game
Up to 4 players
Each player assigned a color
Player must stay on his color
Tiles change color randomly at increasing rate
Players eliminated when they miss pads
Last player remaining wins
Possible Single player mode

## Slide 3: Pad Construction
Silicone bubble
Rim
Top metal contact
Bottom metal contacts
Rim
RGB LEDs
Hard mounting surface
Silicone bubble

## Slide 4: Electronics
3.3V Wall adapter
Arduino Mini
Red Shift Register
Green Shift Register
Blue Shift Register
clock
Data lines
Pad0 Blue LED
Multiplexer
Pad0 Contact Switch

## Slide 5: Parts needed
Pourable translucent silicone
RGB LEDs
Casting resin (for rim)
Hardboard (for mat)
Arduino microcontroller and power supply
ICS: transistors, multiplexers, shift registers
Misc: caulking, epoxy glue, wiring, etc

## Slide 6: Risks / Mitigation
Risks | Mitigation
Arduino code will be too bloated to fit in the processor memory or too slow because of the libraries that we’re using | Write code in c without using arduino libraries, use avr-gcc to complile the code and upload the binary image manually
Wiring will break or become undone when the mat is folded | Keep wiring slack, use flexible wiring and put in strain reliefs.
The pads will not be able to handle lateral loads | Use a strong epoxy around the outer edges, make the pads shallow, place a hard rim around the outside of the pads.
The contact mechanism of the pads will not work properly | A lot of experimentation to get the design down

## Slide 7: Status Update
Arduino A2D conversion, pwm working
Working on manufacturing pads
Parts ordered, coming in