Test cases for Ragebraker!

- Initialization:

  - Start up both nodes.

  - Leave the pedal in the released mode.

  - Note that the LED bar does not light up.

- Smoke Test:

  - Nodes already on. Pedal is released.

  - Depress the pedal all the way.

  - Note that the bar is fully lit up.

  - Release the pedal.

  - Note that the LEDs go off.

- Duration Test:

  - Nodes already on. Pedal is released.

  - Watch the LEDs for 5 seconds.

  - Note that the LEDs do not turn on at any point in those 5 seconds.

  - Depress the pedal fully.

  - Watch the LEDs for 5 seconds.

  - Note that all LEDs stay on the whole time.

- Granularity Test:

  - Nodes already on. Pedal is released.

  - Depress the pedal 25%.

  - Note that only 25% of the LEDs are on.

  - Depress the pedal to 50%.

  - Note that only 50% of the LEDs are on.

  - Depress the pedal to 75%.

  - Note that only 75% of the LEDs are on.

  - Depress the pedal to 100%.

  - Note that all LEDs are on.

  - Release pedal fully.

  - Note that all LEDs turn off.

- Failure Test:

  - Nodes are already on. Pedal is released.

  - Depress the pedal fully.

  - Note that all LEDs are on.

  - Disconnect the sensor node from the CAN bus.

  - Wait the timeout time.

  - Note that all LEDs turn off. (Or some other failure mode)

  - Reconnect the sensor node to the CAN bus.

  - Note that all LEDs are on.

- Some kind of interference test with timing and other nodes on the network.