## Slide 1: 18-549 Testing Plan: 3/26/2014 Rapid Ocular Sideline Concussion Diagnostics
Brandon Lee--Andrew Pfeifer--Thomas Phillips--Ryan Quinn
Team 8
1

## Slide 2: Status Update
Restructuring the eye-set
  Fixing the camera to be adjustable
    Allows for tests to include both eyes; will require additional trainer intervention, at least for now
  Exchanging the display screen for several LED’s around rim of glasses
    Enables us to implement additional concussion tests
OpenCV implementation
  RasPi will be sending each video to a laptop to do the analysis after video recording; “send data-process data-receive results loop” ~90 seconds,
Web App set up
  Enables us to persistently store each test of each athlete
  Can do server-side analysis on many test subjects (in the future)
2

## Slide 3: Updated Architecture
Camera
Android Tablet
Concussion-Testing Eye set
App
RasPi
3
Base Station (Laptop)
OpenCV Kernel
Web App
Database
2
Trainer begins test
Glasses performs test*
Video sent to laptop*
OpenCV analysis
Results sent back to glasses
All results sent to tablet
All results pushed to web app
*Done for each individual concussion test
1
4
3
5
6
7

## Slide 4: Component Requirements
Glasses
  Needs to correctly time LED sequence with camera recording
  Ensure that each video is successfully sent to base station
    If unsuccessful, need to alert user!
  Flow of PiUi app must be smooth
    Main interface for instructions/alerts back to training staff
Base Station
  Analyze the correct metric for each test
    Area of pupil vs location of pupil
  Package & transmit results properly back to glasses & server
Server
  Store all test results as well as metadata about each test
    Web interface must be intuitive and informative

## Slide 5: Testing Plan
Glasses
  Unit test each LED sequence to ensure it provides the correct stimulus to athlete
    Will need to play with brightness of the LED’s
  Many iterations of each test to ensure we capture only the video we need
    Too much video => unneeded processing & time
    Too little video => inaccurate results
  Rigorous PiUi user testing
Base Station
  Many iterations of OpenCV application to ensure:
    Same inputs => same outputs, different inputs => different outputs
    No issues analyzing different eyes (eye colors, right vs left)
    Awareness of what metric each test is measuring

## Slide 6: Testing Plan (Cont)
Web App
  Unit tests for all database models
  Unit tests for controllers to ensure HTTP requests are routed and handled properly
Overall System
  Communication between each component is critical. We will be testing the system by simulating failures of each node.
  System should remain stable if a node has an unexpected restart