Chapter 0(

Video Coding Standards for Multimedia Communication:		H.261, H.263, and Beyond

Tsuhan Chen

### Introduction

Standards are essential for communication.  Without a common language that both the transmitter and the receiver understand, communication is impossible.  For multimedia communication that involves transmission of video data, standards play an even more important role.  Not only does a video coding standard have to specify a common language, or formally known as the bitstream syntax, the language also has to be efficient.  Efficiency has two aspects.  One is that the standard has to support a good compression algorithm that brings down the bandwidth requirement for transmitting the video data.  The other is that the standard has to allow efficient implementation of the encoder and the decoder, i.e., the complexity of the compression algorithm has to be as low as possible.

In this chapter, we will discuss technologies used in video coding standards.  We will focus on the standards developed by International Telecommunication Union - Telecommunication Standardization Sector (ITU-T), formerly called the Consultative Committee of the International telephone and Telegraph (CCITT).  These include H.261, H.263, and a recent effort, informally known as H.263+, to provide a new version of H.263, i.e., H.263 Version 2, in 1998.  These video codec standards form important components of the ITU-T H-Series Recommendations that standardize audiovisual terminals in a variety of network environments.

This chapter is outlined as follows.  In Section 0.2, we will explain the roles of standards for video coding, and provide an overview of standard organizations and video coding standards.  In Section 0.3, we will present in detail the techniques used in a historically very important video coding standard, H.261.  In Section 0.4, H.263, a video coding standard that has a similar framework as that of H.261 but with superior coding efficiency, will be discussed.  Section 0.5 covers recent activities in H.263+ that resulted in a new version of H.263 with several enhancements.  We will conclude this chapter with some remarks in Section 0.6.

### Fundamentals of Standards

While standards may not be crucial for multimedia storage applications, they are very important for multimedia communication.  Suppose some multimedia content needs to be transmitted from a source to a destination.  The success of the communication is mainly determined by whether the source and the destination understand the same language.  Adoption of standards by equipment manufacturers and service providers results in higher volume and hence lowers the cost.  In addition, it offers consumers more freedom of choice among manufacturers, and therefore is highly welcomed by the consumers.

For transmission of video content, standards play an even more crucial role.  Not only the source and the destination need to speak the same language, i.e., bitstream syntax, the language also has to be efficient for compression of video content.  This is due to the relatively large amount of bits required to transmit uncompressed video data.

There are two major types of standards.  Industrial or commercial standards are mainly defined by mutual agreement among a number of companies.  Sometimes these standards can become very popular in the market and hence become the de facto standards, and widely accepted by other companies.  The other type is called voluntary standards that are defined by volunteers in open committees.  The agreement of these standards have to been based on consensus of all committee members.  These standards are usually driven by market needs.  At the same time, they need to stay ahead of the development of technologies.  It would be very difficult for the product vendors to agree on a common ground if each one has already developed products based on its own proprietary techniques.

The standards we will discuss in this chapter belong to the second type.  For multimedia communication, there are two major standard organizations: the International Telecommunication Union - Telecommunication Standardization Sector (ITU-T), and the International Organization for Standardization (ISO).  Recent video coding standards defined by these two organizations are summarized in Table 1.  These standards differ mainly in the operating bit-rates due to the applications they are originally designed for, although all standards can essentially be used for all applications at a wide range of bit rates.  In terms of coding algorithms, all standards in Table 1 follow a similar framework, as we will explain later, differ only in the ranges of parameters and some specific coding modes.  In this chapter, we will focus on the standards developed by ITU-T: H.261, H.263, and H.263 Version 2.

Table 1  Video Coding Standards

| Standards Organization | Video Coding Standard | Typical Range of Bit Rates | Typical Applications |
| --- | --- | --- | --- |
| ITU-T | H.261 | p(64 kbits/s, p=1…30 | ISDN Video Phone |
| ISO | IS 11172-2 MPEG-1 Video | 1.2 Mbits/s | CD-ROM |
| ISO | IS 13818-2 MPEG-2 Video | 4-80 Mbits/s | SDTV, HDTV |
| ITU-T | H.263 | 64 kbits/s or below | PSTN Video Phone |
| ISO | CD 14496-2 MPEG-4 Video | 24-1024 kbits/s |  |
| ITU-T | H.263 Version 2 | < 64 kbits/s | PSTN Video Phone |
| ITU-T | H.263L | < 64 kbits/s | - |

There are two approaches to understanding a video coding standard.  One approach is to focus on the bitstream syntax and try to understand what each layer of the syntax represents and what each bit in the bitstream indicates.  This approach is very important for manufacturers who need to build equipment that is compliant to the standard.  The other approach is to focus on coding algorithms that can be used to generate standard-compliant bitstreams, and try to understand what each component does and why some algorithms are better than others.  Although strictly speaking a standards does not specify any encoding algorithms, the latter approach provides a better understanding of video coding techniques as a whole, not just the standard bitstream syntax.  Therefore, we will take this approach in this chapter, and will describe certain bitstream syntax only when necessary.

### H.261

H.261 is a video coding standard defined by the ITU-T Study Group XV (SG15) for video telephony and video conferencing applications [].  It emphasizes low bit rates and the low coding delay.  It was originated in 1984 and intended to be used for audiovisual services at bit rates around m(384 kbits/s, where m is between 1 and 5.  In 1988, the focus shifted and it was decided to aim at bit rates around p(64 kbits/s, where p is from 1 to 30.  Therefore, H.261 also has an informal name called p(64 (pronounced as p times 64).  H.261 was approved in December 1990.  The coding algorithm used in H.261 is basically a hybrid of motion compensation to remove temporal redundancy and transform coding to reduce spatial redundancy.  Such a framework forms the basis of all video coding standards that were developed later.  Therefore, H.261 has very significant influence on many other existing and evolving video coding standards.

#### Source Picture Formats and Positions of Samples

Digital video is composed of a sequence of pictures, or frames, that occur at a certain rate.  For H.261, the frame rate is specified to be 30000/1001 (approximately 29.97) pictures per second.  Each picture is composed of a number of samples.  These samples are often referred to as pixels (picture elements), or simply pels.  For a video coding standard, it is important to understand the picture sizes that the standard applies to, and the position of samples.  H.261 is designed to deal with two picture formats: the common intermediate format (CIF) and the quarter CIF (QCIF).  Please refer to Table 2 that summarizes a variety of picture formats.  Using the terminology of the computer industry, the CIF is close to the CGA format commonly used in computer displays.  At such a resolution, the picture quality is not very high.  It is close to the quality of a typical video cassette recorder, and is much less than the quality of the broadcast television.  This is because H.261 is designed for video telephony and video conferencing, in which typical source material is composed of scenes of talking persons, so-called head and shoulder sequences, rather than general TV programs that contain a lot of motion and scene changes.

Table 2  Picture Formats Supported by H.261 and H.263

|  | Sub-QCIF | QCIF | CIF | 4CIF | 16CIF |
| --- | --- | --- | --- | --- | --- |
| No. of Pixels per Line | 128 | 176 | 352 | 704 | 1408 |
| No. of Lines | 96 | 144 | 288 | 576 | 1152 |
| Uncompressed Bit Rate | 4.4Mbs | 9.1 Mb/s | 37 Mb/s | 146 Mb/s | 584 Mb/s |

In H.261, each sample contains a luminance component, called Y, and two chrominance components, called CB and CR.  The values of these components are defined as in [].  In particular, “Black” is represented by Y=16, “White” is represented by Y=235, and the range of CB and CR is between 16 and 240, with 128 representing zero color difference (i.e., gray).  A picture format, as shown in Table 2, defines the size of the image, hence the resolution of the Y pels.  The chrominance pels, however, typically have a lower resolution than the luminance pels, in order to take advantage of the fact that human eyes are less sensitive to chrominance than to luminance.  In H.261, the CB and CR pels are specified to have half the resolution, both horizontally and vertically, of that of the Y pels.  This is commonly referred to as the 4:2:0 format.  Each CB or CR pel lies in the center of four neighboring Y pels, as shown in Figure 1.  Note that block edges, to be defined in the next section, lie in-between rows or columns of Y pels.

Figure 1  Positions of Samples for H.261

#### Blocks, Macroblocks, and Group of Blocks

Typically, we do not code an entire picture all at once.  Instead, it is divided into blocks that are processed one by one, both by the encoder and the decoder, in a scan order as shown in Figure 2.  This approach is often referred to as block-based coding.

Figure 2  Illustration of block-based coding

In H.261, a block is defined as a group of 8(8 pels.  Because of the downsampling in the chrominance components as mentioned earlier, one block of CB pels and one block of CR pels correspond to four blocks of Y pels.  The collection of these six blocks is called a macroblock (MB), as shown in Figure 3, with the order of blocks marked as 1 to 6.  A MB is treated as one unit in the coding process.

| 1 | 2 |  | 5 |  |  | 6 |  |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 3 | 4 |  |  |  |  |  |  |
| Y |  |  | CB |  |  | CR |  |

Figure 3 A macroblock

A number of MBs are grouped together and called a group of block (GOB).  For H.261, a GOB contains 33 MBs, as shown in Figure 4.  The resulting GOB structures for a picture, in the CIF case and the QCIF case, are shown in Figure 5.

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 |
| 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 |

Figure 4  A group of blocks (GOB)

| GOB 1 | GOB 2 |  |  |
| --- | --- | --- | --- |
| GOB 3 | GOB 4 |  |  |
| GOB 5 | GOB 6 |  | GOB 1 |
| GOB 7 | GOB 8 |  | GOB 3 |
| GOB 9 | GOB 10 |  | GOB 5 |
| GOB 11 | GOB 12 |  | QCIF |
| CIF |  |  |  |

Figure 5  GOB strucutres

#### The Compression Algorithm

Compression of video data typically is based on two principles: the reduction of spatial redundancy and the reduction of temporal redundancy.  H.261 uses discrete cosine transform to remove spatial redundancy, and motion compensation to remove temporal redundancy.  We now discuss these techniques in detail.

##### Transform Coding

Transform coding has been widely used to remove redundancy between data samples.  In transform coding, a set of data samples are first linearly transformed into a set of transform coefficients.  These coefficients are then quantized and entropy coded.  A proper linear transform can de-correlate the input samples, and hence remove the redundancy.  Another way to look at this is that a properly chosen transform can concentrate the energy of input samples into a small number of transform coefficients, so that resulting coefficients are easier to encode than the original samples.

The most commonly used transform for video coding is the discrete cosine transform (DCT) [,].  Both in terms of objective coding gain and subjective quality, DCT performs very well for typical image data.  The DCT operation can be expressed in terms of matrix multiplication:

where  represents the original image block, and  represents the resulting DCT coefficients.  The elements of , for an 8(8 image block, are defined as

where

After the transform, the DCT coefficients in are quantized.  Quantization implies loss of information, and is mainly where the compression comes from.  The quantization step size depends on the available bit rate, and can also depend on the coding modes.  Except for the intra DC coefficients that are uniformly quantized with a step size of 8, the “dead zone” is used to quantize all other coefficients in order to remove noise around zero.  The input-output relations for the two cases are shown in Figure 6.

Figure 6  Quantization with and without “dead zone”

The quantized  8(8 DCT coefficients are then converted into a one-dimensional (1D) array for entropy coding.  Figure 7 shows the scan order used in H.261 for this conversion.  Most of the energy concentrates on the low frequency coefficients, and the high frequency coefficients are usually very small and are quantized to zero before the scanning process.  Therefore, the scan order in Figure 7 can create long runs of zero coefficients, which is important for efficient entropy coding, as we will discuss in the next paragraph.

Figure 7  Scan order of the DCT coefficients

The resulting 1D array is then decomposed into segments, with each segment containing one or more (or none) zeros followed by a nonzero coefficient. Let an event represent the pair of (run, level), where “run” represents the number of zeros and “level” represents the magnitude of the nonzero coefficient.  This coding process is sometimes called “run-length coding.”  Then, a Huffman coding table is built to represent each event by a specific codeword, i.e., a sequence of bits.  Events that occur more often are represented by shorter codewords, and less frequent events are represented by longer codewords.  So, the table is often called a variable length coding (VLC) table.  In H.261, this table is often referred to as a two-dimensional (2D) VLC table because of its 2D nature, i.e., each event representing a pair of (run, level).  Some entries of VLC table used in H.261 are shown in Table 3.  In this table, the last bit “s” of each codeword denotes the sign of the level, “0” for positive and “1” for negative.  It can be seen that more likely events, i.e., short runs and low levels, are represented with short codewords, and vice versa.  After the last non-zero DCT coefficient is sent, the EOB symbol, represented by 10, is sent to indicate the end of block.

Table 3  Part of the VLC table

| Run | Level | Code |
| --- | --- | --- |
| 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 0 1 1 1 1 1 1 1 2 2 2 2 2 3 3 3 3 … | 1 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15 1 2 3 4 5 6 7 1 2 3 4 5 1 2 3 4 … | 1s If first coefficient in block 11s Not first coefficient in block 0100 s 0010 1s 0000 110s 0010 0110 s 0010 0001 s 0000 0010 10s 0000 0001 1101 s 0000 0001 1000 s 0000 0001 0011 s 0000 0001 0000 s 0000 0000 1101 0s 0000 0000 1100 1s 0000 0000 1100 0s 0000 0000 1011 1s 011s 0001 10s 0010 0101 s 0000 0011 00s 0000 0001 1011 s 0000 0000 1011 0s 0000 0000 1010 1s 0101 s 0000 100s 0000 0010 11s 0000 0001 0100 s 0000 0000 1010 0s 0011 1s 0010 0100 s 0000 0001 1100 s 0000 0000 1001 1s … |

At the decoder, all the above steps are reversed one by one.  Note that all the steps can be exactly reversed except for the quantization step, which is where the loss of information arises.

##### Motion Compensation

The transform coding described in the previous section removes spatial redundancy within each frame of picture.  It is therefore referred to as intra coding.  However, for video material, inter coding is also very useful.  Typical video material contains a large amount of redundancy along the temporal axis.  Video frames that are close in time usually have a large amount of similarity.  Therefore, transmitting the difference between frame is more efficient than transmitting the original frames. This is similar to the concept of differential coding and predictive coding.  The previous frame is used as an estimate of the current frame, and the residual, the difference between the estimate and the true value, is coded.  When the estimate is good, it is more efficient to code the residual than to code the original frame.

Consider the fact that typical video material is composed of moving objects.  Therefore, it is possible to improve the prediction result by first estimating the motion of each region in the scene.  More specifically, the encoder can estimate the motion (i.e., displacement) of each block between the previous frame and the current frame.  This is often achieved by matching each block (actually, macroblock) in the current frame with the previous frame to find the best matching area.  This area is then offset accordingly to form the estimate of the corresponding block in the current frame.  Now, the residue has much less energy and therefore is much easier to code.  This process is called motion compensation (MC), or more precisely, motion-compensated prediction [,].  This is illustrated in Figure 8.  The residue is then coded using the same process as that of intra coding.

Figure 8  Motion Compensation

Frames that are coded without any reference to previously coded frames are called intra frames, or simply I-frames.  Frames that are coded using a previous frame as a reference for prediction are called predicted frames, or simply P-frames.  However, note that a P-frame may contain also intra coded blocks.  The reason is as follows.  For a certain block, it may be impossible to find a good enough matching area in the reference frame to be used as prediction.  In this case, direct intra coding of such a block is more efficient.  This situation happens often when there is occlusion in the scene, or when the motion is very heavy.

Motion compensation saves the bits for coding the DCT coefficients.  However, it does imply that extra bits are require to carry information about the motion vectors.  Efficient coding of motion vector is therefore also an important part of H.261.  Because motion vectors of neighboring blocks tend to be similar, differential coding of the horizontal and vertical components of motion vectors is used.  That is, instead of coding motion vectors directly, the previous motion vector is used as a prediction for the current motion vector, and the difference, in both the horizontal component and the vertical component, is then coded using VLC table, part of which is shown in Table 4.  Note two things in this table.  First, short codewords are used to represent small difference, because these are more likely events.  Second, note that one codeword can represent up to two possible values for motion vector difference.  Because the range of either the horizontal component and the vertical component of motion vectors is between -15 and +15, only one will yield a motion vector with the allowable range.

Table 4  Part of the VLC table for coding of motion vectors

| MVD | Code |
| --- | --- |
| o… o–7 & 25 o–6 & 26 o–5 & 27 o–4 & 28 o–3 & 29 o–2 & 30 o–1 & 23 o–0 & 23 o–1 & 23 o–2 & –30 o–3 & –29 o–4 & –28 o–5 & –27 o–6 & –26 o–7 & –25 o–… | … 0000 0111 111 0000 1001 110 0000 1011 110 0000 1111 110 0001 1111 110 0011 1111 110 0111 0100 110 1000 0100 110 01000 0100 1 0010 1111 111 0001 0111 111 0000 1101 111 0000 1010 111 0000 1000 110 0000 0110 110 … |

##### Summary

The coding algorithm used in H.261 can be summarized into block diagrams in Figure 9 and Figure 10.  At the encoder, the input picture is compared with the previously decoded frame with motion compensation.  The difference signal is DCT transformed and quantized, and then entropy coded and transmitted.  At the decoder, the decoded DCT coefficients are inverse DCT transformed and then added to the previously decoded picture with motion compensation.

Figure 9  Block diagram of a video encoder

Figure 10  Block diagram of a video decoder

Since the prediction of the current frame is composed of blocks at various locations in the reference frame, the prediction itself (or simply called the predicted frame) may contain coding noise and blocking artifacts.  These artifacts may cause a higher prediction error.  It is possible to reduce the prediction error by passing the predicted frame through a lowpass filter before it is used as the prediction for the current frame.  This filter is referred a loop filter, because it operates inside the motion compensation loop.

#### Reference Model

As in all video coding standards, H.261 specifies only the bitstream syntax and how a decoder should interpret the bitstream to decode the image.  Therefore, it specifies only the design of the decoder, not how the encoding should be done.  For example, an encoder can simply decide to use only zero motion vectors and let the transform coding takes all the burden of coding the residual.  This may not be an efficient encoding algorithm, but it does generate a standard-compliant bitstream.

Therefore, to illustrate the effectiveness of a video coding standard, an example encoder is often provided by the group that defines the standard.  For H.261, such an example encoder is called a reference model (RM), and the latest version is RM 8 [].  It specifies details about motion estimation, quantization, decisions for inter/intra coding and MC/no MC, buffering, and the rate control.

#### ITU-T H Series Related to H.261

H.261 has been included in several ITU-T H-series terminal standards for various network environments.  One example is H.320 that is mainly designed for narrow-band ISDN terminals [].  H.320 defines the systems and terminal equipment that use H.261 for video coding, H.221 for frame multiplexing, H.242 for signaling protocol [], and G.711, G.722, and G.728 for audio coding.  Sometimes, H.320 is also used to referred to this set of standards.  H.261 can also be used in other terminal standards including H.321, H.322, H.323, and H.324.

### H.263

H.263 [] was defined by ITU-T SG15, the same group that defined H.261.  The activities of H.263 started around November 1993, and the standard was adopted in March 1996.  The main goal of this endeavor was to design a video coding standard suitable for applications with bit rates below 64 kbits/s (the so-called very-low bit-rate applications).  For example, when sending video data over the public service telephone network (PSTN) and the mobile network, the video bit rates typically range from 10 to 24 kbits/s.  During the development of H.263, it was identified that the near-term goal would be to enhance H.261 using the same general framework, and the long-term goal would be to design a video coding standard that may be fundamentally different from H.261 in order to achieve further improvement in coding efficiency.  As the standardization activities move along, the near-term effort became H.263 and H.263 Version 2 (to be discussed in the next section), and the long-term effort is now referred to as H.263L.

In this section, we will discuss H.263.  In essence, H.263 combines the features of H.261 together with MPEG, and is optimized for very low bit rates.  In terms of signal to noise ratio (SNR), H.263 can provides 3 to 4 dB gain over H.261 at bit rates below 64 kbits/s.  In fact, H.263 provides superior coding efficiency to that of H.261 at all bit rates.  When compared with MPEG-1, H.263 can give 30% bit rate saving.

#### H.263 vs. H.261

Since H.263 was built on top of H.261, the main structures of the two standards are essentially the same.  Therefore, we will focus only on the differences between the two standards.  The major differences are:

- H.236 supports more picture formats, and uses a different GOB structure.

- H.263 uses half-pel motion compensation, but does note use loop filtering as in H.261.

- H.263 uses 3D VLC for coding of DCT coefficients.

- In addition to the basic coding algorithm, four options that are negotiable between the encoder and the decoder provide improved performance.

- H.263 allows the quantization step size to change at each MB with less overhead.

#### Picture Formats, Sample Positions, and the GOB Structure

In addition to CIF and QCIF as supported by H.261, H.263 also supports sub-QCIF, 4CIF and 16CIF.  Resolutions of these picture formats can been found in Table 2.  Chrominance subsampling and the relative positions of chrominance pels are the same as those defined in H.261.  However, H.263 uses different GOB structures.  These are shown in Figure 11 for various formats.  Unlike H.261, a GOB in H.263 always contains at least one full row of MBs.

| GOB 0 |  | GOB 0 |
| --- | --- | --- |
| GOB 1 |  | GOB 1 |
| GOB 2 |  | GOB 2 |
| GOB 3 |  | GOB 3 |
| GOB 4 |  | GOB 4 |
| GOB 5 |  | GOB 5 |
| GOB 6 |  | GOB 6 |
| GOB 7 |  | GOB 7 |
| GOB 8 |  | GOB 8 |
| GOB 9 |  | QCIF |
| GOB 10 |  |  |
| GOB 11 |  |  |
| GOB 12 |  | GOB 0 |
| GOB 13 |  | GOB 1 |
| GOB 14 |  | GOB 2 |
| GOB 15 |  | GOB 3 |
| GOB 16 |  | GOB 4 |
| GOB 17 |  | GOB 5 |
| CIF |  | sub-QCIF |

Figure 11  GOB structures for H.263

#### Half-Pel Prediction and Motion Vector Coding

A major difference between H.261 and H.263 is the half-pel prediction in the motion compensation.  This concept is also used in MPEG.  While the motion vectors in H.261 can have only integer values, H.263 allows the precision of motion vectors to be at a half of a pel.  For example, it is possible to have a motion vector with values (4.5, -2.5).  When a motion vector has non-integer values, bilinear interpolation is used to find the corresponding pel values for prediction.

The coding of motion vectors in H.263 is more sophisticated than that in H.261.  The motion vectors of three neighboring MBs (the left, the above, and the above-right, as shown in Figure 12) are used as predictors.  The median of the three predictors is used as the prediction for the motion vector of the current block, and the prediction error is coded and transmitted.  However, around a picture boundary or GOB boundary, special cases are needed.  When only one neighboring MB is outside the picture boundary or GOB boundary, a zero motion vector is used to replace the motion vector of that MB as the predictor.  When two neighboring MBs are outside, the motion vector of the only neighboring MB that is inside is used to as the prediction.  These are shown in Figure 13.

Figure 12  Prediction of motion vectors

Figure 13  Motion vector prediction at picture/GOB boundaries

#### Run Length Coding of DCT Coefficients

H.263 improves the run-length coding used in H.261 by given an extra term “last” to indicate whether the current coefficient is the last nonzero coefficient of the block.  Therefore, a set of (run, level, last) represents an event and is mapped to a codeword in the VLC table, hence the name 3D VLC.  With this scheme, the EOB (end of block) code used in H.261 is not needed anymore.  Table 5 and Table 6 show some entries of the table.

Table 5  Partial VLC table for DCT coefficients

| LAST | RUN | LEVEL | CODE |
| --- | --- | --- | --- |
| 0 | 0 | 1 | 10s |
| 0 | 0 | 2 | 1111 s |
| 0 | 0 | 3 | 0101 01s |
| 0 | 0 | 4 | 0010 111s |
| 0 | 0 | 5 | 0001 1111 s |
| 0 | 0 | 6 | 0001 0010 1s |
| 0 | 0 | 7 | 0001 0010 0s |
| 0 | 0 | 8 | 0000 1000 01s |
| 0 | 0 | 9 | 0000 1000 00s |
| 0 | 0 | 10 | 0000 0000 111s |
| 0 | 0 | 11 | 0000 0000 110s |
| 0 | 0 | 12 | 0000 0100 000s |
| … | … | … | … |

Table 6  Partial VLC table for DCT coefficients

| LAST | RUN | LEVEL | CODE |
| --- | --- | --- | --- |
| … | … | … | … |
| 1 | 0 | 1 | 0111 s |
| 1 | 0 | 2 | 0000 1100 1s |
| 1 | 0 | 3 | 0000 0000 101s |
| 1 | 1 | 1 | 0011 11s |
| 1 | 1 | 2 | 0000 0000 100s |
| 1 | 2 | 1 | 0011 10s |
| 1 | 3 | 1 | 0011 01s |
| 1 | 4 | 1 | 0011 00s |
| 1 | 5 | 1 | 0010 011s |
| 1 | 6 | 1 | 0010 010s |
| 1 | 7 | 1 | 0010 001s |
| 1 | 8 | 1 | 0010 000s |

#### Negotiable Options

H.263 specifies four options that are negotiable between the encoder and the decoder.  At the beginning of each communication session, the decoder signals the encoder which of these options the decoder has the capability to decode.  If the encoder also supports some of these options, it may enable those options.  However, the encoder does not have to enable all the options that are supported by both the encoder and decoder.  The four options in H.263 are: the unrestricted motion vector mode, the syntax-based arithmetic coding mode, the advanced prediction mode, and the PB-frame mode.

##### Unrestricted Motion Vector Mode

This is the first one of the four negotiable options defined in H.263.  In this option, motion vectors are allowed to point outside of the picture boundary.  In this case, edge pels are repeated to extend to the pels outside so that prediction can be done.  Significant coding gain can be achieved with unrestricted motion vectors if there is movement around picture edges, especially for smaller picture formats like QCIF and sub-QCIF.  In addition, this mode allows a wider range of motion vectors than H.261.  Large motion vectors can be very effective when the motion in the scene is caused by heavy motion, e.g., motion due to camera movement.

##### Syntax-Based Arithmetic Coding (SAC)

In this option, arithmetic coding [] is used, instead of VLC tables, for entropy coding.  Under the same coding condition, using arithmetic coding will result in a bitstream different from the bitstream generated by using a VLC table, but the reconstructed frames and the SNR will be the same.  Experiments show that the average bit rate saving is about 3-4% for inter frames, and about 10% for intra blocks and frames.

##### Advanced Prediction Mode

In the advanced prediction mode, overlapped block motion compensation (OBMC) [] is used to code the luminance of P-pictures, which typically results in less blocking artifacts.  This mode also allows the encoder to assign four independent motion vectors to each MB.  That is, each block in a MB can have an independent motion vector.  In general, using four motion vectors gives better prediction, since one motion vector is used to represent the movement of a 8(8 block, instead of a 16(16 MB.  Of course, this implies more motion vectors, and hence requires more bits to code the motion vectors.  Therefore, the encoder has to decide when to use four motion vectors and when to use only one.  Finally, in the advanced prediction mode, motion vectors are allowed to cross picture boundaries as is the case in the unrestricted motion vector mode.

When four vectors are used, the prediction of motion vectors has to be redefined.  In particular, the locations of the three “neighboring” blocks of which the motion vectors are to be used as predictors now depend on the position of the current block in the MB.  These are shown in Figure 14.  It is interesting to note how these predictors are chosen.  Consider the situation depicted in the upper left of Figure 14.  When the motion vector corresponds to the upper left block in a MB, note that the third predictor (MV3) is not even connected to the current block.  What happens if we were to use the motion vector of a closer block, say the one marked with MV* in Figure 14?  In that case, MV* would be very likely the same as MV2 (because they belong to the same MB) and the median of the three predictors would be equal to MV2.  Therefore, the advantage of using three predictors would be lost.

Figure 14  Redefinition of Motion Vector Prediction

##### PB-Frame Mode

In the PB-frame mode, a PB-frame consists of two pictures coded as one unit, as shown in Figure 15.  The first picture, called the P-picture, is a picture predicted from the last decoded picture.  The last decoded picture can be either an I-picture, a P-picture, or the P-picture of a PB-frame.  The second picture, called the B-picture (B for bi-directional), is a picture predicted from both the last decoded picture the P-picture that is currently being decoded.  As opposed to the B-frames used in MPEG, PB frames do not need separate bi-directional vectors.  Instead, forward vectors for the P-picture is scaled, and added to a small delta-vector, to obtain vectors for the B-picture.  This results in less bit rate overhead for the B-picture.  For relatively simple sequences at low bit rates, the picture rate can be doubled with this mode with minimal increase in the bit rate.  However, for sequences with heavy motion, PB-frames do not work as well as B-pictures.  Also, note that the use of PB-frame mode increases the end-to-end delay, so it may not be suitable for two-way interactive communication.

Figure 15  The PB-frame mode

#### Test Model Near-Term (TMN)

Similar to H.261, there are documents drafted by ITU-T SG15 that describe example encoders, i.e., the test models.  For H.263, these are called TMN, where N indicates that H.263 is a near-term effort in improving H.261.  The latest version is TMN6 [].  TMN6 specifies the details of the advanced motion prediction, the overlapped block motion compensation, the choice between the 8(8 mode and 16(16 mode for motion vectors, the syntax-based arithmetic coding, and the use of the PB frame mode.

#### ITU-T H Series Related to H.263

Same as H.261, H.263 can be used in several terminal standards for different network environments.  One example is H.324 [] that defines audiovisual terminals for the traditional public service telephone network (PSTN).  In H.324, a telephone terminal uses H.263 as the video codec, H.223 as the multiplexing protocol [], H.245 as the control protocol [], G.723 for speech coding at 5.3/6.3 kbits/s, and V.34 for the modem interface.  H.324 is sometimes used to refer to the whole set of standards.  H.263 can also be used in other terminal standards, such as H.323 that is designed for local area networks (LAN) without guaranteed quality of service (QoS).

### H.263 Version 2

After the standardization of H.263 was finished, the continued interest in very bit rate video coding made it clear that further enhancements to H.263 were possible, in addition to the four optional modes.  ITU-T SG16 therefore established an effort, informally known as H.263+, to meet the need for standardization of such enhancements of H.263.  The result is a new version of H.263, H.263 Version 2 [], which is expected to be decided (approved by the Study Group) in January-February 1998.  Similar to H.263 Version 1 (the version dated March 1996), H.263 Version 2 is supposed to provide a near-term standardization for the applications of real-time telecommunication and related non-conversational services.  These enhancements are either improved quality of functionalities provided by H.263 Version 1, or additional capabilities to broaden the range of applications.  For example, the enhancements in H.263 Version 2 include: improvement of perceptual compression efficiency, reduction in the video delay, and greater error resilience.

Since H.263 Version 2 was a near term solution to the standardization of enhancements to H.263, it considered only well-developed proposed enhancements that fit into the framework of H.263 (i.e., motion compensation and DCT-based transform coding).  The H.263+ work plan is outlined in Table 7.  On the other hand, H.263L is a parallel activity that is intended to be a long-term effort.  It considers more radical algorithms that do not necessarily fit in the H.263 framework.

Table 7  Work plan for H.263 Version 2

| July ’96 | Evaluate proposals. Begin draft text. |
| --- | --- |
| Nov. ’96 | Final proposal evaluations. Complete draft written. |
| Feb. ’97 | Final evaluations completed. Finalized text written. |
| Mar. ’97 | Determination at SG16 meeting. |
| Jan.-Feb. ’98 | Decision at SG16 meeting. |

#### Development of H.263 Version 2

During the development of H.263 Version 2, proposed techniques are grouped into key technical areas (KTAs).  Altogether, there were about 22 KTAs being identified.  In November 1996, after consideration of the contributions and after some consolidation of KTAs, 12 KTAs were chosen.  These are summarized in a draft text that passed the determination process in March 1997.  Several adopted KTAs result in extra negotiable options.  Combined with the original four options in H.263, this makes the total of sixteen negotiable coding options in H.263 Version 2, which can be used together or separately.  Some KTAs result in extended source formats and a forward error correction method, and some are adopted as the supplemental enhancement information that may be included in the bitstream to indicate extra functionalities.  We will outline these new features in the next few sections.  In addition, a new test model (TMN8) has been prepared by the group for testing, simulation, and comparisons.

#### Source Formats

One feature of H.263 Version 2 is that it extends the possible source formats specified in H.263.  These extensions include:

- Higher Picture Clock Frequency (PCF): This allows picture clock rates higher than 30 frames per second.  This feature helps to support additional camera and display technologies.

- Custom Picture Formats: It is possible for the encoder and the decoder to negotiate a custom picture formats, not limited by a number of fixed formats anymore.  The number of lines can be from 4 to 1152 as long as it is divisible by 4, and the number of pels per line can be from 4 to 2048 as long as divisible by 4.

- Custom Pixel Aspect Ratios (PAR): This allows the use of additional pixel aspect ratios other than those used in CIF (11:12) and SIF (10:11), and the square (1:1) aspect ratio.  All custom PAR are shown in Table 8.

Table 8  Custom pixel aspect ratios

| Pixel Aspect Ratio | Pixel Width : Pixel Height |
| --- | --- |
| Square | 1:1 |
| CIF | 12:11 |
| 525-type for 4:3 picture | 10:11 |
| CIF for 16:9 picture | 16:11 |
| 525-type for 16:9 picture | 40:33 |
| Extended PAR | m:n, m and n are relatively prime |

#### New Coding Modes for Coding efficiency

Among the new negotiable coding options specified by H.263 Version 2, five of them are intended to improve the coding efficiency:

- Advanced Intra Coding Mode: This is an optional mode for intra coding.  In this mode, intra blocks are coded using a predictive method.  A block is predicted from the block to the left or the block above, as shown in Figure 16. For isolated intra blocks that no prediction can be found, the prediction is simply turned off.

- Alternate Inter VLC Mode: This mode provides the ability to apply a VLC table originally designed for intra coding to inter coding where there are often many large coefficients, by simply using a different interpretation of the level and the run.

- Modified Quantization Mode: This mode improves the flexibility of controlling the quantizer stepsize.  It also reduces of the quantizer stepsize for chrominance quantization, in order to reduce the chrominance artifacts.  An extension of the range of values of DCT coefficient is also provided.  In addition, by prohibiting certain unreasonable coefficient representations, this mode increases error detection performance and reduces decoding complexity.

- Deblocking Filter Mode: In this mode, an adaptive filter is applied across the 8x8 block edge boundaries of decoded I- and P-pictures to reduce blocking artifacts.  The filter affects the picture that is used for the prediction of subsequent pictures and thus lies within the motion prediction loop, similar to the loop filtering in H.261.

- Improved PB-frame Mode: This mode deals with the problem that the PB-frame mode in H.263 can not represent large motion very well.  It provides a mode with more robust performance under complex-motion conditions.  Instead of constraining a forward motion vector and a backward motion vector to come from a single motion vector as in H.263, the improved PB frame mode allows them to be totally independent as in the B-frames of MPEG.

Figure 16  Advance intra coding mode

#### Enhancements for Error Robustness

The following optional modes are especially designed to address the needs of mobile video and other unreliable transport environments:

- Slice Structured Mode: In this mode, a “slice” structure replaces the GOB structure.  Slices have more flexible shapes and may appear in any order within the bitstream for a picture.  Each slice has a specified width.  The use of slices allows a flexible partitioning of the picture, in contrast with the fixed partitioning and fixed transmission order required by the GOB structure.  This can provide enhanced error resilience and minimize the video delay.

- Reference Picture Selection Mode: In this mode, the reference picture does not have to be the most recently encoded picture.  Instead, any temporally previous picture can be referenced.  This mode can provide better error resilience in unreliable channels such as mobile and packet-networks, because the codec can avoid using an erroneous picture for future reference.

- Independent Segment Decoding Mode: This mode improves error resilience by ensuring that any error in a certain region of the picture does not propagate to other regions.

#### Enhancements Related to Scalabilities

The temporal, SNR, and spatial scalability mode supports layered-bitstream scalability in three forms, similar to MPEG-2.  Bi-directionally-predicted frames, same as those used in MPEG, are used for temporal scalability by adding enhancement frames between other coded frames.  This is shown in Figure 17. A similar syntactical structure is used to provide an enhancement layer of video data to support spatial scalability by adding enhancement information for construction of a higher-resolution picture, as shown in Figure 18.  Finally, SNR scalability is provided by adding enhancement information for reconstruction of a higher-fidelity picture with the same picture resolution, as in Figure 19.  Furthermore, different scalabilities can be combined together in a very flexible way.  Figure 20 gives an example.

Figure 17  Temporal scalability

Figure 18  Spatial scalability

Figure 19  SNR scalability

Figure 20  Multilayer scalability

#### Other Enhancement Modes

There are two other enhance modes described in H.263 Version 2:

- Reference Picture Resampling Mode: This allows a prior coded picture to be resampled, or warped, before it is used as a reference picture.  The warping is defined by four motion vectors that specify the amounts of offset of the four corners of the reference picture, as shown in Figure 21.  This mode allows an encoder to smoothly switch between different encoded picture sizes, shapes, and resolutions.  It also supports a form of global motion compensation and special-effect image warping.

- Reduced-Resolution Update Mode: This mode allows the encoding of inter frame difference information at a lower spatial resolution than the reference frame.  It gives the encoder the flexibility to maintain an adequate frame rate by encoding foreground information at a reduced spatial resolution while holding on to a higher-resolution representation of more stationary areas of a scene.

Figure 21  Reference Picture Resampling

#### Supplemental Enhancement Information

One important feature of H.263 Version 2 is the usage of supplemental information, which may be included in the bitstream to signal enhanced display capabilities or to provide tagging information for external usage.  For example, it can be used to signal a full-picture or partial-picture freeze, or freeze-release request with or without resizing.  It can be used to label a snapshot, the start and end of a video segment, and the start and end of a progressively-refined video.  The supplemental information may be present in the bitstream even though the decoder may not be capable of providing the enhanced capability to use it, or even to properly interpret it.  In other words, unless a requirement to provide the requested capability has been negotiated by external means in advance, the decoder can simply discard anything in the supplemental information.  Another use of the supplemental enhancement information is to specify chroma key for representing transparent and semitransparent pixels [].  We will now explain this in more detail.

The Chroma Keying Information Flag (CKIF) in the supplemental information indicates that the chroma keying technique is used to represent transparent and semi-transparent pixels in the decoded picture.  When being presented on the display, transparent pixels are not displayed.  Instead, a background picture which is externally controlled is revealed.  Semi-transparent pixels are rendered by blending the pixel value in the current picture with the corresponding value in the background picture.  Typically, an 8-bit number ( is used to indicate the transparency, so ( = 255 indicates that the pixel is opaque, and ( = 0 indicates that the pixel is transparent.  Between 0 and 255, the displayed color is a weighted sum of the original pixel color and the background pixel color.

When CKIF is enabled, one byte is used to indicate the keying color value for each component (Y, CB, or CR) which is used for chroma keying.  After the pixels are decoded, the ( value is calculated as follows.  First, the distance between the pixel color and the key color value is calculated.  The ( value is then computed as follows

if			then ;

else if		then ;

else

where T1 and T2 are the two thresholds that can be set by the encoder.

#### Levels of Preferred Mode Support

It is interesting to note that H.263 Version 2 provides a variety of optional modes that are all useful sometimes, but not all the manufacturers would want to implement all the options.  Therefore, H.263 Version 2 contains an appendix that specifies three levels of preferred modes to be supported.  Each level contains a number of options to be supported by a equipment manufacturer.  This appendix is not a normative part of the standard.  It is only to provide manufacturers some guidelines as which modes are more likely to be widely adopted across a full spectrum of terminals and networks.

Three levels of preferred modes are described in H.263 Version 2, and each level supports the optional modes specified in lower levels.  The first level is composed of the advanced intra coding mode, the deblocking filtering mode, full-frame freeze as defined in the supplementary information, and the modified quantization mode.  The second level supports, in addition to modes supported in Level 1, the unrestricted motion vectors mode, the slice structured mode, and the reference picture resampling mode.  In addition to these modes, Level 3 further supports the advanced prediction mode, the improved PB-frame mode, the independent segment decoding mode, and the alternative inter VLC mode.

#### Further Work

When the proposals for H.263 Version 2 were evaluated and some were adopted, it became apparent that many new proposals fit into the H.263 syntactical framework but were not be ready for determination in March 1997.  SG16 therefore considered another round of H.263 extensions, informally called H.263++, that would create a third generation of H.263 syntax.  Four key technical areas were identified in which the group has an interest in pursuing for further investigation toward possible later standardization.  These KTAs are: variable transform type, adaptive arithmetic coding, error-resilient VLC tables, and deringing filtering.

### Conclusion

By explaining the technical details of a number of important video coding standards defined by ITU-T, we hope we have provided the readers some insight to the significance of international standards for multimedia communication.  Pointers to more up-to-date information about the video coding standards described in this chapter can be found in Table 9.  When this chapter were prepared, activities in H.263++ and H.263L were still going on.  It is there recommended that the readers check the resources in Table 9 for more recent updates of H.263++ and H.263L.

Table 9  Sources of Further Information

| http://www.itu.ch | ITU-T |
| --- | --- |
| ftp://standard.pictel.com | General standards |
| ftp://standard.pictel.com/video-site | ITU-T Video Coding Experts Group (Q.15/16) |
| ftp://standard.pictel.com/lbc-site | ITU-T CSN Experts Group (Q.11/16) |
| ftp://standard.pictel.com/avc-site/ | ITU-T APC Experts Group (Q.12, 13, 14/16) |

Acknowledgments

The author would like to thank the anonymous reviewer for very insightful suggestions that helped significantly improve the quality of this chapter.

References

# Footnotes

( A book chapter in Visual Communication and Image Processing, edited by Chang Wen Chen and Ya-Qin Zhang, to be published by Marcel Dekker.

ITU-T also actively participated in the development of MPEG-2 Video.  In fact, ITU-T H.262 refers to the same standard and uses the same text as IS 13818-2.

Note that after a recent reorganization within ITU-T in early 1997, SG16 is now the group for video coding standards.  In this chapter, however, we will mostly use SG15 to refer to this Study Group.  This should not cause much confusion since most of the development of standards mentioned here actually happened before the reorganization.

In the still image mode as defined in Annex D of H.261, four times the currently transmitted video format is used.  For example, if the video format is CIF, the corresponding still image format is 4CIF.

Note, however, the standard does not specify how motion estimation should be done.

Toward the end of the H.263+ activities, in early 1997, a reorganization within ITU-T moved the activities in video coding standards from SG15 into SG16.

# Endnotes

[] ITU-T Recommendation H.261: “Video codec for audiovisual services at p x 64 kbit/s,” Geneva, 1990, revised at Helsinki, March 1993.

[] ITU-R Recommendation BT.601-4: “Encoding parameters of digital; television for studios.”

[] Ahmed, N., Natarajan, T., and Rao, K. R., “Discrete cosine transform,” IEEE Trans. on Computers, C-23:90-3, 1974.

[] Rao, K. R., and Yip, P., Discrete Cosine Transform, Academia Press, New York, 1990.

[] Netravali, A. N., and Robbins, J. D., “Motion-compensated television coding: Part I,” Bell Systems Technical Journals, v. 58(3), pp. 631-670, March 1979.

[] Netravali, A. N., and Haskell, B. G., Digital Pictures, Plenum Press, New York and London, 1995, 2nd ed.

[] Description of Reference Model 8 (RM8).  CCITT Study Group XV, Specialist Group on Coding for Visual Telephony.  Doc. No. 525, June 1989.

[] ITU-T Recommendation H.320: “Narrow-band ISDN visual telephone systems and terminal equipment,” March 1996.

[] ITU-T Recommendation H.242: “System for establishing communication between audiovisual terminals using digital channels up to 2Mbit/s,” 1993.

[] ITU-T Recommendation H.263: “Video coding for low bitrate communication,” March 1996.

[] Witten, I. H., Neal, R. M., and Cleary, J.G., “Arithmetic coding for data-compression,” Communications of the ACM, v30 (6), pp520-540, June 1987.

[] Orchard, M. T., and Sullivan, G. J., “Overlapped block motion compensation - an estimation-theoretic approach,” IEEE Transactions on Image Processing, v3 (5), pp. 693-699, Sept 1994.

[]ITU-T SG15, H.236+ Ad Hoc Group, “Video test model, TMN6,” LBC-96-141, April 1996.

[] ITU-T Recommendation H.324: “Terminal for low bitrate multimedia communication,” March 1996.

[] ITU-T Recommendation H.223: “Multiplexing protocol for low bitrate multimedia communication,” 1995.

[] ITU-T Recommendation H.245: “Control protocol for multimedia communication,” 1995.

[] ITU-T SG16, Gary Sullivan, ed., “Draft text of Recommendation H.263 Version 2 (“H.263+”) for Decision,” September 1997.

[] Chen, T., Swain, C. T., and Haskell, B. G., “Coding of sub-regions for content-based scalable video,” IEEE Trans. on Circuits and Systems for Video Technology, vol. 7 no. 1, pp. 256–260, February 1997.