Dipole Antennas

Fig.1: Dipole antenna inserted in a circular waveguide. (h = dipole height)

Simulation Results:

By using the ductexplorer program, the average powers and peak-to-peak variations were recorded for different dipole heights. Straight circular ducts were used in the simulations with matched terminations. The antenna separation was varied from 20 m to 200 m in 0.5 m increments. For each antenna separation and dipole height, channel responses at 201 frequency points were recorded. Finally the average power and average peak-to-peak variations were calculated for each dipole heights. Figure 2 shows the results. It seems that the optimum dipole height is about 8 cm that gives a good average power and small peak-to-peak variation in the channel response.

Fig.2: Simulation results for different dipole heights.

Figure 3 shows the average power level as a function of distance. From this figure, the simulated decay rate is about 1.5 dB/100m for the dipole with a 8 cm dipole height inserted in a circular waveguide.

Fig.3: Average power level as a function of antenna separation.

Experiments:

1) a straight duct section

The dipoles were placed at the far end of the ducts. The antenna separation was varied and channel response was recorded. The dipole height was 8 cm.

The experimental setup is shown in Fig. 4, and the channel frequency information is given in Table I.

Fig.4: Experimental setup

Table I: Mean power level for various antenna separation

| L (m) | Mean Power ( dB) |
| --- | --- |
| 16.6 | 16.6 |
| 13.55 | 16 |
| 10.5 | 17.8 |
| 7.45 | 15.3 |
| 4.4 | 16 |

Fig. 5: Experimental distribution of Average power level

The loss is about 0.06 dB/m.

Fig.6: Channel frequency response (L=16.6 meter)

2) T-junction network

| Dipole Height (cm) | Mean (dB) | Peak-to-peak var. (dB) | Stnd. Dev. (dB) |
| --- | --- | --- | --- |
| 6 | -28 | 15 | 3 |
| 6.5 | -28.3 | 12.8 | 3 |
| 7 | -29 | 14 | 3.5 |
| 7.5 | -30.8 | 27 | 6.4 |
| 8 | -27.6 | 20.3 | 5 |
| 8.5 | -25 | 17.9 | 4 |
| 9 | -23.3 | 12.5 | 3.2 |
| 9.5 | -22.5 | 9.7 | 2.9 |
| 10 | -21.9 | 10.4 | 2.7 |
| 10.5 | -21.9 | 10.8 | 2.7 |
| 11 | -22.3 | 11 | 2.7 |
| 11.5 | -22.8 | 11.2 | 2.8 |
| 12 | -23.5 | 10.3 | 2.8 |
| 12.5 | -24.5 | 9.8 | 3 |
| 13 | -25.8 | 12.2 | 3.2 |

A-B

3) T-junctions network

A-B

| Dipole Height (cm) | Mean (dB) | Peak-to-peak var. (dB) | Stnd. Dev. (dB) |
| --- | --- | --- | --- |
| 8 | -36.2 | 42 | 6 |
| 9 | -33.9 | 45 | 7.9 |
| 10 | -28.7 | 32 | 6.6 |
| 11 | -28.3 | 55 | 7.6 |
| 11.5 | -28.8 | 50 | 8 |
| 12 | -29.2 | 37 | 7 |

# Text boxes

h