# Single Mode Experiments

| Points | Average path loss in the 600-700 MHz band (dB) | RMS Delay Spread (ns) |
| --- | --- | --- |
| AB | -10.4 (-22.55)* | 78 |
| AE | -7.9 (-25.3)* | 64 |
| AC | -10.9 (-29.8)* | 45 |
| AD | -15.3 (-31.9)* | 89 |
| BE | -11.7 (-23.2)* | 53 |
| BC | -15.5 (-30.9)* | 57 |
| BD | -17.6 (-28.4)* | 131 |

Fig. 1. The experimental setup for single mode measurements

TABLE I: Single Mode Measurements.

*Average path loss for the same system at 2.4-2.5 GHz band.

Average power loss for T-junction in single mode:

In the straight direction : -3 dB

In the perpendicular direction: -5.3 dB

Insertion Loss:

The received power in a cylindrical duct can be estimated using the Friis-type equation:

where Pr(t) is the received power, PT(t0) is the transmitted power, and t0 is the arrival time of the earliest path. Ae is the effective aperture area, is the attenuation coefficient, v is the group velocity of a particular propagating mode in the duct, and Ax is the cross-sectional area of the duct.

The effective aperture is defined as:

,

where G is the gain of the antenna. The gain of an ideal, lossless monopole above a ground plane is G=3.28.

For 600-700 Mhz, the insertion loss is  -3.4 dB for 30.5 cm diameter duct.

Ariton, Ahmet, Kjetil