## Slide 1: 18-447 Computer Architecture Lecture 21: Main Memory
Prof. Onur Mutlu
Carnegie Mellon University
Spring 2015, 3/23/2015

## Slide 2: Assignment Reminders
Lab 6: Due April 3
  C-level simulation of caches and branch prediction
HW 5: Due March 29
  Will be out later today
Midterm II: TBD
The course will move quickly in the last 1.5 months
  Please manage your time well
  Get help from the TAs during office hours and recitation sessions
  The key is learning the material very well

## Slide 3: Upcoming Seminar on Flash Memory (March 25)
March 25, Wednesday, CIC Panther Hollow Room, 4-5pm
Yixin Luo, PhD Student, CMU
Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery
Yu Cai, Yixin Luo, Erich F. Haratsch, Ken Mai, and Onur Mutlu, "Data Retention in MLC NAND Flash Memory: Characterization, Optimization and Recovery" Proceedings of the 21st International Symposium on High-Performance Computer Architecture (HPCA), Bay Area, CA, February 2015. [Slides (pptx) (pdf)] Best paper session.

## Slide 4: Computer Architecture Seminars
Seminars relevant to many topics covered in 447
  Caching
  DRAM
  Multi-core systems
  …
List of past and upcoming seminars are here:
  https://www.ece.cmu.edu/~calcm/doku.php?id=seminars:seminars
You can subscribe to receive Computer Architecture related event announcements here:
  https://sos.ece.cmu.edu/mailman/listinfo/calcm-list

## Slide 5: Midterm I Statistics: Average
Out of 100:
MEAN 48.69
MEDIAN 47.94
STDEV 12.06
MAX 76.18
MIN 27.06

## Slide 6: Midterm I Grade Distribution (Percentage)

## Slide 7: Midterm I Grade Distribution (Absolute)

## Slide 8: Grade Breakdowns per Question
http://www.ece.cmu.edu/~ece447/s15/lib/exe/fetch.php?media=midterm_distribution.pdf

## Slide 9: Going Forward
What really matters is learning
  And using the knowledge, skills, and ability to process information in the future
  Focus less on grades, and put more weight into understanding
Midterm I is only 12% of your entire course grade
  Worth less than 2 labs + extra credit
There are still Midterm II, Final, 3 Labs and 3 Homeworks
There are many extra credit opportunities (great for learning by exploring your creativity)

## Slide 10: Lab 3 Extra Credit Recognitions
4.00 bmperez (Brandon Perez)
3.75 junhanz (Junhan Zhou)
3.75 zzhao1 (Zhipeng Zhao)
2.50 terencea (Terence An)
2.25 rohitban (Rohit Banerjee)

## Slide 11: Where We Are in Lecture Schedule
The memory hierarchy
Caches, caches, more caches
Virtualizing the memory hierarchy: Virtual Memory
Main memory: DRAM
Main memory control, scheduling
Memory latency tolerance techniques
Non-volatile memory
Multiprocessors
Coherence and consistency
Interconnection networks
Multi-core issues

## Slide 12: Main Memory

## Slide 13: Required Reading (for the Next Few Lectures)
Onur Mutlu, Justin Meza, and Lavanya Subramanian, "The Main Memory System: Challenges and Opportunities" Invited Article in Communications of the Korean Institute of Information Scientists and Engineers (KIISE), 2015.

## Slide 14: Required Readings on DRAM
DRAM Organization and Operation Basics
  Sections 1 and 2 of: Lee et al., “Tiered-Latency DRAM: A Low Latency and Low Cost DRAM Architecture,” HPCA 2013.
  http://users.ece.cmu.edu/~omutlu/pub/tldram_hpca13.pdf
  Sections 1 and 2 of Kim et al., “A Case for Subarray-Level Parallelism (SALP) in DRAM,” ISCA 2012.
  http://users.ece.cmu.edu/~omutlu/pub/salp-dram_isca12.pdf
DRAM Refresh Basics
  Sections 1 and 2 of Liu et al., “RAIDR: Retention-Aware Intelligent DRAM Refresh,” ISCA 2012. http://users.ece.cmu.edu/~omutlu/pub/raidr-dram-refresh_isca12.pdf

## Slide 15: Why Is Memory So Important? (Especially Today)

## Slide 16: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processor
and caches
Main Memory
Storage (SSD/HDD)

## Slide 17: Memory System: A Shared Resource View
Storage

## Slide 18: State of the Main Memory System
Recent technology, architecture, and application trends
  lead to new requirements
  exacerbate old requirements
DRAM and memory controllers, as we know them today, are (will be) unlikely to satisfy all requirements
Some emerging non-volatile memory technologies (e.g., PCM) enable new opportunities: memory+storage merging
We need to rethink/reinvent the main memory system
  to fix DRAM issues and enable emerging technologies
  to satisfy all requirements

## Slide 19: Major Trends Affecting Main Memory (I)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 20: Demand for Memory Capacity
More cores  More concurrency  Larger working set
Modern applications are (increasingly) data-intensive
Many applications/virtual machines (will) share main memory
  Cloud computing/servers: Consolidation to improve efficiency
  GP-GPUs: Many threads from multiple parallel applications
  Mobile: Interactive + non-interactive consolidation
  …
IBM Power7: 8 cores
Intel SCC: 48 cores
AMD Barcelona: 4 cores

## Slide 21: Example: The Memory Capacity Gap
Memory capacity per core expected to drop by 30% every two years
Trends worse for memory bandwidth per core!
Core count doubling ~ every 2 years
DRAM DIMM capacity doubling ~ every 3 years

## Slide 22: Major Trends Affecting Main Memory (II)
Need for main memory capacity, bandwidth, QoS increasing
  Multi-core: increasing number of cores/agents
  Data-intensive applications: increasing demand/hunger for data
  Consolidation: Cloud computing, GPUs, mobile, heterogeneity
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 23: Major Trends Affecting Main Memory (III)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
  IBM servers: ~50% energy spent in off-chip memory hierarchy [Lefurgy, IEEE Computer 2003]
  DRAM consumes power when idle and needs periodic refresh
DRAM technology scaling is ending

## Slide 24: Major Trends Affecting Main Memory (IV)
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending
  ITRS projects DRAM will not scale easily below X nm
  Scaling has provided many benefits:
    higher capacity, higher density, lower cost, lower energy

## Slide 25: The DRAM Scaling Problem
DRAM stores charge in a capacitor (charge-based memory)
  Capacitor must be large enough for reliable sensing
  Access transistor should be large enough for low leakage and high retention time
  Scaling beyond 40-35nm (2013) is challenging [ITRS, 2009]
DRAM capacity, cost, and energy/power hard to scale

## Slide 26: Evidence of the DRAM Scaling Problem
Row of Cells
Row
Row
Row
Row
Wordline
VLOW
VHIGH
Victim Row
Victim Row
Aggressor Row
Repeatedly opening and closing a row enough times within a refresh interval induces disturbance errors in adjacent rows in most real DRAM chips you can buy today
Opened
Closed
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.

## Slide 27: Most DRAM Modules Are At Risk
86%
(37/43)
83%
(45/54)
88%
(28/32)
A company
B company
C company
Up to
1.0×107 errors
Up to
2.7×106 errors
Up to
3.3×105 errors
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.

## Slide 28
DRAM Module
x86 CPU
Y
X
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 29
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 30
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 31
DRAM Module
x86 CPU
loop:
mov (X), %eax
mov (Y), %ebx
clflush (X)
clflush (Y)
mfence
jmp loop
Y
X
Notes: We demonstrate the errors on multiple x86 systems. Shown to the bottom-left is a “disturbance kernel”. When executed, it forces two rows to be opened and closed one after the other – over and over again. Consequently, it induces many errors in the module.

## Slide 32: Observed Errors in Real Systems
A real reliability & security issue
In a more controlled environment, we can induce as many as ten million disturbance errors
CPU Architecture | Errors | Access-Rate
Intel Haswell (2013) | 22.9K | 12.3M/sec
Intel Ivy Bridge (2012) | 20.7K | 11.7M/sec
Intel Sandy Bridge (2011) | 16.1K | 11.6M/sec
AMD Piledriver (2012) | 59 | 6.1M/sec
Kim+, “Flipping Bits in Memory Without Accessing Them: An Experimental Study of DRAM Disturbance Errors,” ISCA 2014.
Notes: When we executed the code on four different processors, all four of them yielded errors. Intel Haswell has the most errors, at 23 thousand, because it has the highest rate of accessing DRAM.
Later on, I’ll show that we can induce as many as ten million disturbance errors in a more controlled environment.
From this, we conclude that disturbance errors are a serious reliability issue.

## Slide 33: Errors vs. Vintage
All modules from 2012–2013 are vulnerable
First
Appearance
Notes: In this figure, the x-axis is the module manufacture date. And the y-axis is the number of errors in a module, normalized to one billion cells. In 2008 and 2009, there are no errors. But, in 2010, we first start to see errors in C modules. After 2010, the errors start to proliferate. For A and B modules, we first start to see errors in 2011. In particular, all modules from 2012 and 2013 are vulnerable.

## Slide 34: Security Implications (I)
http://googleprojectzero.blogspot.com/2015/03/exploiting-dram-rowhammer-bug-to-gain.html
http://users.ece.cmu.edu/~omutlu/pub/dram-row-hammer_isca14.pdf

## Slide 35: Security Implications (II)
“Rowhammer” is a problem with some recent DRAM devices in which repeatedly accessing a row of memory can cause bit flips in adjacent rows.
We tested a selection of laptops and found that a subset of them exhibited the problem.
We built two working privilege escalation exploits that use this effect.
One exploit uses rowhammer-induced bit flips to gain kernel privileges on x86-64 Linux when run as an unprivileged userland process.
When run on a machine vulnerable to the rowhammer problem, the process was able to induce bit flips in page table entries (PTEs).
It was able to use this to gain write access to its own page table, and hence gain read-write access to all of physical memory.

## Slide 36: Recap: The DRAM Scaling Problem

## Slide 37: An Orthogonal Issue: Memory Interference
Main
Memory
Core
Core
Core
Core
Cores’ interfere with each other when accessing shared main memory
Uncontrolled interference leads to many problems (QoS, performance)
Notes: In a multicore system, multiple applications running on the different cores share the main memory.
These applications interfere at the main memory. The result of this interference is unpredictable application slowdowns.

## Slide 38: Major Trends Affecting Main Memory
Need for main memory capacity, bandwidth, QoS increasing
Main memory energy/power is a key system design concern
DRAM technology scaling is ending

## Slide 39: How Can We Fix the Memory Problem & Design (Memory) Systems of the Future?

## Slide 40: Look Backward to Look Forward
We first need to understand the principles of:
  Memory and DRAM
  Memory controllers
  Techniques for reducing and tolerating memory latency
  Potential memory technologies that can compete with DRAM
This is what we will cover in the next few lectures

## Slide 41: Main Memory

## Slide 42: Main Memory in the System
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
DRAM MEMORY CONTROLLER

## Slide 43: The Memory Chip/System Abstraction

## Slide 44: Review: Memory Bank Organization
Read access sequence:
1. Decode row address & drive word-lines
2. Selected bits drive bit-lines
• Entire row read
3. Amplify row data
4. Decode column address & select subset of row
• Send to output
5. Precharge bit-lines
• For next access

## Slide 45: Review: SRAM (Static Random Access Memory)
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m diff pairs
2n
n
m
1
row select
bitline
_bitline
n+m
Read Sequence
  1. address decode
  2. drive row select
  3. selected bit-cells drive bitlines
  (entire row is read together)
  4. diff. sensing and col. select
  (data is ready)
  5. precharge all bitlines
  (for next read or write)
Access latency dominated by steps 2 and 3
Cycling time dominated by steps 2, 3 and 5
  step 2 proportional to 2m
  step 3 and 5 proportional to 2n

## Slide 46: Review: DRAM (Dynamic Random Access Memory)
row enable
_bitline
bit-cell array
2n row x 2m-col
(nm to minimize
overall latency)
sense amp and mux
2m
2n
n
m
1
RAS
CAS
A DRAM die comprises
of multiple such arrays
Bits stored as charges on node capacitance (non-restorative)
  bit cell loses charge when read
  bit cell loses charge over time
Read Sequence
  1~3 same as SRAM
  4. a “flip-flopping” sense amp amplifies and regenerates the bitline, data bit is mux’ed out
  5. precharge all bitlines
Refresh: A DRAM controller must periodically read all rows within the allowed refresh time (10s of ms) such that charge is restored in cells

## Slide 47: Review: DRAM vs. SRAM
DRAM
  Slower access (capacitor)
  Higher density (1T 1C cell)
  Lower cost
  Requires refresh (power, performance, circuitry)
  Manufacturing requires putting capacitor and logic together
SRAM
  Faster access (no capacitor)
  Lower density (6T cell)
  Higher cost
  No need for refresh
  Manufacturing compatible with logic process (no capacitor)

## Slide 48: Some Fundamental Concepts (I)
Physical address space
  Maximum size of main memory: total number of uniquely identifiable locations
Physical addressability
  Minimum size of data in memory can be addressed
  Byte-addressable, word-addressable, 64-bit-addressable
  Microarchitectural addressability depends on the abstraction level of the implementation
Alignment
  Does the hardware support unaligned access transparently to software?
Interleaving

## Slide 49: Some Fundamental Concepts (II)
Interleaving (banking)
  Problem: a single monolithic memory array takes long to access and does not enable multiple accesses in parallel
  Goal: Reduce the latency of memory array access and enable multiple accesses in parallel
  Idea: Divide the array into multiple banks that can be accessed independently (in the same cycle or in consecutive cycles)
    Each bank is smaller than the entire memory storage
    Accesses to different banks can be overlapped
  A Key Issue: How do you map data to different banks? (i.e., how do you interleave data across banks?)

## Slide 50: Interleaving

## Slide 51: Interleaving Options

## Slide 52: Some Questions/Concepts
Remember CRAY-1 with 16 banks
  11 cycle bank latency
  Consecutive words in memory in consecutive banks (word interleaving)
  1 access can be started (and finished) per cycle
Can banks be operated fully in parallel?
  Multiple accesses started per cycle?
What is the cost of this?
  We have seen it earlier
Modern superscalar processors have L1 data caches with multiple, fully-independent banks; DRAM banks share buses

## Slide 53: The Bank Abstraction

## Slide 54
Rank

## Slide 55: The DRAM Subsystem

## Slide 56: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column
Cell

## Slide 57: Page Mode DRAM
A DRAM bank is a 2D array of cells: rows x columns
A “DRAM row” is also called a “DRAM page”
“Sense amplifiers” also called “row buffer”
Each address is a <row,column> pair
Access to a “closed row”
  Activate command opens row (placed into row buffer)
  Read/write command reads/writes column in the row buffer
  Precharge command closes the row and prepares the bank for next access
Access to an “open row”
  No need for an activate command

## Slide 58: The DRAM Bank Structure

## Slide 59: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 60: The DRAM Chip
Consists of multiple banks (8 is a common number today)
Banks share command/address/data buses
The chip itself has a narrow interface (4-16 bits per read)
Changing the number of banks, size of the interface (pins), whether or not command/address/data buses are shared has significant impact on DRAM system cost

## Slide 61: 128M x 8-bit DRAM Chip

## Slide 62: DRAM Rank and Module
Rank: Multiple chips operated together to form a wide interface
All chips comprising a rank are controlled at the same time
  Respond to a single command
  Share address and command buses, but provide different data
A DRAM module consists of one or more ranks
  E.g., DIMM (dual inline memory module)
  This is what you plug into your motherboard
If we have chips with 8-bit interface, to read 8 bytes in a single access, use 8 chips in a DIMM

## Slide 63: A 64-bit Wide DIMM (One Rank)

## Slide 64: A 64-bit Wide DIMM (One Rank)
Advantages:
  Acts like a high-capacity DRAM chip with a wide interface
  Flexibility: memory controller does not need to deal with individual chips
Disadvantages:
  Granularity: Accesses cannot be smaller than the interface width

## Slide 65: Multiple DIMMs
Advantages:
  Enables even higher capacity
Disadvantages:
  Interconnect complexity and energy consumption can be high
   Scalability is limited by this

## Slide 66: DRAM Channels
2 Independent Channels: 2 Memory Controllers (Above)
2 Dependent/Lockstep Channels: 1 Memory Controller with wide interface (Not Shown above)

## Slide 67: Generalized Memory Structure

## Slide 68: Generalized Memory Structure

## Slide 69: The DRAM Subsystem The Top Down View

## Slide 70: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column
Cell

## Slide 71: The DRAM subsystem
Memory channel
Memory channel
DIMM (Dual in-line memory module)
Processor
“Channel”

## Slide 72: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM

## Slide 73: Breaking down a DIMM
DIMM (Dual in-line memory module)
Side view
Front of DIMM
Back of DIMM
Rank 0: collection of 8 chips
Rank 1

## Slide 74: Rank
Rank 0 (Front)
Rank 1 (Back)
Data <0:63>
CS <0:1>
Addr/Cmd
<0:63>
<0:63>
Memory channel

## Slide 75: Breaking down a Rank
Rank 0
<0:63>
Chip 0
Chip 1
Chip 7
. . .
<0:7>
<8:15>
<56:63>
Data <0:63>

## Slide 76: Breaking down a Chip
Chip 0
<0:7>
8 banks
Bank 0
<0:7>
<0:7>
<0:7>
...
<0:7>

## Slide 77: Breaking down a Bank
Bank 0
<0:7>
row 0
row 16k-1
...
2kB
1B
1B (column)
1B
Row-buffer
1B
...
<0:7>

## Slide 78: DRAM Subsystem Organization
Channel
DIMM
Rank
Chip
Bank
Row/Column
Cell

## Slide 79: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Channel 0
DIMM 0
Rank 0
Mapped to

## Slide 80: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
. . .

## Slide 81: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
Row 0
Col 0
. . .

## Slide 82: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 0
. . .
8B

## Slide 83: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
Row 0
Col 1
. . .

## Slide 84: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
. . .
8B

## Slide 85: Example: Transferring a cache block
0xFFFF…F
0x00
0x40
...
64B
cache block
Physical memory space
Rank 0
Chip 0
Chip 1
Chip 7
<0:7>
<8:15>
<56:63>
Data <0:63>
8B
8B
Row 0
Col 1
A 64B cache block takes 8 I/O cycles to transfer.
During the process, 8 columns are read sequentially.
. . .

## Slide 86: Latency Components: Basic DRAM Operation
CPU → controller transfer time
Controller latency
  Queuing & scheduling delay at the controller
  Access converted to basic commands
Controller → DRAM transfer time
DRAM bank latency
  Simple CAS (column address strobe) if row is “open” OR
  RAS (row address strobe) + CAS if array precharged OR
  PRE + RAS + CAS (worst case)
DRAM → Controller transfer time
  Bus latency (BL)
Controller to CPU transfer time

## Slide 87: Multiple Banks (Interleaving) and Channels
Multiple banks
  Enable concurrent DRAM accesses
  Bits in address determine which bank an address resides in
Multiple independent channels serve the same purpose
  But they are even better because they have separate data buses
  Increased bus bandwidth
Enabling more concurrency requires reducing
  Bank conflicts
  Channel conflicts
How to select/randomize bank/channel indices in address?
  Lower order bits have more entropy
  Randomizing hash functions (XOR of different address bits)

## Slide 88: How Multiple Banks/Channels Help

## Slide 89: Multiple Channels
Advantages
  Increased bandwidth
  Multiple concurrent accesses (if independent channels)
Disadvantages
  Higher cost than a single channel
    More board wires
    More pins (if on-chip memory controller)

## Slide 90: Address Mapping (Single Channel)
Single-channel system with 8-byte memory bus
  2GB memory, 8 banks, 16K rows & 2K columns per bank
Row interleaving
  Consecutive rows of memory in consecutive banks
  Accesses to consecutive cache blocks serviced in a pipelined manner
Cache block interleaving
    Consecutive cache block addresses in consecutive banks
    64 byte cache blocks
    Accesses to consecutive cache blocks can be serviced in parallel
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits

## Slide 91: Bank Mapping Randomization
DRAM controller can randomize the address mapping to banks so that bank conflicts are less likely
Column (11 bits)
3 bits
Byte in bus (3 bits)
XOR
Bank index (3 bits)

## Slide 92: Address Mapping (Multiple Channels)
Where are consecutive cache blocks?
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C
Low Col.
High Column
Row (14 bits)
Byte in bus (3 bits)
Bank (3 bits)
3 bits
8 bits
C

## Slide 93: Interaction with VirtualPhysical Mapping
Operating System influences where an address maps to in DRAM
Operating system can influence which bank/channel/rank a virtual page is mapped to.
It can perform page coloring to
  Minimize bank conflicts
  Minimize inter-application interference [Muralidhara+ MICRO’11]
Column (11 bits)
Bank (3 bits)
Row (14 bits)
Byte in bus (3 bits)
Page offset (12 bits)
Physical Frame number (19 bits)
Page offset (12 bits)
Virtual Page number (52 bits)
VA
PA
PA

## Slide 94: More on Reducing Bank Conflicts
Read Sections 1 through 4 of:
  Kim et al., “A Case for Exploiting Subarray-Level Parallelism in DRAM,” ISCA 2012.