## Slide 1: Practical Data Compression for Modern Memory Hierarchies
Gennady Pekhimenko
Thesis Oral
Committee:
Todd Mowry (Co-chair)
Onur Mutlu (Co-chair)
Kayvon Fatahalian
David Wood, University of Wisconsin-Madison
Doug Burger, Microsoft
Michael Kozuch, Intel
Presented in partial fulfillment of the requirements for the degree of Doctor of Philosophy

## Slide 2: Performance and Energy Efficiency
Energy efficiency
Applications today are data-intensive
Memory Caching
Databases
Graphics

## Slide 3: Computation vs. Communication
Data movement is very costly
  Integer operation: ~1 pJ
  Floating operation: ~20 pJ
  Low-power memory access: ~1200 pJ
Implications
  ½ bandwidth of modern mobile phone memory exceeds power budget
  Transfer less or keep data near processing units
Modern memory systems are bandwidth constrained

## Slide 4: Data Compression across the System
Processor
Cache
Memory
Disk
Network







## Slide 5: Software vs. Hardware Compression
Layer
Disk
Cache/Memory
Latency
milliseconds
nanoseconds
Software vs. Hardware
Algorithms
Dictionary-based
Arithmetic
  Existing dictionary-based algorithms are too slow
  for main memory hierarchies

## Slide 6: Key Challenges for Compression in Memory Hierarchy
Fast Access Latency
Practical Implementation and Low Cost
High Compression Ratio

## Slide 7: Thesis Statement
It is possible to develop a new set of designs for data compression within modern memory hierarchies that is:
  Fast
  Simple
  Effective
in saving storage space and consumed bandwidth
so that the resulting improvements in performance, cost, and energy efficiency will make it attractive to implement in future systems

## Slide 8: Contributions of This Dissertation
Base-Delta-Immediate (BDI) Compression algorithm with low latency and high compression ratio
Compression-Aware Management Policies (CAMP) that incorporate compressed block size into cache management decisions
Linearly Compressed Pages (LCP) framework for efficient main memory compression
Toggle-Aware Bandwidth compression mechanisms for energy-efficient bandwidth compression

## Slide 9: Practical Data Compression in Memory
Processor
Cache
Memory
Disk





1. Cache Compression



2. Compression and Cache Replacement
3. Memory Compression

4. Bandwidth Compression


## Slide 10: 1. Cache Compression
PACT
2012

## Slide 11: Background on Cache Compression
Key requirement:
  Low decompression latency
CPU
L2 Cache
Data
Compressed
Decompression
Uncompressed
L1 Cache
Hit
(~15 cycles)
Hit
(3-4 cycles)

## Slide 12: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000C0
0x000000C0
0x000000C0
0x000000C0
…
0x000000C0
0x000000C8
0x000000D0
0x000000D8
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region

## Slide 13: How Common Are These Patterns?
Chart: Cache Coverage (%)
| libquantum | lbm | mcf | tpch17 | sjeng | omnetpp | tpch2 | sphinx3 | xalancbmk | bzip2 | tpch6 | leslie3d | apache | gromacs | astar | gobmk | soplex | gcc | hmmer | wrf | h264ref | zeusmp | cactusADM | GemsFDTD | Arith.Mean
Zero | 1.2e-05 | 7e-06 | 0.008911 | 0.033323 | 0.032362 | 2.7e-05 | 0.065765 | 0.022031 | 0.000272 | 0.000176 | 0.12314 | 0.16955 | 0.072498 | 0.065675 | 0.016314 | 0.34373 | 0.26863 | 0.30068 | 0.003261 | 0.81434 | 0.00837 | 0.83736 | 0.66632 | 0.99428 | 0.20196
Repeated Values | 0.0001 | 6.5e-05 | 0.0001 | 0.000508 | 0.000146 | 0.0001 | 0.000529 | 0.008812 | 2e-06 | 0.036901 | 0.002005 | 0.095993 | 0.005072 | 0.010873 | 0.005914 | 0.020917 | 0.29969 | 0.038812 | 0.031345 | 0.083856 | 0.006414 | 0.13684 | 0.32178 | 0.001628 | 0.046184
Other Patterns | 0.000177 | 0.000138 | 0.060209 | 0.045394 | 0.070763 | 0.11701 | 0.075432 | 0.1168 | 0.21336 | 0.18863 | 0.12998 | 0.016265 | 0.23912 | 0.24082 | 0.42076 | 0.086109 | 0.18536 | 0.45647 | 0.84697 | 0.017818 | 0.91843 | 0.000306 | 0.000699 | 0.000345 | 0.18531
SPEC2006, databases, web workloads, 2MB L2 cache
“Other Patterns” include Narrow Values
43%
  43% of the cache lines belong to key patterns

## Slide 14: Key Data Patterns in Real Applications
0x00000000
0x00000000
0x00000000
0x00000000
…
0x000000C0
0x000000C0
0x000000C0
0x000000C0
…
0x000000C0
0x000000C8
0x000000D0
0x000000D8
…
0xC04039C0
0xC04039C8
0xC04039D0
0xC04039D8
…
  Zero Values: initialization, sparse matrices, NULL pointers
  Repeated Values: common initial values, adjacent pixels
  Narrow Values: small values stored in a big data type
  Other Patterns: pointers to the same memory region

## Slide 15: Key Data Patterns in Real Applications
  Low Dynamic Range:
  Differences between values are significantly smaller than the values themselves
Low Latency Decompressor
Low Cost and Complexity Compressor
Compressed Cache Organization

## Slide 16: Key Idea: Base+Delta (B+Δ) Encoding
32-byte Uncompressed Cache Line
0xC04039C0
0xC04039C8
0xC04039D0
…
0xC04039F8
4 bytes
0xC04039C0
Base
0x00
1 byte
0x08
1 byte
0x10
1 byte
…
0x38
12-byte
Compressed Cache Line
  20 bytes saved
   Effective: good compression ratio

## Slide 17: B+Δ Decompressor Design
Δ0
B0
Δ1
Δ2
Δ3
Compressed Cache Line
V0
V1
V2
V3
+
+
Uncompressed Cache Line
+
+
B0
Δ0
B0
B0
B0
B0
Δ1
Δ2
Δ3
V0
V1
V2
V3
  Vector addition
   Fast Decompression: 1-2 cycles

## Slide 18: Can We Get Higher Compression Ratio?
Uncompressible cache line (with a single base):
Key idea - use more bases
  More cache lines can be compressed
  Unclear how to find these bases efficiently
  Higher overhead (due to additional bases)
0x00000000
0x09A40178
0x0000000B
0x09A4A838
…
struct A {
int* next;
int count;};

## Slide 19: B+Δ with Multiple Arbitrary Bases
Chart: Compression Ratio
| GeoMean
1 | 1.3961
2 | 1.5113
3 | 1.4982
4 | 1.4326
8 | 1.3118
10 | 1.2742
16 | 1.2242
   2 bases – empirically the best option
# of bases is fixed

## Slide 20: How to Find Two Bases Efficiently?
  First base - first element in the cache line
  Second base - implicit base of 0
   Base+Delta part
   Immediate part
  Base-Delta-Immediate (BΔI) Compression

## Slide 21: BΔI Cache Organization
Conventional 2-way cache with 32-byte cache lines
Tag0
Tag1
…
…
…
…
Tag Storage:
Set0
Set1
Way0
Way1
Data0
…
…
Set0
Set1
Way0
Way1
…
Data1
…
32 bytes
Data Storage:
BΔI: 4-way cache with 8-byte segmented data
Tag0
Tag1
…
…
…
…
Tag Storage:
Way0
Way1
Way2
Way3
…
…
Tag2
Tag3
…
…
Set0
Set1
Twice as many tags
C - Compr. encoding bits
C
Set0
Set1
…
…
…
…
…
…
…
…
S0
S0
S1
S2
S3
S4
S5
S6
S7
…
…
…
…
…
…
…
…
8 bytes
Tags map to multiple adjacent segments

## Slide 22: Methodology
Simulator
  x86 event-driven simulator (MemSim [Seshadri+, PACT’12])
Workloads
  SPEC2006 benchmarks, TPC, Apache web server
  1 – 4 core simulations for 1 billion representative instructions
System Parameters
  L1/L2/L3 cache latencies from CACTI
  BDI (1-cycle decompression)
  4GHz, x86 in-order core, cache size (1MB - 16MB)
Notes: In our experiments, we used MemSim event-driven simulator based on Simics as a front-end.

## Slide 23: Comparison Summary
Comp. Ratio
1.53
1.51
Decompression
1-2 cycles
5-9 cycles
Compression
1-9 cycles
3-10+ cycles
Prior Work vs. BΔI
  Average performance of a twice larger cache

## Slide 24
Processor
Cache
Memory
Disk

1. Cache Compression
2. Compression and Cache Replacement
3. Memory Compression
4. Bandwidth Compression




## Slide 25: 2. Compression and Cache Replacement
HPCA 2015

## Slide 26: Cache Management Background
Not only about size
  Cache management policies are important
  Insertion, promotion and eviction
Belady’s OPT Replacement
  Optimal for fixed-size caches fixed-size blocks
  Assumes perfect future knowledge
Y
Cache:
X
Z
X A Y B C
Access stream:
A
Notes: Optimal for minimizing miss rate

## Slide 27: Block Size Can Indicate Reuse
Sometimes there is a relation between the compressed block size and reuse distance
compressed
block size
data structure
This relation can be detected through the compressed block size
Minimal overhead to track this relation (compressed block information is a part of design)
reuse distance

## Slide 28: Code Example to Support Intuition
int A[N]; // small indices: compressible
double B[16]; // FP coefficients: incompressible
for (int i=0; i<N; i++) {
int idx = A[i];
for (int j=0; j<N; j++) {
sum += B[(idx+j)%16];
}
}
long reuse, compressible
short reuse, incompressible
Compressed size can be an indicator of reuse distance
Notes: Simple code example to support intuition.

## Slide 29: Block Size Can Indicate Reuse
Block size, bytes
Different sizes have different dominant reuse distances

## Slide 30: Compression-Aware Management Policies (CAMP)
The benefits are on-par with cache compression - 2X additional increase in capacity
CAMP
MVE:
Minimal-Value Eviction
SIP:
Size-based
Insertion Policy
Value =
Probability of reuse
Compressed block size
compressed
block size
data structure
reuse distance

## Slide 31
Processor
Cache
Memory
Disk

1. Cache Compression
2. Compression and Cache Replacement
3. Memory Compression
4. Bandwidth Compression





## Slide 32: 3. Main Memory Compression
MICRO 2013

## Slide 33: Challenges in Main Memory Compression
Address Computation
Mapping and Fragmentation

## Slide 34: Address Computation
L0
L1
L2
. . .
LN-1
Cache Line (64B)
Address Offset
0
64
128
(N-1)*64
L0
L1
L2
. . .
LN-1
Compressed Page
0
?
?
?
Address Offset
Uncompressed Page

## Slide 35: Mapping and Fragmentation
Virtual Page
(4KB)
Physical Page
(? KB)
Fragmentation
Virtual
Address
Physical
Address

## Slide 36: Shortcomings of Prior Work
Compression Mechanisms | Compression Ratio | Address Comp. Latency | Decompression Latency | Complexity and Cost
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
64 cycles

## Slide 37: Shortcomings of Prior Work
Compression Mechanisms | Compression Ratio | Address Comp. Latency | Decompression Latency | Complexity and Cost
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 
5 cycles

## Slide 38: Shortcomings of Prior Work
Compression Mechanisms | Compression Ratio | Address Comp. Latency | Decompression Latency | Complexity and Cost
IBM MXT [IBM J.R.D. ’01] |  |  |  | 
Robust Main Memory Compression [ISCA’05] |  |  |  | 
Linearly Compressed Pages: Our Proposal |  |  |  | 

## Slide 39: Linearly Compressed Pages (LCP): Key Idea
64B
64B
64B
64B
. . .
. . .
4:1 Compression
64B
Uncompressed Page (4KB: 64*64B)
Compressed Data
(1KB)
 LCP effectively solves challenge 1: address computation
LCP sacrifices some compression ratio in favor of design simplicity

## Slide 40: LCP: Key Idea (2)
64B
64B
64B
64B
. . .
. . .
M
E
Metadata (64B):
? (compressible)
Exception
Storage
4:1 Compression
64B
Uncompressed Page (4KB: 64*64B)
Compressed Data
(1KB)

## Slide 41: LCP Framework Overview
Page Table entry extension
  compression type and size
OS support for multiple page sizes
  4 memory pools (512B, 1KB, 2KB, 4KB)
Handling uncompressible data
Hardware support
  memory controller logic
  metadata (MD) cache
PTE

## Slide 42: Physical Memory Layout
4KB
2KB
2KB
1KB
1KB
1KB
1KB
512B
512B
...
512B
4KB
…
…
Page Table
PA0
offset
PA1
…
PA1 + 512

## Slide 43: LCP Optimizations
Metadata cache
  Avoids additional requests to metadata
Memory bandwidth reduction:
Zero pages and zero cache lines
  Handled separately in TLB (1-bit) and in metadata
  (1-bit per cache line)
64B
64B
64B
64B
1 transfer
instead of 4

## Slide 44: Summary of the Results
Comp. Ratio
1.62
1.59
Performance
+14%
-4%
Energy Consumption
↓5%
↑6%
Prior Work vs. LCP

## Slide 45
Processor
Cache
Memory
Disk

1. Cache Compression
2. Compression and Cache Replacement
3. Memory Compression
4. Bandwidth Compression






## Slide 46: 4. Energy-Efficient Bandwidth Compression
HPCA 2016
CAL 2015

## Slide 47: Energy Efficiency: Bit Toggles
0
1
0011
Previous data:
Bit Toggles
Energy = C*V2
How energy is spent in data transfers:
0101
New data:
0
0
1
0
1
1
Energy:
Energy of data transfers (e.g., NoC, DRAM) is proportional to the bit toggle count

## Slide 48: Excessive Number of Bit Toggles
0x00003A00
0x8001D000
0x00003A01
0x8001D008
…
Flit 0
Flit 1
XOR
000000010….00001
=
# Toggles = 2
Compressed Cache Line
0x5 0x3A00
0x7 8001D000
0x5 0x3A01
Flit 0
Flit 1
XOR
001001111 … 110100011000
=
# Toggles = 31
0x7 8001D008
…
5 3A00 7 8001D000 5 1D
1 01 7 8001D008 5 3A02 1
Uncompressed Cache Line

## Slide 49: Effect of Compression on Bit Toggles
Chart: Normalized Bit Toggle #
| FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | Discrete | Mobile | Open-Source
Without EC | 1.1884 | 1.1267 | 1.1487 | 1.1993 | 1.1116 | 1.0919 | 2.1276 | 2.1399 | 1.9797 | 2.1896 | 1.93 | 1.4886 | 1.6155 | 1.2358 | 2.0462
Compression significantly increases bit toggle count

## Slide 50: Energy Control
Bit toggle count: compressed vs. uncompressed
Use a heuristic (Energy X Delay or Energy X Delay2 metric) to estimate the trade-off
Take bandwidth utilization into account
Throttle compression when it is not beneficial

## Slide 51: Methodology
Simulator: GPGPU-Sim 3.2.x and in-house simulator
Workloads:
  NVIDIA apps (discrete and mobile): 221 apps
  Open-source (Lonestar, Rodinia, MapReduce): 21 apps
System parameters (Fermi):
  15 SMs, 32 threads/warp
  48 warps/SM, 32768 registers, 32KB Shared Memory
  Core: 1.4GHz, GTO scheduler, 2 schedulers/SM
  Memory: 177.4GB/s BW, GDDR5
  Cache: L1 - 16KB; L2 - 768KB

## Slide 52: Effect of EC on Bit Toggle Count
Chart: Normalized Bit Toggle Count
| FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | Discrete | Mobile | Open-Source
Without EC | 1.1884 | 1.1267 | 1.1487 | 1.1993 | 1.1116 | 1.0919 | 2.1276 | 2.1399 | 1.9797 | 2.1896 | 1.93 | 1.4886 | 1.6155 | 1.2358 | 2.0462
With EC | 1.0382 | 1.0284 | 1.0494 | 1.009 | 1.047 | 1.0021 | 1.0345 | 1.0352 | 1.1484 | 1.1513 | 1.5484 | 1.3533 | 1.4125 | 1.0317 | 1.7288
EC significantly reduces the bit toggle count
Works for different compression algorithms

## Slide 53: Effect of EC on Compression Ratio
Chart: Compression Ratio
| FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | FPC | BDI | BDI+FPC | Fibonacci | C-Pack | Discrete | Mobile | Open-Source
Without EC | 1.2773 | 1.2912 | 1.3721 | 1.2468 | 1.4379 | 1.0061 | 1.2549 | 1.2557 | 1.5687 | 1.4733 | 1.4291 | 1.6303 | 1.7156 | 1.724 | 1.5616
With EC | 1.2653 | 1.2793 | 1.3631 | 1.2174 | 1.419 | 1.0034 | 1.1321 | 1.1324 | 1.4144 | 1.3154 | 1.3681 | 1.5866 | 1.6537 | 1.6867 | 1.5121
EC preserves most of the benefits of compression

## Slide 54: Acknowledgments
Todd Mowry and Onur Mutlu
Phil Gibbons and Mike Kozuch
Kayvon Fatahalian, David Wood, and Doug Burger
SAFARI and LBA group members
Collaborators at CMU, MSR, NVIDIA and GaTech
CALCM and PDL
Deb Cavlovich
Family and friends

## Slide 55: Conclusion
Data stored in memory hierarchies has significant redundancy
  Inefficient usage of existing limited resources
Simple and efficient mechanisms for hardware-based data compression
  On-chip caches
  Main memory
  On-chip/off-chip interconnects
Our mechanisms improve performance, cost and energy efficiency

## Slide 56: Practical Data Compression for Modern Memory Hierarchies
Gennady Pekhimenko
Thesis Oral
Committee:
Todd Mowry (Co-chair)
Onur Mutlu (Co-chair)
Kayvon Fatahalian
David Wood, University of Wisconsin-Madison
Doug Burger, Microsoft
Michael Kozuch, Intel
Presented in partial fulfillment of the requirements for the degree of Doctor of Philosophy