## Slide 1
Understanding and Improving Latency of DRAM-Based Memory Systems
Thesis Oral
Kevin Chang
Committee:
Prof. Onur Mutlu (Chair)
Prof. James Hoe
Prof. Kayvon Fatahalian
Prof. Stephen Keckler (NVIDIA, UT Austin)
Prof. Moinuddin Qureshi (Georgia Tech.)
Committee:
Prof. Onur Mutlu (Chair)
Prof. James Hoe
Prof. Kayvon Fatahalian
Prof. Stephen Keckler (NVIDIA, UT Austin)
Prof. Moinuddin Qureshi (Georgia Tech.)

## Slide 2: The March For “Moore”
Processor
4K transistors
4B transistors
Main Memory
1Kb
8Gb
DRAM (Dynamic Random Access Memory)
Intel 8080, 1974
Intel 1103, 1970
or

## Slide 3
PROBLEM
DRAM latency has been relatively stagnant

## Slide 4: Main Memory Latency Lags Behind
Chart: DRAM Improvement (log)
| 1999.0 | 2003.0 | 2006.0 | 2008.0 | 2011.0 | 2013.0 | 2014.0 | 2015.0 | 2016.0 | 2017.0
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant

## Slide 5: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck

## Slide 6
Goal
Improve latency of DRAM (main memory)

## Slide 7: Different DRAM Latency Problems
DRAM
CPU
1. Slow bulk data movement between two memory locations
2. Refresh delays memory accesses
4. Voltage affects latency
Voltage
chip
3. High standard latency to mitigate cell variation

## Slide 8: Thesis Statement
Memory latency can be significantly reduced with a multitude of low-cost architectural techniques that aim to reduce different causes of long latency

## Slide 9
Contributions

## Slide 10
DRAM
CPU
1. Slow bulk data movement between two memory locations
2. Refresh delays memory accesses
4. Voltage affects latency
Voltage
Low-Cost Inter-Linked Subarrays (LISA) [HPCA’16]
Mitigating Refresh Latency by Parallelizing Accesses with Refreshes (DSARP) [HPCA’14]
3. High standard latency to mitigate cell variation
Understanding and Exploiting Latency Variation in DRAM (FLY-DRAM) [SIGMETRICS’16]
Understanding and Exploiting Latency-Voltage Trade-Off (Voltron) [SIGMETRICS’17]
Low-Cost Architectural Features in DRAM
Understanding and overcoming the latency limitation in DRAM

## Slide 11
DRAM Background
What’s inside a DRAM chip?
How to access DRAM?
How long does accessing data take?

## Slide 12: High-Level DRAM Organization
DRAM
Channel
DIMM
(Dual in-line memory module)
DRAM
chip

## Slide 13
Bank
Bitline
Row Buffer
Sense amplifier
S
S
S
S
S
Precharge unit
P
P
P
P
P
Row Decoder
Wordline
Subarray
512 x 8Kb
I/O
64b
Internal Data Bus
Subarray
Chips
DRAM Cell

## Slide 14: Reading Data From DRAM
To Bank I/O
ACTIVATE: Store the row into the row buffer
READ: Select the target column and drive to CPU
PRECHARGE: Reset the bitlines for a new ACTIVATE
S
P
S
P
S
P
S
P
1
1
1
1
1
2
3

## Slide 15: DRAM Access Latency
Command
Data
Duration
ACTIVATE
READ
PRECHARGE
1
1
1
1
Cache line (64B)
Next
ACT
Activation latency: tRCD (13ns / 50 cycles)
1
Precharge latency: tRP (13ns / 50 cycles)
2

## Slide 16
DRAM
CPU
1. Slow bulk data movement between two memory locations
2. Refresh delays memory accesses
4. Voltage affects latency
Voltage
Low-Cost Inter-Linked Subarrays (LISA) [HPCA’16]
Mitigating Refresh Latency by Parallelizing Accesses with Refreshes (DSARP) [HPCA’14]
3. High standard latency to mitigate cell variation
Understanding and Exploiting Latency Variation in DRAM (FLY-DRAM) [SIGMETRICS’16]
Understanding and Exploiting Latency-Voltage Trade-Off (Voltron) [SIGMETRICS’17]
Low-Cost Architectural Features in DRAM
Understanding and overcoming the latency limitation in DRAM

## Slide 17: Problem: Inefficient Bulk Data Movement
Bulk data movement is a key operation in many applications
  memmove & memcpy: 5% cycles in Google’s datacenter [Kanev+, ISCA’15]
Memory Controller
CPU
Memory
Channel
dst
src
Long latency and high energy
LLC
Core
Core
Core
Core
64 bits

## Slide 18
Move Data inside DRAM?

## Slide 19: Moving Data Inside DRAM?
Subarray 1
Subarray 2
Subarray 3
Subarray N
…
Internal Data Bus (64b)
8Kb
512 rows
Bank
Bank
Bank
Bank
DRAM
…
Low connectivity in DRAM is the fundamental bottleneck for bulk data movement
Goal: Provide a new substrate to enable wide connectivity between subarrays

## Slide 20
Our proposal: Low-Cost Inter-Linked SubArrays (LISA)

## Slide 21: Observations
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
…
Bitlines serve as a bus that is as wide as a row
1
Bitlines between subarrays are close but disconnected
2
Internal Data Bus (64b)

## Slide 22: Low-Cost Interlinked Subarrays (LISA)
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
…
Interconnect bitlines of adjacent subarrays in a bank using isolation transistors (links)
ON
64b
8kb

## Slide 23: Low-Cost Interlinked Subarrays (LISA)
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
…
LISA forms a wide datapath b/w subarrays
64b
8kb
ON
Row Buffer Movement (RBM): Move a row of data in an activated row buffer to a precharged one
4KB data in 8ns → 500 GB/s, 26x bandwidth of a DDR4-2400 channel
0.8% DRAM chip area overhead
Charge
Sharing

## Slide 24
Three New Applications of LISA to Reduce Latency
1 Fast bulk data copy

## Slide 25: 1. Rapid Inter-Subarray Copying (RISC)
Goal: Efficiently copy a row across subarrays
Key idea: Use RBM to form a new command sequence
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
Subarray 1
Subarray 2
Activate dst row (write row buffer into dst row)
3
RBM SA1→SA2
2
Activate src row
1
src row
dst row
Reduces row-copy latency by 9x, DRAM energy by 48x

## Slide 26: Methodology
Cycle-level simulator: Ramulator [Kim+, CAL’15]
Four out-of-order cores
Two DDR3-1600 channels
Benchmarks: TPC, STREAM, SPEC2006, DynoGraph, random, bootup, forkbench, shell script

## Slide 27: RISC Outperforms Prior Work
Chart: Normalized Speedup
| Normalized Speedup
RowClone | 0.76
RISC | 1.662
[Seshadri+, MICRO’13]
Chart: Normalized DRAM Energy
RowClone | 0.949
RISC | 0.446
-24%
RowClone limits bank-level parallelism
66%
-55%
-5%
50 workloads
50 workloads
Rapid Inter-Subarray Copying (RISC) using LISA improves system performance

## Slide 28
Three New Applications of LISA to Reduce Latency
1 Fast bulk data copy
2 In-DRAM caching

## Slide 29: 2. Variable Latency DRAM (VILLA)
Goal: Reduce access latency with low area overhead
Motivation: Trade-off between area and latency
High area overhead
Long Bitline
Short Bitline
High latency
Low latency
  Lower resistance and capacitance

## Slide 30: 2. Variable Latency DRAM (VILLA)
Key idea: Heterogeneous DRAM design by adding a few fast subarrays as a low-cost cache in each bank
Benefits: Reduce access latency for frequently-accessed data
Slow Subarray
Slow Subarray
Fast Subarray
LISA: Cache rows rapidly from slow to fast subarrays
32 rows
512 rows
Reduces hot data access latency by 2.2x at only 1.6% area overhead
Challenge: How to move data efficiently from slow to fast subarrays?

## Slide 31: VILLA Improves System Performance by Caching Hot Data
Chart: Workloads (50)
VILLA | 0.99914 | 1.0049 | 1.0103 | 1.014 | 1.0151 | 1.0189 | 1.019 | 1.0199 | 1.0204 | 1.0206 | 1.0206 | 1.0218 | 1.0222 | 1.0225 | 1.0228 | 1.0229 | 1.0242 | 1.0249 | 1.0253 | 1.0272 | 1.0281 | 1.0297 | 1.0299 | 1.0304 | 1.0362 | 1.0394 | 1.0461 | 1.0461 | 1.0518 | 1.052 | 1.054 | 1.061 | 1.0622 | 1.0642 | 1.0646 | 1.0714 | 1.075 | 1.0754 | 1.0782 | 1.0816 | 1.0823 | 1.0839 | 1.0893 | 1.1018 | 1.1027 | 1.1039 | 1.112 | 1.1334 | 1.1446 | 1.1605
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
VILLA Cache Hit Rate | 0.8 | 8.3 | 16.3 | 8.7 | 14.4 | 16.7 | 21.5 | 8 | 23 | 16.7 | 32.8 | 15.4 | 16.8 | 26.5 | 18.8 | 26.7 | 23.1 | 29.2 | 19.4 | 18.3 | 20.1 | 30.7 | 23 | 24.7 | 18.6 | 26.6 | 40.2 | 36.2 | 39.7 | 33.8 | 50.1 | 39.2 | 33.7 | 38 | 41.5 | 43.1 | 38.4 | 41.6 | 43.9 | 40.4 | 52.9 | 35.4 | 37.6 | 45.9 | 49.8 | 49.9 | 61.3 | 52.7 | 64.9 | 69.1
Avg: 5%
Max: 16%
LISA enables an effective in-DRAM caching scheme

## Slide 32
Three New Applications of LISA to Reduce Latency
1 Fast bulk data copy
2 In-DRAM caching
3 Fast precharge

## Slide 33: 3. Linked Precharge (LIP)
Problem: The precharge time is limited by the strength of one precharge unit
Linked Precharge (LIP): LISA precharges a subarray using multiple precharge units
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
S
P
Precharging
S
P
S
P
S
P
S
P
Activated row
on
on
on
Linked Precharging
Conventional DRAM
LISA DRAM
Reduces precharge latency by 2.6x
Activated row

## Slide 34: LIP Improves System Performance by Accelerating Precharge
Chart: Workloads (50)
LIP | 1.0297 | 1.0328 | 1.0356 | 1.0448 | 1.0464 | 1.0521 | 1.0561 | 1.0576 | 1.0585 | 1.0619 | 1.0622 | 1.0625 | 1.0642 | 1.0656 | 1.0675 | 1.0706 | 1.0706 | 1.0724 | 1.0727 | 1.0731 | 1.074 | 1.0741 | 1.0752 | 1.0798 | 1.0804 | 1.0839 | 1.0862 | 1.0866 | 1.0878 | 1.0886 | 1.0893 | 1.0907 | 1.0908 | 1.0918 | 1.0921 | 1.0931 | 1.0939 | 1.0966 | 1.0974 | 1.0979 | 1.1009 | 1.1081 | 1.109 | 1.1096 | 1.1149 | 1.1151 | 1.1228 | 1.1247 | 1.1312 | 1.1318
Baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Avg: 8%
Max: 13%
LISA reduces precharge latency

## Slide 35: Latency Reduction of LISA
Latency of Operations
ACTIVATE
PRECHARGE
VILLA
VILLA
1.7x
1.5x
LIP
2.6x
READ
WRITE
x64
x64
9x
4KB data copying
LISA is a versatile substrate that enables many new techniques

## Slide 36
DRAM
CPU
1. Slow bulk data movement between two memory locations
2. Refresh delays memory accesses
4. Voltage affects latency
Voltage
Low-Cost Inter-Linked Subarrays (LISA) [HPCA’16]
Mitigating Refresh Latency by Parallelizing Accesses with Refreshes (DSARP) [HPCA’14]
3. High standard latency to mitigate cell variation
Understanding and Exploiting Latency Variation in DRAM (FLY-DRAM) [SIGMETRICS’16]
Understanding and Exploiting Latency-Voltage Trade-Off (Voltron) [SIGMETRICS’17]
Low-Cost Architectural Features in DRAM
Understanding and overcoming the latency limitation in DRAM

## Slide 37: What Does DRAM Latency Mean to You?
DRAM latency: Delay as specified in DRAM standards
Memory controllers use these standardized latency to access DRAM
Key question: How does reducing latency affect DRAM accesses?
“The purpose of this Standard is to define the minimum set of requirements for JEDEC compliant … SDRAM devices” (p.1) JEDEC DDRx standard

## Slide 38: Goals
1 Understand and characterize reduced-latency behavior in modern DRAM chips
2 Develop a mechanism that exploits our observation to improve DRAM latency
2

## Slide 39: Experimental Setup
Custom FPGA-based infrastructure
  Existing systems: Commands are generated and controlled by HW
PCIe
DDR3
PC
FPGA
DIMM

## Slide 40: Experiments
Swept each timing parameter to read data
  Time step of 2.5ns (FPGA cycle time)
Check the correctness of data read back from DRAM
  Any errors (bit flips)?
Tested 240 DDR3 DRAM chips from three vendors
  30 DIMMs
  Capacity: 1GB

## Slide 41
Experimental Results Activation Latency

## Slide 42: Variation in Activation Errors
Different characteristics across cells
Results from 7500 rounds over 240 chips
Very few errors
Many errors
<10 bits
8KB (one row)
step size
Rife with errors
No Errors
13.1ns
standard
Activation Latency/tRCD (ns)
Modern DRAM chips exhibit significant variation in activation latency

## Slide 43: DRAM Latency Variation
High
Low
DRAM Latency
DRAM B
DRAM A
DRAM C
Slow cells
Imperfect manufacturing process → latency variation in timing parameters

## Slide 44
Experimental Results Precharge Latency

## Slide 45: Variation in Precharge Errors
Results from 4000 rounds over 240 chips
Very few errors
Many errors
8KB (one row)
step size
Rife with errors
No Errors
13.1ns
standard
100 rows
Precharge Latency/tRP (ns)
Modern DRAM chips exhibit significant variation in precharge latency

## Slide 46: Spatial Locality of Slow Cells
Slow cells are concentrated at certain regions
One DIMM: tRCD=7.5ns
One DIMM: tRP=7.5ns

## Slide 47
FLY
Mechanism: Flexible-Latency (FLY) DRAM

## Slide 48: Mechanism to Reduce DRAM Latency
Observation: DRAM timing errors (slow DRAM cells) are concentrated on certain regions
Flexible-LatencY (FLY) DRAM
  A memory controller design that reduces latency
Key idea:
  1) Divide memory into regions of different latencies
  2) Memory controller: Use lower latency for regions without slow cells; higher latency for other regions
Latency profile through DRAM vendors or online tests

## Slide 49: Benefits of FLY-DRAM
Chart: 40 Workloads
Baseline (DDR3) | 1
FLY-DRAM (DIMM 1) | 1.176
FLY-DRAM (DIMM 2) | 1.195
Upper Bound | 1.197
17.6%
19.5%
19.7%
FLY-DRAM improves performance by exploiting latency variation in DRAM
83%
99%
0%
100%
Fast cells (%)

## Slide 50: Latency Reduction of FLY-DRAM
Latency of Operations
ACTIVATE
PRECHARGE
VILLA
VILLA
1.7x
1.5x
LIP
2.6x
READ
WRITE
x64
x64
9x
4KB data copying
FLY
FLY
1.7x
1.7x
Experimental demonstration of latency variation enables techniques to reduce latency

## Slide 51
DRAM
CPU
1. Slow bulk data movement between two memory locations
2. Refresh delays memory accesses
4. Voltage affects latency
Voltage
Low-Cost Inter-Linked Subarrays (LISA) [HPCA’16]
Mitigating Refresh Latency by Parallelizing Accesses with Refreshes (DSARP) [HPCA’14]
3. High standard latency to mitigate cell variation
Understanding and Exploiting Latency Variation in DRAM (FLY-DRAM) [SIGMETRICS’16]
Understanding and Exploiting Latency-Voltage Trade-Off (Voltron) [SIGMETRICS’17]
Low-Cost Architectural Features in DRAM
Understanding and overcoming the latency limitation in DRAM

## Slide 52
DRAM voltage is an important factor that affects: latency, power, and reliability
Goal: Understand the relationship between latency and DRAM voltage and exploit this trade-off
Motivation

## Slide 53: Methodology
FPGA platform
Tested 124 DDR3L DRAM chips (31 DIMMs)
Voltage
Controller
DIMM

## Slide 54: Key Result: Voltage vs. Latency
Circuit-level SPICE simulation
Trade-off between access latency and voltage
Potential latency range

## Slide 55: Goal and Key Observation
Goal: Exploit the trade-off between voltage and latency to reduce energy consumption
Approach: Reduce voltage
  Performance loss due to increased latency
  Energy: Function of time (performance) and power (voltage)
Observation: Application’s performance loss due to higher latency has a strong linear relationship with its memory intensity

## Slide 56: Mechanism: Voltron
Build a performance (linear) model to predict performance loss based on the selected voltage value
Use the model to select a minimum voltage that satisfies a performance loss target specified by the user
Results: Reduces system energy by 7.3% with a small performance loss of 1.8%

## Slide 57: Reducing Latency by Exploiting Voltage-Latency Trade-Off
Voltron exploits the latency-voltage trade-off to improve energy efficiency
Another perspective: Increase voltage to reduce latency

## Slide 58
CPU
1. Slow bulk data movement between two memory locations
2. Refresh delays memory accesses
3. High standard latency to mitigate cell variation
4. Voltage affects latency
Voltage
Low-Cost Inter-Linked Subarrays (LISA) [HPCA’16]
Mitigating Refresh Latency by Parallelizing Accesses with Refreshes (DSARP) [HPCA’14]
DRAM
Understanding and Exploiting Latency Variation in DRAM (FLY-DRAM) [SIGMETRICS’16]
Understanding and Exploiting Latency-Voltage Trade-Off (Voltron) [SIGMETRICS’17]
Low-Cost Architectural Features in DRAM
Understanding and overcoming the latency limitation in DRAM

## Slide 59
Problem: Refreshing DRAM blocks memory accesses
  Prolongs latency of memory requests
Goal: Reduce refresh-induced latency on demand requests
Key observation: Some subarrays and I/O remain completely idle during refresh
Dynamic Subarray Access-Refresh Parallelization (DSARP):
  DRAM modification to enable idle DRAM subarrays to serve accesses during refresh
  0.7% DRAM area overhead
20.2% system performance improvement for 8-core systems using 32Gb DRAM
Summary of DSARP

## Slide 60: Prior Work on Low-Latency DRAM
Uniform short-bitlines DRAM: FCRAM, RLDRAM
  Large area overhead (30% - 80%)
Heterogeneous bitline design
  TL-DRAM: Intra-subarray [Lee+, HPCA’13] Requires two fast rows to cache one slow row
  CHARM: Inter-bank [Son+, ISCA’13] High movement cost between slow and fast banks
SRAM cache in DRAM [Hidaka+, IEEE Micro’90]
  Large area overhead (38% for 64KB) and complex control
Our work:
  Low cost
  Detailed experimental understanding via characterization of commodity chips

## Slide 61
CONCLUSION

## Slide 62: Conclusion
Memory latency has remained mostly constant over the past decade
  System performance bottleneck for modern applications
Simple and low-cost architectural mechanisms
  New DRAM substrate for fast inter-subarray data movement
  Refresh architecture to mitigate refresh interference
Understanding latency behavior in commodity DRAM
  Experimental characterization of: 1) Latency variation inside DRAM 2) Relationship between latency and DRAM voltage

## Slide 63: Thesis Statement
Memory latency can be significantly reduced with a multitude of low-cost architectural techniques that aim to reduce different causes of long latency

## Slide 64: Future Research Direction
Latency characterization and optimization for other memory technologies
  eDRAM
  Non-volatile memory: PCM, STT-RAM, etc.
Understanding other aspects of DRAM
  Variation in power/energy consumption
  Security/reliability

## Slide 65: Other Areas Investigated
Energy Efficient Networks-On-Chip [NOCS’12, SBACPAD’12, SBACPAD’14]
DRAM Testing Platform [HPCA’17]
Low-latency DRAM Architecture [HPCA’15]
Memory Schedulers for Heterogeneous Systems [ISCA’12, TACO’16]

## Slide 66: Acknowledgements
Onur Mutlu
James Hoe, Kayvon Fatahalian, Moinuddin Qureshi, and Steve Keckler
Safari group: Rachata Ausavarungnirun, Amirali Boroumand, Chris Fallin, Saugata Ghose, Hasan Hassan, Kevin Hsieh, Ben Jaiyen, Abhijith Kashyap, Samira Khan, Yoongu Kim, Donghyuk Lee, Yang Li, Jamie Liu, Yixin Luo, Justin Meza, Gennady Pekhimenko, Vivek Seshadri, Lavanya Subramanian, Nandita Vijaykumar, Hanbin Yoon, Hongyi Xin
Georgia Tech. collaborators: Prashant Nair, Jaewoong Sim
CALCM group
Friends
Family — parents, sister, and girlfriend
Intern mentors and industry collaborators:

## Slide 67: Sponsors
Intel and SRC for my fellowship
NSF and DOE
Facebook, Google, Intel, NVIDIA, VMware, Samsung

## Slide 68: Thesis Related Publications
Improving DRAM Performance by Parallelizing Refreshes with Accesses Kevin Chang, Donghyuk Lee, Zeshan Chishti, Alaa Alameldeen, Chris Wilkerson, Yoongu Kim, Onur Mutlu HPCA 2014
Low-Cost Inter-Linked Subarrays (LISA): Enabling Fast Inter-Subarray Data Movement in DRAM Kevin Chang, Prashant J. Nair, Donghyuk Lee, Saugata Ghose, Moinuddin K. Qureshi, and Onur Mutlu HPCA 2016
Understanding Latency Variation in Modern DRAM Chips: Experimental Characterization, Analysis, and Optimization Kevin Chang, Abhijith Kashyap, Hasan Hassan Samira Khan, Kevin Hsieh, Donghyuk Lee, Saugata Ghose, Gennady Pekhimenko, Tianshi Li, Onur Mutlu SIGMETRICS 2016
Understanding Reduced-Voltage Operation in Modern DRAM Devices: Experimental Characterization, Analysis, and Mechanisms Kevin Chang, Abdullah Giray Yağlikçi, Saugata Ghose, Aditya Agrawal, Niladrish Chatterjee, Abhijith Kashyap, Donghyuk Lee, Mike O’connor, Hasan Hassan, Onur Mutlu SIGMETRICS 2017

## Slide 69
Understanding and Improving Latency of DRAM-Based Memory Systems
Thesis Oral
Kevin Chang
Committee:
Prof. Onur Mutlu (Chair)
Prof. James Hoe
Prof. Kayvon Fatahalian
Prof. Stephen Keckler (NVIDIA, UT Austin)
Prof. Moinuddin Qureshi (Georgia Tech.)
Committee:
Prof. Onur Mutlu (Chair)
Prof. James Hoe
Prof. Kayvon Fatahalian
Prof. Stephen Keckler (NVIDIA, UT Austin)
Prof. Moinuddin Qureshi (Georgia Tech.)