## Slide 1: Simple DRAM and Virtual Memory Abstractions for Highly Efficient Memory Systems
Thesis Oral
Committee:
Todd Mowry (Co-chair)
Onur Mutlu (Co-chair)
Phillip B. Gibbons
David Andersen
Rajeev Balasubramonian, University of Utah
Vivek Seshadri
Presented in partial fulfillment of the requirements for the degree of Doctor of Philosophy

## Slide 2
CPU
DRAM
Caches
Applications
System Software
MMU
Memory
Controller
Instruction Set Architecture
Cache line granularity (64B)
Word granularity
(4B or 8B)
Page granularity
(4KB or larger)

## Slide 3: The Curse of Multiple Granularities
Fine-grained memory capacity management
  Existing virtual memory frameworks result in unnecessary work
  High memory redundancy and low performance
Bulk data operations
  Existing interfaces require large data transfers
  High latency, bandwidth, and energy
Non-unit strided access patterns
  Poor spatial locality
  Existing systems optimized to transfer cache lines
  High latency, bandwidth, and energy

## Slide 4: Thesis Statement
Our thesis is that
exploiting the untapped potential of existing hardware structures (processor and DRAM) by augmenting them with simple, low-cost features can enable significant improvement in the efficiency of different memory operations

## Slide 5: Contributions of this Dissertation
Page Overlays – a new virtual memory framework to enable fine-grained memory management
RowClone – a mechanism to perform bulk data copy and initialization completely inside DRAM
Buddy RAM – a mechanism to perform bulk bitwise operations completely inside DRAM
Gather-Scatter DRAM – a mechanism to exploit DRAM architecture to accelerate strided access patterns
Dirty-Block Index – a mechanism to restructure dirty bits in on-chip caches to suit queries for dirty blocks

## Slide 6: Outline for the Talk
1. Page Overlays
– efficient fine-grained memory management
3. RowClone + Buddy RAM
– in-DRAM bulk copy + bitwise operations
2. Gather-Scatter DRAM
– accelerating strided access patterns
4. Dirty-Block Index
– maintaining coherence of dirty blocks

## Slide 7: Copy-on-Write
Virtual page
Physical Page
Write
Copy entire page
2
Change mapping
3
1
Allocate new page
Copy-on-Write
Copy
Page
Tables
Virtual Address Space
Physical Address Space

## Slide 8: Shortcomings of Page-granularity Management
Virtual page
Physical Page
Write
Copy entire page
2
Change mapping
3
1
Allocate new page
Copy-on-Write
Copy
Page
Tables
Virtual Address Space
Physical Address Space
High memory redundancy

## Slide 9: Shortcomings of Page-granularity Management
Virtual page
Physical Page
Write
Copy entire page
2
Change mapping
3
1
Allocate new page
Copy-on-Write
Copy
Page
Tables
Virtual Address Space
Physical Address Space
4KB copy: High Latency
Wouldn’t it be nice to map pages at a
finer granularity (smaller than 4KB)?

## Slide 10: Fine-grained Memory Management
Fine-grained
Memory Management
Fine-grained
data protection
(simpler programs)
More efficient
capacity management
(avoid internal fragmentation, deduplication)
Fine-grained
metadata management
(better security, efficient software debugging)
Higher Performance
(e.g., more efficient
copy-on-write)
Notes: * fine-grained \n

## Slide 11: The Page Overlay Framework
C0
C1
C2
C3
C4
C5
Virtual Page
C0
C1
C2
C3
C4
C5
Physical Page
C2
C5
Overlay
The overlay contains only a subset of cache lines from the virtual page
Access Semantics:
Only cache lines not present in the overlay are accessed from the physical page
C1
C1
C5
C5
Overlay maintains the newer version of a subset of cache lines from the virtual page

## Slide 12: Overlay-on-Write: An Efficient Copy-on-Write
Virtual page
Physical Page
Write
Copy-on-Write
Page
Tables
Virtual Address Space
Physical Address Space
Overlay
Overlay contains only modified cache lines
Does not require full page copy

## Slide 13: Implementation Overview
V
Virtual Address Space
P
O
Main Memory
Regular Physical Pages
Overlays
No changes!

## Slide 14: Addressing Overlay Cache Lines: Naïve Approach
V
Virtual Address Space
P
O
Main Memory
Use the location of the overlay in main memory to tag overlay cache lines
1. Processor must compute the address
2. Does not work with virtually-indexed caches
3. Complicates overlay cache line insertion

## Slide 15: Addressing Overlay Cache Lines: Dual Address Design
V
Virtual Address Space
P
O
Main Memory
P
O
Page Tables
Physical Address Space
Unused physical address space
Overlay cache address space
same size
Notes: Mention the simple approach (put the second address in the page table)
* Overlay in main memory contains only a few cache lines

## Slide 16: Virtual-to-Overlay Mappings
V
Virtual Address Space
P
O
Main Memory
P
O
Page Tables
Physical Address Space
Overlay cache address space
Direct Mapping
Overlay Mapping Table (OMT)
(maintained by memory controller)

## Slide 17: Methodology
Memsim memory system simulator [Seshadri+ PACT 2012]
2.67 GHz, single core, out-of-order, 64 entry instruction window
64-entry L1 TLB, 1024-entry L2 TLB
64KB L1 cache, 512KB L2 cache, 2MB L3 cache
Multi-entry Stream Prefetcher [Srinath+ HPCA 2007]
Open row, FR-FCFS, 64 entry write buffer, drain when full
64-entry OMT cache
DDR3 1066 MHz, 1 channel, 1 rank, 8 banks

## Slide 18: Overlay-on-Write
Lower memory redundancy
Lower latency
Virtual page
Physical Page
Write
2
3
1
Copy-on-Write
Virtual page
Physical Page
Write
Copy-on-Write
Overlay
Copy-on-Write
Overlay-on-Write

## Slide 19: Fork Benchmark
Additional memory consumption
Performance (cycles per instruction)
Parent Process
Fork
(child idles)
Copy-on-Write
Overlay-on-Write
Time
write
300 million insts
Applications from SPEC CPU 2006 (varying write working sets)

## Slide 20: Overlay-on-Write vs. Copy-on-Write on Fork
Chart: Write Working Set
| Small | Dense | Sparse | Mean
Copy-on-write | 1.764 | 14.246 | 53.744 | 23.25
Overlay-on-write | 1.58 | 14.062 | 16.918 | 10.85
Chart: Write Working Set
| Small | Dense | Sparse | Mean
Copy-on-write | 1.318 | 4.626 | 7.13 | 3.07
Overlay-on-write | 1.318 | 4.5 | 5.824 | 2.59
Copy-on-Write
Overlay-on-Write
53%
15%

## Slide 21: Page Overlays: Applications
Overlay-on-Write
Sparse Data Structure Representation
  Exploit any degree of cache line sparsity
  Allow dynamic insertion of non-zero values
Flexible Super-page Management
  Share super pages across processes
Fine-grained Deduplication
Memory Checkpointing
Virtualizing Speculation
Fine-grained Metadata Management
Notes: Reorder and animate

## Slide 22: Outline for the Talk
1. Page Overlays
– efficient fine-grained memory management
3. RowClone + Buddy RAM
– in-DRAM bulk copy + bitwise operations
2. Gather-Scatter DRAM
– accelerating strided access patterns
4. Dirty-Block Index
– maintaining coherence of dirty blocks

## Slide 23: Example 2: Strided access pattern
Physical layout of the data structure (row store)
Record 1
Record 2
Record n
In-Memory Database Table
Field 1
Field 3

## Slide 24: Shortcomings of existing systems
Cache Line
Data unnecessarily transferred on the memory channel and stored in on-chip cache
High latency
Wasted bandwidth
Wasted cache space
High energy

## Slide 25: Goal: Eliminate inefficiency
Cache Line
Can we retrieve only useful data from memory?
Gather-Scatter DRAM
(Power-of-2 strides)

## Slide 26: DRAM modules have multiple chips
READ addr
Cache Line
?
Two Challenges!
Data
Cmd/Addr
Notes: Introduce the values .. Each chip provides 8 bytes.

## Slide 27: Challenge 1: Chip conflicts
Data of each cache line is spread across all the chips!
Cache line 0
Cache line 1
Useful data mapped to only two chips!

## Slide 28: Challenge 2: Shared address bus
All chips share the same address bus!
No flexibility for the processor to read different addresses from each chip!
One address bus for each chip is costly!
Notes: More pins from the processor to add address bus.

## Slide 29: Gather-Scatter DRAM
Cacheline-ID-based data shuffling
(shuffle data of each cache line differently)
Pattern ID – In-DRAM address translation
(locally compute column address at each chip)
Challenge 1: Minimizing chip conflicts
Challenge 2: Shared address bus
Notes: Add “solution to challenge 1” etc.

## Slide 30: Cacheline-ID-based data shuffling
Cache Line
Stage 1
Stage 2
Stage 3
Stage “n” enabled only if
nth LSB of cacheline ID is set
Cacheline ID
1
0
1
Chip 0
Chip 1
Chip 2
Chip 3
Chip 4
Chip 5
Chip 6
Chip 7
(implemented in the memory controller)

## Slide 31: Effect of data shuffling
Chip conflicts
Minimal chip conflicts!
CL 0
CL 1
CL 2
CL 3
Chip 0
Chip 1
Chip 2
Chip 3
Chip 4
Chip 5
Chip 6
Chip 7
Chip 0
Chip 1
Chip 2
Chip 3
Chip 4
Chip 5
Chip 6
Chip 7
Before shuffling
After shuffling
Can be retrieved in a single command

## Slide 32: Gather-Scatter DRAM
Cacheline-ID-based data shuffling
(shuffle data of each cache line differently)
Pattern ID – In-DRAM address translation
(locally compute the cacheline address at each chip)
Challenge 1: Minimizing chip conflicts
Challenge 2: Shared address bus

## Slide 33: Per-chip column translation logic
READ addr, pattern
cmd
addr
pattern
CTL
AND
pattern
chip ID
addr
cmd =
READ/WRITE
output address
XOR
Notes: Don’t send address – “locally compute the new address at each chip”
Ensure consistency in capitalization

## Slide 34: Gather-Scatter DRAM (GS-DRAM)
32 values contiguously stored in DRAM (from address 0)
read addr 0, pattern 0 (stride = 1, default operation)
read addr 0, pattern 1 (stride = 2)
read addr 0, pattern 3 (stride = 4)
read addr 0, pattern 7 (stride = 8)

## Slide 35: Methodology
Simulator
  Gem5 x86 simulator
  Use “prefetch” instruction to implement pattern load
  Cache hierarchy
    32KB L1 D/I cache, 2MB shared L2 cache
  Main Memory: DDR3-1600, 1 channel, 1 rank, 8 banks
Energy evaluations
  McPAT + DRAMPower

## Slide 36: In-memory databases
Layouts
Workloads
Row Store
Column Store
GS-DRAM
Transactions
Analytics
Hybrid
Database
Table
Notes: Tie it back non-unit strides
Background database

## Slide 37: Workload
Database
  1 table with million records
  Each record = 1 cache line
Transactions
  Operate on a random record
  Varying number of read-only/write-only/read-write fields
Analytics
  Sum of k columns
Hybrid
  Transactions thread: random records with 1 read-only, 1 write-only
  Analytics thread: sum of one column

## Slide 38: Transaction throughput and energy
Chart: 
| Transaction Throughput
Row Store | 24.24
Column Store | 8.55
GS-DRAM | 24.08
Chart: 
| Energy
Row Store | 16.99
Column Store | 49.65
GS-DRAM | 17.08
Throughput
(millions/second)
Energy
(mJ for 10000 trans.)
Row Store
GS-DRAM
Column Store
3X

## Slide 39: Analytics performance and energy
Row Store
GS-DRAM
Column Store
Chart: 
| Execution Time
Row Store | 2.07
Column Store | 0.86
GS-DRAM | 1.06
Chart: 
| Energy
Row Store | 95.44
Column Store | 40.32
GS-DRAM | 49.82
Execution Time (mSec)
Energy (mJ)
2X

## Slide 40: Hybrid Transactions/Analytical Processing
Chart: 
| Analytics
Row Store | 1.9225
Column Store | 0.605
GS-DRAM | 0.6625
Chart: 
| Transactions
Row Store | 19.68
Column Store | 16.62
GS-DRAM | 27.24
Execution Time (mSec)
Throughput
(millions/second)
Row Store
GS-DRAM
Column Store

## Slide 41: Outline for the Talk
1. Page Overlays
– efficient fine-grained memory management
3. RowClone + Buddy RAM
– in-DRAM bulk copy + bitwise operations
2. Gather-Scatter DRAM
– accelerating strided access patterns
4. Dirty-Block Index
– maintaining coherence of dirty blocks

## Slide 42: Today, DRAM is just a storage device!
Processor
DRAM
Channel
Write (64B)
Read (64B)
Bulk data operations => many data transfers

## Slide 43: Inside a DRAM Chip
…
…
…
…
…
…
2D Array
of DRAM Cells
Sense amplifiers
8KB

## Slide 44: DRAM Cell Operation
Sense Amp
enable
bitline
wordline
capacitor
access transistor

## Slide 45: DRAM Cell Operation
½ VDD + δ
enable
bitline
wordline
capacitor
access transistor
0
½ VDD
0
1
1
VDD
raise wordline
enable sense amp
connects cell to bitline
cell loses charge to bitline
cell regains charge
Sense Amp
deviation in bitline voltage
½ VDD
0

## Slide 46: RowClone: In-DRAM Bulk Data Copy
½ VDD + δ
0
½ VDD
0
1
1
VDD
enable sense amp
Sense Amp
0
1
activate
source
activate
destination
data gets copied source to destination

## Slide 47: Triple-Row Activation
½ VDD + δ
0
½ VDD
0
1
1
VDD
enable sense amp
Sense Amp
activate
all three rows
0
1
0
1

## Slide 48: Bitwise AND/OR Using Triple-Row Activation
Output
Output = AB + BC + CA
= C (A OR B) + ~C (A AND B)
1
1
1
1
VDD
Sense Amp
A
B
C

## Slide 49: Negation Using the Sense Amplifier
Sense Amp
Dual Contact Cell
Regular wordline
Negation wordline

## Slide 50: Negation Using the Sense Amplifier
enable sense amp
Sense Amp
½ VDD + δ
½ VDD
VDD
½ VDD
0
activate
source
activate
negation wordline

## Slide 51: Summary of operations
…
…
…
…
…
…
Sense amplifiers
Copy
AND
OR
NOT

## Slide 52: Throughput Comparison: Bitwise AND/OR
Chart: AND/OR Throughput (GB/s)
| 32 KB | 64 KB | 128 KB | 256 KB | 512 KB | 1 MB | 2 MB | 4 MB | 8 MB | 16 MB | 32 MB
1 Core | 32.42 | 32 | 20.55 | 18.89 | 18.96 | 18.94 | 18.9 | 8.14 | 6.12 | 5.2 | 4.83
2 Core | 62.89 | 65.04 | 61.63 | 39.14 | 36.83 | 36.83 | 36.65 | 15.84 | 7.38 | 5.97 | 5.52
4 Core | 202.49 | 116.06 | 117.54 | 113.97 | 71.81 | 67.17 | 66.3 | 30.22 | 9.77 | 6.14 | 5.78
Buddy | 38.92 | 38.92 | 38.92 | 38.92 | 38.92 | 38.92 | 38.92 | 38.92 | 38.92 | 38.92 | 38.92
Buddy | 155.68 | 155.68 | 155.68 | 155.68 | 155.68 | 155.68 | 155.68 | 155.68 | 155.68 | 155.68 | 155.68
2-Core
4-Core
1-Core
Buddy (4 banks)
Buddy (1 bank)

## Slide 53: Throughput and Energy
Chart: GB/s of Result (higher is better)
| NOT | AND/OR | NAND/NOR | XOR/XNOR
Baseline | 7.9 | 5.78 | 5.78 | 5.78
Buddy | 77.84 | 38.92 | 31.14 | 22.24
Chart: Energy (nJ per KB) (lower is better)
| NOT | AND/OR | NAND/NOR | XOR/XNOR
Baseline | 93.7 | 137.85 | 137.85 | 137.85
Buddy | 1.575 | 3.1375 | 3.925 | 5.5
Baseline
Buddy (1 bank)

## Slide 54: Applications
Implementation of set operations
  Buddy accelerates bitvector based implementations
  More attractive than red-black trees
    Insert, lookup, union, intersection, difference
In-memory bitmap indices
  Used by many online web applications
  Buddy improves query performance by 6X

## Slide 55: Outline for the Talk
1. Page Overlays
– efficient fine-grained memory management
3. RowClone + Buddy RAM
– in-DRAM bulk copy + bitwise operations
2. Gather-Scatter DRAM
– accelerating strided access patterns
4. Dirty-Block Index
– maintaining coherence of dirty blocks

## Slide 56: Cache Coherence Problem
DRAM
Channel
Cache
MC
src
dst
Is src block 1 dirty?
Is src block 2 dirty?
Is src block 3 dirty?
Is src block 128 dirty?
…
List all dirty blocks from the source row

## Slide 57: Dirty-Block Index
Dirty-Block Index
V
D
tag
V
D
tag
V
D
tag
V
D
tag
V
D
tag
V
D
tag
V
D
tag
V
D
tag
Tag Store
Valid bits
Dirty bits
Is block X dirty?
List all dirty blocks
of DRAM row R.
Simple. Several Applications!

## Slide 58: Acknowledgments
Todd Mowry and Onur Mutlu
Phil Gibbons and Mike Kozuch
Dave Andersen and Rajeev Balasubramonian
LBA and SAFARI
Deb!
CALCM and PDL
Squash partners
Friends
Family – parents and brother

## Slide 59: Conclusion
Different memory resources are managed and accessed at different granularities
  Results in significant inefficiency for many operations
Simple, low-cost abstractions
  New virtual memory framework for fine-grained management
  Techniques to use DRAM to do more than store data
Our mechanisms eliminate unnecessary work
  Reduce memory capacity consumption
  Improve performance
  Reduce energy consumption

## Slide 60: Simple DRAM and Virtual Memory Abstractions for Highly Efficient Memory Systems
Thesis Oral
Committee:
Todd Mowry (Co-chair)
Onur Mutlu (Co-chair)
Phillip B. Gibbons
David Andersen
Rajeev Balasubramonian, University of Utah
Vivek Seshadri
Presented in partial fulfillment of the requirements for the degree of Doctor of Philosophy

## Slide 61: Backup Slides

## Slide 62: End-to-end system support for GS-DRAM
Memory controller
Cache Data Store
Tag
Store
Pattern ID
CPU
New instructions:
pattload/pattstore
GS-DRAM
miss
cacheline(addr), patt
DRAM column(addr), patt
pattload reg, addr, patt
Support for coherence of overlapping cache lines
Notes: Animation of a pattload execution

## Slide 63: GS-DRAM improves transaction performance
Chart: Execution time for 10000 trans.
| 1-0-1 | 2-1-2 | 0-2-2 | 2-4-2 | 5-0-1 | 2-0-4 | 6-1-2 | 4-2-2
Row Store | 1.56 | 1.56 | 1.65 | 1.65 | 1.66 | 1.74 | 1.66 | 1.74
Column Store | 2.43 | 3.29 | 4.28 | 6.08 | 6.03 | 6.2 | 6.91 | 7.99
GS-DRAM | 1.58 | 1.58 | 1.65 | 1.65 | 1.68 | 1.74 | 1.68 | 1.74

## Slide 64: GS-DRAM with Odd Stride
Odd stride => minimal chip conflicts
  No shuffling required
Alignment problem
  Objects do not fit perfectly into a DRAM row
  Data may be part of different DRAM rows
Addressing problem
  A value may be part of different addresses in the same pattern
  Difficult to maintain coherence

## Slide 65: Buddy RAM – Implementation
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
…
…
…
Sense
Amplifiers
Dual Contact Cells
Temporary Rows
for Triple Activate
Regular
Data Rows
Pre-initialized Rows

## Slide 66: Buddy RAM – Activate Activate Precharge (AAP)
AAP copies result of first activation into row corresponding to second activation
  Can be used to perform a simple copy
  Bitwise operation if first activation correspond to triple row activation
Example: Bitwise AND
  AAP(d1, t1) -> copy row d1 to temporary row t1
  AAP(d2, t2) -> copy row d2 to temporary row t2
  AAP(c0, t3) -> copy control row zero to temporary row t3
  AAP(t1/t2/t3, d3) -> copy t1&t2 to d3

## Slide 67: Bitmap Indices: Buddy improves performance